10 Point Bonus Problem: Reduce the block diagram below to its transfer function.

Step #1: Simplify by reducing the loop (G2 * G4)   G3, which yields

Step #2: Reduce the inner loop of G1 and H1 to its equivalent form of

which yields

Step #3: Further reduce by multiplying the blocks containing

and

which yields

Step #4: Write the transfer function of this single loop

now simplify to the following

# Text boxes

G1

(

G2

G4

G3

H1

H2

(

X

Y

+

+

+

-

-

+

+

G1

(1+G1H1)

Y

X

H2

H1

(

G1

G3 + G2G4

(

G1

(1+G1H1)

G1

(1+G1H1)

(G3 + G2G4)

G1(G3+G2G4)

(1+G1H1)

(

-

+

+

Y

X

H2

(

G1(G3+G2G4)

(1+G1H1)

1+G1H2(G3+G2G4)

(1+G1H1)

X

Y

G1(G3+G2G4)

1+G1H1+G1H2(G3+G2G4)

Y(s)   =

(X(s)(

(

-

+

+

Y

X

H2

(

G3 + G2G4