For a listing of the parameters that a certain program expects simply type:

program_name.exe <enter>.

All code expects 16-bit signed integers as input and generates the same
as output.


The code is organized as follows:

digit_generation:

This directory contains code that will generate dtmf signals as specified
by the user.  


signal_2_noise:

This directory contains code used to add noise to any signal file. It is 
used for testing robustness to noise.   


dft:

This directory contains an implementation of the Goertzel algorithm for
taking DFT's.  This program simply outputs the response of the algorithm 
at the eight DTMF frequencies.  This code only takes the DFT.  It does
not make any decisions as to which key(if any) has been pressed.


dtmf:

This directory contains the final code we used for DTMF detection.  It expects 
input from stdin(also 16-bit signed integers).  We provided this input
by:

   a) cat signal_file.raw | dtmf_demo.exe sample_frequency

   b) pipe the output from narecord directly to dtmf_demo.exe (real-time)

This code will tell the user: which key was pressed, start time, stop time.
This code does not currently contain a complete USAGE statement.