ATIS-0300076

Numbering and Dialing Plan

within the United States

ATIS is a technical planning and standards development organization that is committed to rapidly developing and promoting technical and operations standards for the communications and related information technologies industry worldwide using a pragmatic, flexible and open approach. Over 1,100 participants from more than 350 communications companies are active in ATIS’ 22 industry committees, and its Incubator Solutions Program. www.atis.org

REvision History

ATIS-0300076: U.S. Numbering and Dialing Plan within the United States

| Version | Date | Changes |
| --- | --- | --- |
| 1.0 | 08-19-2005 | Initial Release |

ATIS-0300076: U.S. Numbering and Dialing Plan within the United States is an ATIS standard developed by the following committee(s) and subcommittee(s) under the ATIS Operations, Administration, Maintenance and Provisioning (OAM&P) functional group:

Industry Numbering Committee (INC), Document Management and Maintenance (DMM) Subcommittee

The Industry Numbering Committee (INC) provides a forum for customers and providers in the telecommunications industry to identify, discuss, and resolve national issues that affect numbering.  The INC is responsible for identifying and incorporating the necessary changes into this document.  All changes to this document shall be made through the INC issue resolution process and adopted by the INC as set forth in the ATIS Operating Procedures.  This document is maintained under the direction of ATIS and the INC.  It is distributed exclusively by ATIS.

Published by:

Alliance for Telecommunications Industry Solutions (ATIS)

1200 G Street, NW, Suite 500

Washington, DC 20005

Copyright © 2005 by Alliance for Telecommunications Industry Solutions

All rights reserved.

No part of this publication may be reproduced in any form, in an electronic retrieval system or otherwise, without the prior written permission of the publisher. For information contact ATIS at (202) 628-6380. ATIS is online at: http://www.atis.org.

Printed in the United States of America.

Disclaimer and Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS.  ATIS SHALL NOT BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY ATIS FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL ATIS BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES.  ATIS EXPRESSLY ADVISES THAT ANY AND ALL USE OF OR RELIANCE UPON THE INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

TABLE OF CONTENTS

1.0 	Scope and Overview	6

2.0 	Introduction	6

3.0 	Historical References and Perspectives	7

3.1 	NANP Management	7

3.2 	Historical NANP Evolution	7

4.0 	United States Telephone Number Format and Values	8

5.0 	United States Dialing Plan	9

6.0 	Other Codes	10

6.1 	Other Codes: Prefixes	10

6.2 	Other Codes: Operator Access Codes	10

6.3 	Other Codes: Codes 000-199	10

6.4 	Other Codes: Star * and Number Sign # 	11

6.5 	Other Codes: N11 Service Access Codes	12

6.5 	Other Codes: N00 Easily Recognized Codes	12

6.6 	Other Codes: Carrier Identification Codes (CIC)	12

6.7 	Other Codes: Carrier Access Codes (CAC)	12

6.8 	Other Codes: Abbreviated Dialing Codes	12

7.0 	References	13

7.0 	Acronyms	13

8.0 	Appendix	15

TABLE 1: STRUCTURE OF THE ITU REC. E.164 NUMBER FIELDS	15

TABLE 2: UNITED STATES NATIONAL DIALING PLAN ITU REC. E.164 COMPLIANCE	15

TABLE 3: UNITED STATES N11 SERVICE ACCESS CODES	16

TABLE 4: N00 NPA CODES	16

TABLE 5: ADDITIONAL NUMBERING NEEDS OF CMRS SERVICE PROVIDERS	17

TABLE 6: UNITED STATES DIALING PLAN	18

## 1.0 Scope and Overview

The purpose of this document is to consolidate the information contained in earlier industry documents into a single standard document that may be used by the industry as the North American Numbering Plan (NANP) evolves.  Further, this document serves as a “snapshot” for anyone interested in numbering issues.

This technical document seeks to document the format and values of telephone numbers in the United States portion of the NANP, thereby coining a “United States Numbering Plan” and a “United States Dialing Plan.”  It further defines the other telecommunications industry uses of numbers and describes these uses in the United States.  The NANP exists under Country Code 1, shared among 19 countries, under the International Telecommunication Union (ITU) Recommendation E.164, "The international public telecommunication numbering plan" (Rec. E.164).

## 2.0 Introduction

2.1 	International Numbering Standards and Conventions

The ITU Telecommunication Standardization Sector (ITU-T) is one of the three Sectors of the International Telecommunication Union, a specialized agency of the United Nations with headquarters in Geneva, Switzerland. The ITU-T studies technical, operating and tariff questions and produces Recommendations and other publications that are used to guarantee the interconnectivity and interoperability of networks and enables telecommunication services to be provided worldwide. The ITU-T website is at http://www.itu.int/ITU-T/index.html.

In the United States telephone numbers follow international standards and are compliant with the major recommendations contained in ITU Rec. E.164 “The international public telecommunications numbering plan” (See TABLE 1 in the Appendix).  This is essential for participation in International Direct Distance Dialing (IDDD).

United States compliance with ITU Rec. E.164 is contained in the Appendix, TABLE 2.  In the NANP, the Numbering Plan Area code is very similar to the National Destination Code contained in ITU-T Rec. E.164, and the Central Office (CO) Code and Line Number are very similar to the Station Number contained in ITU-T Rec. E.164.

## 3.0 Historical References and Perspectives

## 3.1 	NANP Management

AT&T developed and evolved the numbering portion of the NANP from its inception in 1947 until the breakup of AT&T (Modification of Final Judgment) on January 1, 1984.  The NANP was then managed by Bell Communications Research Corporation (Bellcore, now Telcordia Technologies), on behalf of the Regional Bell Operating Companies (RBOC), from 1984 until the enactment of the Telecommunications Act of 1996 (TA-96).  In this time period, Bellcore maintained and coordinated the evolution of the NANP by working with regulators and industry consensus fora through the Alliance for Telecommunications Industry Solutions’ (ATIS) Industry Carriers Compatibility Forum (ICCF).

Since 1996, the ATIS Industry Numbering Committee (INC) has been responsible for the technical definition and use of NANP resources. Numbering policy decisions in the United States are made by the Federal Communications Commission (FCC) under Section 251(e) of the Communications Act of 1934 as amended by the Telecom Act of 1996.  State regulators may also create policies that do not contradict FCC decisions.

In addition, Section 251(e) of the Communications Act of 1934 (Communications Act), as amended by TA-96, grants the FCC plenary jurisdiction over the NANP and related telephone numbering issues in the United States.

The FCC has delegated the overall responsibility for the neutral administration of NANP numbering resources to the North American Numbering Plan Administration (NANPA), subject to directives from regulatory authorities in the countries that share the NANP. NANPA's responsibilities include assignment of NANP resources, and, in the U.S. and its territories, coordination of area code relief planning and collection of utilization and forecast data.  NANPA is not a policy-making entity. In making assignment decisions, NANPA follows regulatory directives and industry-developed guidelines.  In the U.S., central office codes are assigned by the NANPA and, where applicable, thousands blocks are assigned by the Pooling Administrator.

## 3.2 	Historical NANP Evolution

- 1947: Original NANP Format and Values = N (0 or 1) X – NNX – XXXX where N = digits 2 through 9 and X = any digit of 0 through 9.  Initially the NN digits in the NNX portion of a NANP number had "exchange" names whose first two letters corresponded to letters associated with the NN digits on North American telephone dials. (e.g., BEachwood 4 was BE 4)

- 1958: All Number Calling where the NNX was listed as all numbers rather than 2-letters and 1-number.

- 1973: Initial introduction of Interchangeable CO Code NANP format: N (0 or 1)1 X – NXX – XXXX

- 1995: Interchangeable NPA codes implemented NANP format: NXX – NXX – XXXX

## 4.0 United States Telephone Number Format and Values

The telephone numbering address is a ten-digit number that consists of the following three basic parts:

- A 3-digit Numbering Plan Area (NPA) code, commonly called the area code.

- A 3-digit Central Office (CO) code referred to as the NXX code.  The term Central Office, or CO, code is used in this document because of its long-standing use and because the NXX format is used for both CO Codes and NPA codes.

- A 4-digit line number, previously referred to as a station number.

The format of a NANP Number is NXX-NXX-XXXX where N = digits 2 through 9 and X = any digit of 0 through 9.  The digit positions in the NANP format can be identified by alphabetical characters using the following format ABC-DEF-GHIJ, where ABC is the NPA, DEF is the CO Code, and GHIJ is the Line Number.

Therefore:

A United States telephone number is a ten-digit number that contains two 3-digit codes and a 4-digit line number.  The values of these telephone numbers are the decimal digits 0 through 9.

When written or printed, these groups of digits should be visually separated by dashes, spaces or periods in accordance with ITU-T Rec. E.123 “Notation for national and international telephone numbers, e-mail addresses and Web addresses” in order to make them easier to recognize and remember (e.g., NXX-NXX-XXXX).

When a United States telephone number is written or printed as an international number, the number should be prefixed by “+1” and a space (e.g., +1 NXX-NXX-XXXX).

Some documents define telephone numbers and line numbers as being synonymous.  In switching systems, line numbers define the physical location of the line equipment that connects a wireline customer to a wireline switch.  This distinction is important to some industry segments.  Most stored program controlled switching systems can associate multiple numbers with a single line.  They can also associate multiple lines to a single number.

## 5.0 United States Dialing Plan

In the United States, there is no single dialing plan that applies universally in all areas.  In general, local calling within a defined geographic area requires dialing the last 7 digits of the NANP number (i.e., the CO Code and Line Number).  In certain locations where overlay NPAs have been implemented or where local calling crosses an NPA boundary, local calling requires dialing all 10-digits of the NANP number.  In general, long distance calling to NANP locations outside the originating caller’s local calling area requires dialing the prefix 1 plus the 10-digit NANP number for direct dialed calls or dialing the prefix 0 plus the 10-digit NANP number for operator assisted calls (see TABLE 3 in the Appendix for further information regarding prefix dialing requirements).  For long distance calling outside Country Code 1, the dialing plan is the appropriate international calling prefix (e.g., 01 and 011) plus the international telephone number.

In the late 1990s, the INC (see ATIS-0300059) examined the need for a Uniform Dialing Plan (UDP).  After consideration of many options, the INC concluded that adoption of a UDP would be beneficial for the industry and customers.  The INC recommended to regulators of all NANP nations that a Uniform Dialing Plan be adopted.  The benefits of a Uniform Dialing Plan include reduced customer confusion in today’s mobile society, and support for a consistent, fair and equitable competitive environment.  Specifically the INC recommended that 10-Digit Dialing be adopted as the UDP for both local and toll calling.  The INC noted that implementation of the recommendation requires regulatory approval and resolution of the need for “1+” as a toll indicator.  In Canada, some carriers supported the implementation of a toll warning indicator tone when additional toll charges would apply.  The need for a toll warning indicator is lessening over time as the charges for toll services decline.

The INC suggested that migration to the UDP should begin by first adopting the following dialing arrangements as interim steps:

- 10-digit local dialing within the home NPA with 1+ 10-digit dialing on a permissive basis

- 10-digit local dialing to a foreign NPAs with 1+10 digit dialing on a permissive basis

In conjunction with the migration to the UDP, the INC recommended that the industry address the need for the continued use of a toll indicator.  The successful completion of the above steps would allow for the implementation of the UDP throughout the NANP area.

All other numbers used by telephone systems fall in the category of prefixes or access codes. All of the numbers, access codes and prefixes comprise the United States Dialing Plan found in TABLE 6 in the Appendix.

## 6.0 Other Codes

The industry has always employed prefixes and access codes to activate certain capabilities or call types.

## 6.1 	Other Codes: Prefixes

The most commonly used prefixes in the wireline sector are the digit 1 (preceding a sent paid toll call) and the digit 0 (preceding an operator handled toll call). The current list of commonly used wireline prefixes is shown below. Prefixes are usually deleted or processed in the originating switch before the NANP number digits are used to route the call to its final destination.

| PREFIX | USE OF CODE |
| --- | --- |
| 0+ NANP 10-digit Number | Person Paid Collect Special (PPCS) Call |
| 01+ International Number | International PPCS Call |
| 011 + International Number | International Station to Station Sent Paid (SSSP) Call |
| 1+ NANP 10-digit Number | Toll Access for SSSP Calls |

## 6.2 	Other Codes: Operator Access Codes

Two other codes can be dialed to access operators, as per the table below:

| OPERATOR ACCESS CODE | USE OF CODE |
| --- | --- |
| 0 | Telephone Company Operator |
| 00 | Long Distance Carrier Operator |

## 6.3 	Other Codes: Codes 000-199

The codes, 000-199 are not part of the defined NANP format for either of the NPA or CO Code portions of a NANP number.  The codes 000-199 were excluded from the original NANP format and all subsequent redefinitions implemented to date.  The values 0 and 1 in the first and fourth digit positions of a ten-digit NANP number, creates the codes 000-199.

The codes 000-199 are used by the telephone industry for Test Codes, Inward Operator Codes, Special Billing Numbers, Revenue Accounting Office (RAO) Credit Card Numbers and special routing of calls.  Various switching systems have software checks that block calls to and from numbers with these values.  These software checks were installed to minimize fraud.  Operator Services switching systems have software tables to validate credit card calls that utilize these codes.  Numbers utilizing the codes 000-199 are not dialable by the public.

## 6.4 	Other Codes: Star * and Number Sign #

The dialing use of * and # is standardized in order to minimize confusion with the public.  It is also important that consistent terminology be known and used when referring to these characters.  The * and the # should be called the star and the number sign, respectively.  Use of the terms asterisk for * and pound sign for # should be avoided in documentation dealing with dialing procedures.

Currently, the characters # and * have the following general applications:

1) The first use of the number sign (#) is as an end-of-dialing indicator or to conclude the present action and to proceed to the next action indicator.  This end-of-dialing use exists today and avoids a timing period used in certain types of switching systems.  The conclude-and-proceed use also occurs in some telephone credit card services where the customer wants to indicate that the present call is over and a new call is about to be placed (for example, sequence calling).

2) The second use of the number sign (#) is as the first character when dialing a call that is a wideband or other data call requiring special treatment. In certain types of data calls, both an initial and concluding # may be required.  Functionally, this is similar in many respects to the KP + (address) + ST multi-frequency signaling format used by operators.

There are also a number of non-standard uses of the # sign for PIN Number Calling features.  The # sign is also used in ancillary services offered via the PSTN.  An example of this is voice mail.

3) The first use of the star * is as a prefix when dialing a Vertical Service Code (VSC) (for example, call forwarding) of the form *XX(X).  In this application, the * indicates to the switching system that the digits following specify a certain desired feature/service.

In order to allow rotary dial telephone access to VSCs, the digits 11 are translated to simulate the star key in stored program controlled switches.

| VERTICAL SERVICE CODE FORMAT | USE OF CODE |
| --- | --- |
| *XX (*XXX) | Vertical Service Code Access |
| 11XX (11XXX) | Vertical Service Code Alternate (Permissive) Access |

Vertical Service Codes are considered numbering resources and are therefore administered by NANPA.  The current assignments of VSCs are available at the web site: http://www.nanpa.com

4) The second major use of the * is to provide an error correcting function for customer-dialing of various strings on a sequential basis in response to prompting. This could include a customer interactive session with an operator services system when placing automated calling card billed calls. Instead of the customer hanging-up and redialing when detecting a keying error (before the card system detects the keyed error), the caller can simply dial * to back up to a pre-established point and then redial the segment.

## 6.5 	Other Codes: N11 Service Access Codes

N11 Service Access Codes have been declared national resources in the United States and are assigned by the FCC (See TABLE 3 in the Appendix for N11 Codes).

## 6.5 	Other Codes: N00 Easily Recognized Codes

N00 codes are classified as Easily Recognized Codes.  Their uses are assigned by the Alliance for Telecommunications Industry Solutions’ (ATIS) Industry Numbering Committee (INC) (See TABLE 4 in the Appendix for N00 Codes).

## 6.6 	Other Codes: Carrier Identification Codes (CIC)

CICs are 4-digit codes used mainly by carriers to route long-distance calls to a customer's carrier of choice for 1+ and 0+ calls. In the United States, NANPA assigns CICs following the Carrier Identification Code Assignment Guidelines developed by the INC.

## 6.7 	Other Codes: Carrier Access Codes (CAC)

In order to select a carrier on a per-call basis, customers may choose to dial an access code that also contains a Carrier Identification Code (CIC) to reach an IXC.  The format of this code is 101XXXX, where the XXXX is the CIC.

| CARRIER ACCESS CODE FORMAT | USE OF CODE |
| --- | --- |
| 101XXXX | Carrier Access Code (CAC), Feature Group “D” |
| 950XXXX | Carrier Access Code (CAC), Feature Group “B” |

## 6.8 	Other Codes: Abbreviated Dialing Codes

FCC documents have attempted to define the term “Abbreviated Dialing Codes” and have equated N11 Codes to Abbreviated Dialing Codes.  Any code can be made to function as an Abbreviated Dialing Code by the use of switch translations.  Some N11 Codes may be translated to a NANP telephone number and thus function as an Abbreviated Dialing Code.  In another switch, the same N11 Code may translate to a specific trunk group and thus not function as an Abbreviated Dialing Code.  This functionality is at the discretion of each service provider in setting up switch translation.

The wireless telecom industry also has other numbering requirements, separate from the number associated with the wireless subscriber.  Most of these requirements are necessitated by wireless roaming and access to emergency services via dialing 9-1-1 (See TABLE 5 in the Appendix).

## 7.0 References

- “The international public telecommunication numbering plan,” Recommendation E.164, International Telecommunication Union, February 2005.

- “The Communications Act of 1934 as amended by the Telecom Act of 1996.”

- “NPA Allocation Plan & Assignment Guidelines,” ATIS-0300055 (INC), July 2004.

- “Central Office Code (NXX) Assignment Guidelines,” ATIS-0300051 (INC), June 2005.

- “Notation for national and international telephone numbers, e-mail addresses and Web addresses,” Recommendation E.123, International Telecommunication Union, February 2001.

- “Uniform Dialing Plan,” ATIS-0300059 (INC), July 1998.

- “Carrier Identification Code (CIC) Assignment Guidelines” ATIS-0300050 (INC), May 2005.

- “Notes on the Networks,” SR-2275 Issue 04, Telcordia Technologies, October 2000.

## 7.0 Acronyms

AT&T			American Telephone and Telegraph

ATIS			Alliance for Telecommunications Industry Solutions

CAC			Carrier Access Code

CDMA			Code Division Multiple Access

CIC			Carrier Identification Code

CMRS			Commercial Mobile Radio Services

CO Code			Central Office Code

DDD			Direct Distance Dialing

FCC			Federal Communications Commission

GSM			Global System for Mobile communications

IDDD			International Direct Distance Dialing

INC			Industry Numbering Committee

ITU			International Telecommunication Union

IXC			Interexchange Carrier

NANC			North American Numbering Council

NANP			North American Numbering Plan

NANPA			North American Numbering Plan Administrator

NPA			Numbering Plan Area (Area Code)

PIN			Personal Identification Number

PSTN			Public Switched Telephone Network

RAO			Revenue Accounting Office

TDMA			Time Division Multiple Access

UMTS			Universal Mobile Telecommunications System

USITA			United States Independent Telephone Association

(now called United States Telecom Association)

VSC			Vertical Service Code

## 8.0 Appendix

## TABLE 1: STRUCTURE OF THE ITU REC. E.164 NUMBER FIELDS

## TABLE 2: UNITED STATES NATIONAL DIALING PLAN
ITU REC. E.164 COMPLIANCE

CC = 1

NDC = Area Code = NXX Format

SN = CO Code plus Line Number = NXX-XXXX format

n = 1 digit (the number of digits in a country code can be from 1-3; U.S. is assigned 1 digit)

## TABLE 3: UNITED STATES N11 SERVICE ACCESS CODES

| N11 Code | Assigned Use |
| --- | --- |
| 211 | Community Information |
| 311 | Non-emergency access to government |
| 411* | Directory Assistance |
| 511 | Traffic or Travel Information |
| 611* | Telco Repair Service |
| 711 | Telecommunications Relay Service |
| 811 | Pipeline and Utility Safety |
| 911 | Emergency |
| * Commonly accepted use but not yet officially assigned by the FCC |

## TABLE 4: N00 NPA CODES

| N00 NPA Code | Assigned Use |
| --- | --- |
| 200 | Future |
| 300 | Future |
| 400 | Future |
| 500 | Personal Communications Services |
| 600 | Assigned to Canada |
| 700 | IXC Services |
| 800 | Toll Free Number Access |
| 900 | Premium Services |

## TABLE 5: ADDITIONAL NUMBERING NEEDS OF
CMRS SERVICE PROVIDERS

| ACRONYM | MEANING | FORMAT | COMMENTS |
| --- | --- | --- | --- |
| ESRD | Emergency Services Routing Digit | 10 digit NANP # (NPA-NXX-XXXX) or 10 digit Fictitious numbers | Identifies the cell site and sector from which a CMRS E9-1-1 call originates. |
| ESRK | Emergency Services Routing Key | 10 digit NANP # (NPA-NXX-XXXX) or 10 digit Fictitious numbers | In addition to identifying the cell site and sector from which a CMRS E9-1-1 call originates, also identifies and delivers specific call data to the appropriate PSAP |
| MSRN | Mobile Station Routing Number | NPA-NXX-XXXX | A number dynamically assigned on a per call basis by the serving wireless service provider to a CMRS roaming subscriber for incoming call setup purposes. This is used for signaling in GSM/UMTS technology. |
| TLDN | Temporary Local Directory Number | NPA-NXX-XXXX | A number dynamically assigned on a per call basis by the serving wireless service provider to a CMRS roaming subscriber for incoming call setup purposes. This is used for signaling in CDMA/TDMA/AMPS technology. |

## TABLE 6: UNITED STATES DIALING PLAN

| QUANTITY OF DIGITS DIALED | FORMAT | CALL TYPE | COMMENTS |
| --- | --- | --- | --- |
| None | Seizure (off hook) | Hot Line, Warm Line | Automatic connection to predetermined location |
| One Digit | 0 | Operator | Connection to LEC Operator |
| Two Digits | 00 | Operator | Connection to IXC Operator |
| Three Digits | N11 *XX | Services Vertical Services | Connection Activation of service, acknowledgment tone is returned to customer and dial tone is returned. |
| Four/Five Digits | 11XX 11XXX *XXX | Vertical Service from Dial Pulse phone Vertical Services | Activation of service, acknowledgment tone is returned to customer and dial tone is returned. Expansion of *XX |
| Seven Digits | NXX-XXXX | Local Call | Call Completion |
| Ten Digits | NXX-NXX-XXXX | Local Call, where 10 digit local calls are required. | Call Completion |
| Eleven Digits | 1 NXX-NXX-XXXX 0 NXX-NXX-XXXX | SSSP Call to another NANP location PPCS Call to another NANP location | Call Completion Call Completion Note: These call types are routed differently dependent upon Intra-LATA or Inter-LATA jurisdictions. |
| More than Eleven Digits | 01 + CC + CC + Number 011 + CC + CC + Number CC= Country Code and City Code | International PPCS Call International SSSP Call | Call Completion Call Completion Note: These calls can be from 12 to 15 digits plus the Access Code. |

# Footnotes

The use of the parenthesis in this instance indicates that the central digit of the Area Code could only be a 1 or a 0.

The use of the Area Code is optional in some areas that permit 7 digit local dialing.

AT&T Technical Advisory #3, NPL 81-09-27, Issue 2, December 1, 1981, and “Notes on the Networks” SR-2275, Issue 04, Telcordia Technologies, October 2000.

See www.nanpa.com for complete listing of toll free NPA assignments.

# Text boxes

CC

NDC

SN

1 to 3 Digits

National (Significant) Number

Max (15 – n) Digits

Max 15 Digits

International Public Telecommunication Number for Geographic Areas