## Slide 1: Part II Extreme Models

## Slide 2
About This Presentation
Edition | Released | Revised | Revised
First | Spring 2005 | Spring 2006 | Fall 2008
This presentation is intended to support the use of the textbook Introduction to Parallel Processing: Algorithms and Architectures (Plenum Press, 1999, ISBN 0-306-45970-1). It was prepared by the author in connection with teaching the graduate-level course
ECE 254B: Advanced Computer Architecture: Parallel Processing, at the University of California, Santa Barbara. Instructors can use these slides in classroom teaching and for other educational purposes. Any other use is strictly prohibited. © Behrooz Parhami

## Slide 3: II Extreme Models
Study the two extremes of parallel computation models:
  Abstract SM (PRAM); ignores implementation issues
  Concrete circuit model; incorporates hardware details
  Everything else falls between these two extremes
Topics in This Part
Chapter 5 PRAM and Basic Algorithms
Chapter 6 More Shared-Memory Algorithms
Chapter 7 Sorting and Selection Networks
Chapter 8 Other Circuit-Level Examples

## Slide 4: 5 PRAM and Basic Algorithms
PRAM, a natural extension of RAM (random-access machine):
  Present definitions of model and its various submodels
  Develop algorithms for key building-block computations
Topics in This Chapter
5.1 PRAM Submodels and Assumptions
5.2 Data Broadcasting
5.3 Semigroup or Fan-in Computation
5.4 Parallel Prefix Computation
5.5 Ranking the Elements of a Linked List
5.6 Matrix Multiplication

## Slide 5: 5.1 PRAM Submodels and Assumptions
Fig. 4.6 Conceptual view of a parallel random-access machine (PRAM).
Processor i can do
the following in three
phases of one cycle:
Fetch a value from address si in shared memory
Perform computations on data held in local registers
3. Store a value into address di in shared memory

## Slide 6: Types of PRAM
Fig. 5.1 Submodels of the PRAM model.

## Slide 7: Types of CRCW PRAM
Undefined: The value written is undefined (CRCW-U)
Detecting: A special code for “detected collision” is written (CRCW-D)
Common: Allowed only if they all store the same value (CRCW-C)
[ This is sometimes called the consistent-write submodel ]
Random: The value is randomly chosen from those offered (CRCW-R)
Priority: The processor with the lowest index succeeds (CRCW-P)
Max / Min: The largest / smallest of the values is written (CRCW-M)
Reduction: The arithmetic sum (CRCW-S),
logical AND (CRCW-A),
logical XOR (CRCW-X),
or another combination of values is written
CRCW submodels are distinguished by the way they treat multiple writes:

## Slide 8: Power of CRCW PRAM Submodels
Theorem 5.1: A p-processor CRCW-P (priority) PRAM can be simulated (emulated) by a p-processor EREW PRAM with slowdown factor Q(log p).
Intuitive justification for concurrent read emulation (write is similar):
Write the p memory addresses in a list
Sort the list of addresses in ascending order
Remove all duplicate addresses
Access data at desired addresses
Replicate data via parallel prefix computation
Each of these steps requires constant or O(log p) time
Model U is more powerful than model V if TU(n) = o(TV(n)) for some problem
EREW < CREW < CRCW-D < CRCW-C < CRCW-R < CRCW-P
1
6
5
2
3
6
1
1
2
1
1
1
2
2
3
5
6
6
1
2
3
5
6

## Slide 9: Implications of the CRCW Hierarchy of Submodels
Our most powerful PRAM CRCW submodel can be emulated by the least powerful submodel with logarithmic slowdown
Efficient parallel algorithms have polylogarithmic running times
Running time still polylogarithmic after slowdown due to emulation
A p-processor CRCW-P (priority) PRAM can be simulated (emulated) by a p-processor EREW PRAM with slowdown factor Q(log p).
EREW < CREW < CRCW-D < CRCW-C < CRCW-R < CRCW-P
We need not be too concerned with the CRCW submodel used
Simply use whichever submodel is most natural or convenient

## Slide 10: Some Elementary PRAM Computations
Initializing an n-vector (base address = B) to all 0s:
for j = 0 to n/p – 1 processor i do
if jp + i < n then M[B + jp + i] := 0
endfor
Adding two n-vectors and storing the results in a third
(base addresses B, B, B)
Convolution of two n-vectors: Wk = i+j=k Ui  Vj
(base addresses BW, BU, BV)
n / p
segments
p
elements

## Slide 11: 5.2 Data Broadcasting
Fig. 5.2 Data broadcasting in EREW PRAM via recursive doubling.
Making p copies of B[0] by recursive doubling
for k = 0 to log2 p – 1
Proc j, 0  j < p, do
Copy B[j] into B[j + 2k]
endfor
Fig. 5.3 EREW PRAM data broadcasting without redundant copying.
Can modify the algorithm so that redundant copying does not occur and array bound is not exceeded

## Slide 12: All-to-All Broadcasting on EREW PRAM
EREW PRAM algorithm for all-to-all broadcasting
Processor j, 0  j < p, write own data value into B[j]
for k = 1 to p – 1 Processor j, 0  j < p, do
Read the data value in B[(j + k) mod p]
endfor
This O(p)-step algorithm is time-optimal
Naive EREW PRAM sorting algorithm (using all-to-all broadcasting)
Processor j, 0  j < p, write 0 into R[ j ]
for k = 1 to p – 1 Processor j, 0  j < p, do
l := (j + k) mod p
if S[ l ] < S[ j ] or S[ l ] = S[ j ] and l < j
then R[ j ] := R[ j ] + 1
endif
endfor
Processor j, 0  j < p, write S[ j ] into S[R[ j ]]
j
This O(p)-step sorting algorithm is far from optimal; sorting is possible in O(log p) time
p – 1
0

## Slide 13: Class Participation: Broadcast-Based Sorting
Each person write down an arbitrary nonnegative integer with 3 or fewer digits on a piece of paper
Students take turn broadcasting their numbers by calling them out aloud
Each student puts an X on paper for every number called out that is smaller than his/her own number, or is equal but was called out before the student’s own value
j
Each student counts the number of Xs on paper to determine the rank of his/her number
p – 1
0
Students call out their numbers in order of the computed rank

## Slide 14: 5.3 Semigroup or Fan-in Computation
EREW PRAM semigroup computation algorithm
Proc j, 0  j < p, copy X[j] into S[j]
s := 1
while s < p Proc j, 0  j < p – s, do
S[j + s] := S[j]  S[j + s]
s := 2s
endwhile
Broadcast S[p – 1] to all processors
If we use p processors on a list
of size n = O(p log p), then optimal speedup can be achieved
This algorithm is optimal for PRAM, but its speedup of O(p / log p) is not
Fig. 5.4 Semigroup computation in EREW PRAM.
Fig. 5.5 Intuitive justification of why parallel slack helps improve the efficiency.

## Slide 15: 5.4 Parallel Prefix Computation
Fig. 5.6 Parallel prefix computation in EREW PRAM via recursive doubling.
Same as the first part of semigroup computation (no final broadcasting)

## Slide 16: A Divide-and-Conquer Parallel-Prefix Algorithm
Fig. 5.7 Parallel prefix computation using a divide-and-conquer scheme.
In hardware, this is the basis for Brent-Kung carry-lookahead adder
T(p) = T(p/2) + 2
T(p)  2 log2 p
Each vertical line represents a location in shared memory

## Slide 17: Another Divide-and-Conquer Algorithm
Fig. 5.8 Another divide-and-conquer scheme for parallel prefix computation.
Strictly optimal algorithm, but requires commutativity
T(p) = T(p/2) + 1
T(p) = log2 p
Each vertical line represents a location in shared memory

## Slide 18: 5.5 Ranking the Elements of a Linked List
Fig. 5.9 Example linked list and the ranks of its elements.
Fig. 5.10 PRAM data structures representing a linked list and the ranking results.
List ranking appears to be hopelessly sequential; one cannot get to a list element except through its predecessor!

## Slide 19: List Ranking via Recursive Doubling
Fig. 5.11 Element ranks initially and after each of the three iterations.
Many problems that appear to be unparallelizable
to the uninitiated
are parallelizable;
Intuition can be quite misleading!

## Slide 20: PRAM List Ranking Algorithm
Question: Which PRAM submodel is implicit in this algorithm?
If we do not want to modify the original list, we simply make a copy of it first, in constant time
PRAM list ranking algorithm (via pointer jumping)
Processor j, 0  j < p, do {initialize the partial ranks}
if next [ j ] = j
then rank[ j ] := 0
else rank[ j ] := 1
endif
while rank[next[head]]  0 Processor j, 0  j < p, do
rank[ j ] := rank[ j ] + rank[next [ j ]]
next [ j ] := next [next [ j ]]
endwhile
Answer: CREW

## Slide 21: 5.6 Matrix Multiplication
Sequential matrix multiplication
for i = 0 to m – 1 do
for j = 0 to m – 1 do
t := 0
for k = 0 to m – 1 do
t := t + aikbkj
endfor
cij := t
endfor
endfor
A
B
C
cij := Sk=0 to m–1 aikbkj
PRAM solution with m3 processors:
each processor does one multiplication
(not very efficient)
m  m
matrices

## Slide 22: PRAM Matrix Multiplication with m 2 Processors
Fig. 5.12 PRAM matrix multiplication; p = m2 processors.
PRAM matrix multiplication using m2 processors
Proc (i, j), 0  i, j < m, do
begin
t := 0
for k = 0 to m – 1 do
t := t + aikbkj
endfor
cij := t
end
Q(m) steps: Time-optimal
CREW model is implicit
Processors are numbered (i, j), instead of 0 to m2 – 1
A
B
C

## Slide 23: PRAM Matrix Multiplication with m Processors
PRAM matrix multiplication using m processors
for j = 0 to m – 1 Proc i, 0  i < m, do
t := 0
for k = 0 to m – 1 do
t := t + aikbkj
endfor
cij := t
endfor
Q(m2) steps: Time-optimal
CREW model is implicit
Because the order of multiplications is immaterial, accesses to B can be skewed to allow the EREW model
A
B
C

## Slide 24: PRAM Matrix Multiplication with Fewer Processors
Algorithm is similar, except that each processor is in charge of computing m / p rows of C
Q(m3/p) steps: Time-optimal
EREW model can be used
A drawback of all algorithms thus far is that only two arithmetic operations (one multiplication and one addition) are performed for each memory access.
This is particularly costly for NUMA shared-memory machines.
B
C
A

## Slide 25: More Efficient Matrix Multiplication (for NUMA)
Fig. 5.13 Partitioning the matrices for block matrix multiplication .
Block matrix multiplication follows the same algorithm as simple matrix multiplication.
p
p
q=m/p
Partition the matrices
into p square blocks

## Slide 26: Details of Block Matrix Multiplication
Fig. 5.14 How Processor (i, j) operates on an element of A and one block-row of B to update one block-row of C.
A multiply-add computation
on q  q blocks needs
2q 2 = 2m 2/p memory accesses and
2q 3 arithmetic operations
So, q arithmetic operations are done per memory access

## Slide 27: 6 More Shared-Memory Algorithms
Develop PRAM algorithm for more complex problems:
  Must present background on the problem in some cases
  Discuss some practical issues such as data distribution
Topics in This Chapter
6.1 Sequential Ranked-Based Selection
6.2 A Parallel Selection Algorithm
6.3 A Selection-Based Sorting Algorithm
6.4 Alternative Sorting Algorithms
6.5 Convex Hull of a 2D Point Set
6.6 Some Implementation Aspects

## Slide 28: 8.1 Searching and Dictionary Operations
Example:
n = 26, p = 2
A single search in a sorted list
can’t be significantly speeded up
through parallel processing,
but all hope is not lost:
Dynamic data (sorting overhead)
Batch searching (multiple lookups)
Parallel p-ary search on PRAM
logp+1(n + 1)
= log2(n + 1) / log2(p + 1)
= Q(log n / log p) steps
Speedup  log p
Optimal: no comparison-based
search algorithm can be faster

## Slide 29: 6.1 Sequential Ranked-Based Selection
Selection: Find the (or a) kth smallest among n elements
Example: 5th smallest element in the following list is 1:
6 4 5 6 7 1 5 3 8 2 1 0 3 4 5 6 2 1 7 1 4 5 4 9 5
Naive solution through sorting, O(n log n) time
But linear-time sequential algorithm can be developed
max(|L|, |G|)  3n/4

## Slide 30: Linear-Time Sequential Selection Algorithm
Sequential rank-based selection algorithm select(S, k)
1. if |S| < q {q is a small constant}
then sort S and return the kth smallest element of S
else divide S into |S|/q subsequences of size q
Sort each subsequence and find its median
Let the |S|/q medians form the sequence T
endif
2. m = select(T, |T|/2) {find the median m of the |S|/q medians}
3. Create 3 subsequences
L: Elements of S that are < m
E: Elements of S that are = m
G: Elements of S that are > m
4. if |L|  k
then return select(L, k)
else if |L| + |E|  k
then return m
else return select(G, k – |L| – |E|)
endif
endif
O(n)
T(n/q)
T(3n/4)
O(n)

## Slide 31: Algorithm Complexity and Examples
We must have q  5;
for q = 5, the solution is T(n) = 20cn
T(n) = T(n / q) + T(3n / 4) + cn
------------ n/q sublists of q elements -------------
S 6 4 5 6 7 1 5 3 8 2 1 0 3 4 5 6 2 1 7 1 4 5 4 9 5
--------- --------- --------- --------- ---------
T 6 3 3 2 5
m 3
1 2 1 0 2 1 1 3 3 6 4 5 6 7 5 8 4 5 6 7 4 5 4 9 5
------------- --- -------------------------------
L E G
|L| = 7 |E| = 2 |G| = 16
To find the 5th smallest element in S, select the 5th smallest element in L
S 1 2 1 0 2 1 1
--------- ---
T 1 1
m 1
0 1 1 1 1 2 2
- ------- ---
L E G
Answer: 1
The 9th smallest element of S is 3.
The 13th smallest element of S is found by selecting the 4th smallest element in G.

## Slide 32
Parallel rank-based selection algorithm PRAMselect(S, k, p)
1. if |S| < 4
then sort S and return the kth smallest element of S
else broadcast |S| to all p processors
divide S into p subsequences S(j) of size |S|/p
Processor j, 0  j < p, compute Tj := select(S(j), |S(j)|/2)
endif
2. m = PRAMselect(T, |T|/2, p) {median of the medians}
3. Broadcast m to all processors and create 3 subsequences
L: Elements of S that are < m
E: Elements of S that are = m
G: Elements of S that are > m
4. if |L|  k
then return PRAMselect(L, k, p)
else if |L| + |E|  k
then return m
else return PRAMselect(G, k – |L| – |E|, p)
endif
endif
O(n x)
T(n1–x, p)
T(3n/4, p)
O(n x)
6.2 A Parallel Selection Algorithm
Let p = O(n1–x)

## Slide 33: Algorithm Complexity and Efficiency
The solution is O(n x);
verify by substitution
T(n, p) = T(n1–x, p) + T(3n / 4, p) + cnx
Speedup = Q(n) / O(n x) = W(n1–x) = W(p)
Efficiency = W(1)
Work(n, p) = pT(n, p) = Q(n1–x) Q(n x) = Q(n)
What happens if we set x to 1? ( i.e., use one processor)
T(n, 1) = O(n x) = O(n)
What happens if we set x to 0? (i.e., use n processors)
T(n, n) = O(n x) = O(1) ?
Remember
p = O(n1–x)
No, because in asymptotic analysis,
we ignored several
O(log n) terms
compared with O(nx) terms

## Slide 34: 6.3 A Selection-Based Sorting Algorithm
Parallel selection-based sort PRAMselectionsort(S, p)
1. if |S| < k then return quicksort(S)
2. for i = 1 to k – 1 do
mj := PRAMselect(S, i|S|/k, p) {let m0 := –; mk := +}
endfor
3. for i = 0 to k – 1 do
make the sublist T(i) from elements of S in (mi, mi+1)
endfor
4. for i = 1 to k/2 do in parallel
PRAMselectionsort(T(i), 2p/k)
{p/(k/2) proc’s used for each of the k/2 subproblems}
endfor
5. for i = k/2 + 1 to k do in parallel
PRAMselectionsort(T(i), 2p/k)
endfor
O(n x)
T(n/k, 2p/k)
O(1)
O(n x)
Fig. 6.1 Partitioning of the sorted list for selection-based sorting.
T(n/k, 2p/k)
Let p = n1–x
and k = 21/x

## Slide 35: Algorithm Complexity and Efficiency
The solution is O(n x log n);
verify by substitution
T(n, p) = 2T(n/k, 2p/k) + cnx
Speedup(n, p) = W(n log n) / O(n x log n) = W(n1–x) = W(p)
Efficiency = speedup / p = W(1)
Work(n, p) = pT(n, p) = Q(n1–x) Q(n x log n) = Q(n log n)
What happens if we set x to 1? ( i.e., use one processor)
T(n, 1) = O(n x log n) = O(n log n)
Our asymptotic analysis is valid for x > 0 but not for x = 0;
i.e., PRAMselectionsort cannot sort p keys in optimal O(log p) time.
Remember
p = O(n1–x)

## Slide 36: Example of Parallel Sorting
S: 6 4 5 6 7 1 5 3 8 2 1 0 3 4 5 6 2 1 7 0 4 5 4 9 5
Threshold values for k = 4 (i.e., x = ½ and p = n1/2 processors):
m0 = –
n/k = 25/4  6 m1 = PRAMselect(S, 6, 5) = 2
2n/k = 50/4  13 m2 = PRAMselect(S, 13, 5) = 4
3n/k = 75/4  19 m3 = PRAMselect(S, 19, 5) = 6
m4 = +
m0 m1 m2 m3 m4
T: - - - - - 2|- - - - - - 4|- - - - - 6|- - - - - -
T: 0 0 1 1 1 2|2 3 3 4 4 4 4|5 5 5 5 5 6|6 6 7 7 8 9

## Slide 37: 6.4 Alternative Sorting Algorithms
Parallel randomized sort PRAMrandomsort(S, p)
1. Processor j, 0  j < p, pick |S|/p2 random samples of
its |S|/p elements and store them in its corresponding
section of a list T of length |S|/p
2. Processor 0 sort the list T
{comparison threshold mi is the (i |S| / p2)th element of T}
3. Processor j, 0  j < p, store its elements falling
in (mi, mi+1) into T(i)
4. Processor j, 0  j < p, sort the sublist T(j)
Sorting via random sampling (assume p <<  n)
Given a large list S of inputs, a random sample of the elements
can be used to find k comparison thresholds
It is easier if we pick k = p, so that each of the resulting
subproblems is handled by a single processor

## Slide 38: Parallel Radixsort
In binary version of radixsort, we examine every bit of the
k-bit keys in turn, starting from the LSB
In Step i, bit i is examined, 0  i < k
Records are stably sorted by the value of the ith key bit
Input Sort by Sort by Sort by
list LSB middle bit MSB
–––––– –––––– –––––– ––––––
5 (101) 4 (100) 4 (100) 1 (001)
7 (111) 2 (010) 5 (101) 2 (010)
3 (011) 2 (010) 1 (001) 2 (010)
1 (001) 5 (101) 2 (010) 3 (011)
4 (100) 7 (111) 2 (010) 4 (100)
2 (010) 3 (011) 7 (111) 5 (101)
7 (111) 1 (001) 3 (011) 7 (111)
2 (010) 7 (111) 7 (111) 7 (111)
Binary
forms
Question:
How are
the data
movements
performed?

## Slide 39: Data Movements in Parallel Radixsort
Running time consists mainly of the time to perform 2k parallel prefix computations: O(log p) for k constant
Input Compl. Diminished Prefix sums Shifted
list of bit 0 prefix sums Bit 0 plus 2 list
–––––– ––– –––––– ––– ––––––––– ––––––
5 (101) 0 – 1 1 + 2 = 3 4 (100)
7 (111) 0 – 1 2 + 2 = 4 2 (010)
3 (011) 0 – 1 3 + 2 = 5 2 (010)
1 (001) 0 – 1 4 + 2 = 6 5 (101)
4 (100) 1 0 0 – 7 (111)
2 (010) 1 1 0 – 3 (011)
7 (111) 0 – 1 5 + 2 = 7 1 (001)
2 (010) 1 2 0 – 7 (111)

## Slide 40: 6.5 Convex Hull of a 2D Point Set
Fig. 6.2 Defining the
convex hull problem.
Fig. 6.3 Illustrating the properties
of the convex hull.
Best sequential algorithm for p points:
W(p log p) steps

## Slide 41: PRAM Convex Hull Algorithm
Fig. 6.4 Multiway divide and conquer for the convex hull problem
Parallel convex hull algorithm PRAMconvexhull(S, p)
1. Sort point set by x coordinates
2. Divide sorted list into p subsets Q (i) of size p, 0  i < p
3. Find convex hull of each subset Q (i) using p processors
4. Merge p convex hulls CH(Q (i)) into overall hull CH(Q)
Upper
hull
Lower
hull

## Slide 42: Merging of Partial Convex Hulls
Fig. 6.5 Finding points in a partial hull that belong to the combined hull.
Analysis:
T(p, p)
= T(p1/2, p1/2) + c log p  2c log p
The initial sorting also takes O(log p) time
Tangent lines are found through binary search in log time

## Slide 43: 6.6 Some Implementation Aspects
Fig. 4.3 A parallel processor with global (shared) memory.
Options:
Crossbar
Bus(es)
MIN
Bottleneck
Complex
Expensive
This section has been expanded; it will eventually become a separate chapter

## Slide 44: Processor-to-Memory Network
Crossbar switches offer full permutation capability (they are nonblocking),
but are complex and expensive: O(p2)
An 8  8 crossbar switch
P0
P1
P2
P3
P4
P5
P6
P7
M0
M1
M2
M3
M4
M5
M6
M7
Practical processor-to-memory networks cannot realize all permutations
(they are blocking)
Even with a permutation network, full PRAM functionality is not realized: two processors cannot access different addresses in the same memory module

## Slide 45: Bus-Based Interconnections
Memory
Proc
Proc
Proc
Proc
. . .
I/O
Memory
Proc
Proc
Proc
Proc
. . .
I/O
Single-bus system:
Bandwidth bottleneck
Bus loading limit
Scalability: very poor
Single failure point
Conceptually simple
Forced serialization
Multiple-bus system:
Bandwidth improved
Bus loading limit
Scalability: poor
More robust
More complex scheduling
Simple serialization

## Slide 46: Back-of-the-Envelope Bus Bandwidth Calculation
Memory
Proc
Proc
Proc
Proc
. . .
I/O
Single-bus system:
Bus frequency: 0.5 GHz
Data width: 256 b (32 B)
Mem. Access: 2 bus cycles
(0.5G)/2  32 = 8 GB/s
Bus cycle = 2 ns
Memory cycle = 100 ns
1 mem. cycle = 50 bus cycles
Multiple-bus system:
Peak bandwidth multiplied by the number of buses
(actual bandwidth is likely to be much less)
Mem
Proc
Proc
Proc
Proc
. . .
I/O
Mem
Mem
Mem

## Slide 47: Hierarchical Bus Interconnection
Fig. 4.9 Example of a hierarchical interconnection architecture.
Heterogeneous system

## Slide 48: Removing the Processor-to-Memory Bottleneck
Fig. 4.4 A parallel processor with global memory and processor caches.
Challenge:
Cache coherence

## Slide 49: Why Data Caching Works
Fig. 18.1 Data storage and access in a two-way set-associative cache.
Hit rate r (fraction of memory accesses satisfied by cache)
Ceff = Cfast + (1 – r)Cslow
Cache parameters:
Size
Block length (line width)
Placement policy
Replacement policy
Write policy

## Slide 50: Benefits of Caching Formulated as Amdahl’s Law
Generalized form of Amdahl’s speedup formula:
S = 1/(f1/p1 + f2/p2 + . . . + fm/pm), with f1 + f2 + . . . + fm = 1
In this case, a fraction 1 – r is slowed down by a factor (Cslow + Cfast) / Cslow, and a fraction r is speeded up by a factor Cslow / Cfast
Fig. 18.3 of Parhami’s Computer Architecture text (2005)
This corresponds to the miss-rate fraction 1 – r of accesses being unaffected
and the hit-rate fraction r (almost 1) being speeded up by a factor Cslow/Cfast
Hit rate r (fraction of memory accesses satisfied by cache)
Ceff = Cfast + (1 – r)Cslow
S = Cslow / Ceff
1
=
(1 – r) + Cfast/Cslow

## Slide 51
18.2 Cache Coherence Protocols
Fig. 18.2 Various types of cached data blocks in a parallel processor with global memory and processor caches.

## Slide 52: Example: A Bus-Based Snoopy Protocol
Fig. 18.3 Finite-state control mechanism for a bus-based snoopy cache coherence protocol.
Each transition is labeled with the event that triggers it, followed by the action(s) that must be taken

## Slide 53: Implementing a Snoopy Protocol
Fig. 27.7 of Parhami’s Computer Architecture text.
A second tags/state storage unit allows snooping to be done concurrently with normal cache operation
Getting all the implementation timing and details right is nontrivial

## Slide 54: Distributed Shared Memory
Fig. 4.5 A parallel processor with distributed memory.
Some Terminology:
NUMA
Nonuniform memory access
(distributed shared memory)
UMA
Uniform memory access
(global shared memory)
COMA
Cache-only memory arch

## Slide 55: Example: A Directory-Based Protocol
Fig. 18.4 States and transitions for a directory entry in a directory-based coherence protocol (c denotes the cache sending the message).
sharing set +
Correction to text

## Slide 56: Implementing a Directory-Based Protocol
Sharing set implemented as a bit-vector (simple, but not scalable)
When there are many more nodes (caches) than the typical size of a sharing set, a list of sharing units may be maintained in the directory
0
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
1
1
0
0
0
0
0
0
0
1
0
0
0
0
The sharing set can be maintained as a distributed doubly linked list
(will discuss in Section 18.6 in connection with the SCI standard)

## Slide 57: Hiding the Memory Access Latency
By assumption, PRAM accesses memory locations right when they are needed, so processing must stall until data is fetched
Method 1: Predict accesses (prefetch)
Method 2: Pipeline multiple accesses
Not a smart strategy:
Memory access time =
100s times that of add time
Proc. 0’s access request
Proc. 0’s access response

## Slide 58: 21.3 Vector-Parallel Cray Y-MP
Fig. 21.5 Key elements of the Cray Y-MP processor. Address registers, address function units, instruction buffers, and control not shown.

## Slide 59: Cray Y-MP’s Interconnection Network
Fig. 21.6 The processor-to-memory interconnection network of Cray Y-MP.

## Slide 60: Butterfly Processor-to-Memory Network
Fig. 6.9 Example of a multistage memory access network.
Not a full permutation network
(e.g., processor 0 cannot be connected to memory bank 2 alongside the two connections shown)
Is self-routing: i.e., the bank address determines the route
A request going to memory bank 3
(0 0 1 1) is routed:
lower upper upper

## Slide 61: Butterfly as Multistage Interconnection Network
Fig. 6.9 Example of a multistage memory access network
Generalization of the butterfly network
High-radix or m-ary butterfly, built of m  m switches
Has mq rows and q + 1 columns (q if wrapped)
Fig. 15.8 Butterfly network used to connect modules that are on the same side

## Slide 62: Beneš Network
Fig. 15.9 Beneš network formed from two back-to-back butterflies.
A 2q-row Beneš network:
Can route any 2q  2q permutation
It is “rearrangeable”

## Slide 63: Routing Paths in a Beneš Network
Fig. 15.10 Another example of a Beneš network.
To which memory modules can we connect proc 4 without rearranging the other paths?
What about
proc 6?

## Slide 64: 16.6 Multistage Interconnection Networks
Numerous indirect or multistage interconnection networks (MINs) have been proposed for, or used in, parallel computers
They differ in topological, performance, robustness, and realizability attributes
We have already seen the butterfly, hierarchical bus, beneš, and ADM networks
Fig. 4.8 (modified)
The sea of indirect interconnection networks.

## Slide 65: Self-Routing Permutation Networks
Do there exist self-routing permutation networks? (The butterfly network is self-routing, but it is not a permutation network)
Permutation routing through a MIN is the same problem as sorting
Fig. 16.14 Example of sorting on a binary radix sort network.

## Slide 66: Partial List of Important MINs
Augmented data manipulator (ADM): aka unfolded PM2I (Fig. 15.12)
Banyan: Any MIN with a unique path between any input and any output (e.g. butterfly)
Baseline: Butterfly network with nodes labeled differently
Beneš: Back-to-back butterfly networks, sharing one column (Figs. 15.9-10)
Bidelta: A MIN that is a delta network in either direction
Butterfly: aka unfolded hypercube (Figs. 6.9, 15.4-5)
Data manipulator: Same as ADM, but with switches in a column restricted to same state
Delta: Any MIN for which the outputs of each switch have distinct labels (say 0 and 1
for 2  2 switches) and path label, composed of concatenating switch output labels
leading from an input to an output depends only on the output
Flip: Reverse of the omega network (inputs  outputs)
Indirect cube: Same as butterfly or omega
Omega: Multi-stage shuffle-exchange network; isomorphic to butterfly (Fig. 15.19)
Permutation: Any MIN that can realize all permutations
Rearrangeable: Same as permutation network
Reverse baseline: Baseline network, with the roles of inputs and outputs interchanged

## Slide 67: Conflict-Free Memory Access
Try to store the data such that parallel accesses are to different banks
For many data structures, a compiler may perform the memory mapping
Fig. 6.6 Matrix storage in column-major order to allow concurrent accesses to rows.
Accessing a column
leads to conflicts
Each matrix column is stored in a different memory module (bank)

## Slide 68: Skewed Storage Format
Fig. 6.7 Skewed matrix storage for conflict-free accesses to rows and columns.

## Slide 69: A Unified Theory of Conflict-Free Access
Fig. 6.8 A 6  6 matrix viewed, in column-major order, as a 36-element vector.
Column: k, k+1, k+2, k+3, k+4, k+5 Stride = 1
Row: k, k+m, k+2m, k+3m, k+4m, k+5m Stride = m
Diagonal: k, k+m+1, k+2(m+1), k+3(m+1),
k+4(m+1), k+5(m+1) Stride = m + 1
Antidiagonal: k, k+m–1, k+2(m–1), k+3(m–1),
k+4(m–1), k+5(m–1) Stride = m – 1
A qD array can be
viewed as a vector,
with “row” / “column”
accesses associated
with constant strides

## Slide 70: Linear Skewing Schemes
Fig. 6.8 A 6  6 matrix viewed, in column-major order, as a 36-element vector.
With a linear skewing scheme, vector elements k, k + s, k +2s, . . . ,
k + (B – 1)s will be assigned to different memory banks iff sb is relatively prime with respect to the number B of memory banks.
A prime value for B ensures this condition, but is not very practical.
Place vector element i in memory bank
a + bi mod B
(word address within bank is irrelevant to conflict-free access;
also, a can be set to 0)

## Slide 71: 7 Sorting and Selection Networks
Become familiar with the circuit model of parallel processing:
  Go from algorithm to architecture, not vice versa
  Use a familiar problem to study various trade-offs
Topics in This Chapter
7.1 What is a Sorting Network?
7.2 Figures of Merit for Sorting Networks
7.3 Design of Sorting Networks
7.4 Batcher Sorting Networks
7.5 Other Classes of Sorting Networks
7.6 Selection Networks

## Slide 72: 7.1 What is a Sorting Network?
Fig. 7.1 An n-input sorting network or an n-sorter.
Fig. 7.2 Block diagram and four different schematic representations for a 2-sorter.

## Slide 73: Building Blocks for Sorting Networks
2-sorter
Fig. 7.3 Parallel and bit-serial hardware realizations of a 2-sorter.
Implementation with bit-parallel inputs
Implementation with bit-serial inputs

## Slide 74: Proving a Sorting Network Correct
Fig. 7.4 Block diagram and schematic representation of a 4-sorter.
Method 1: Exhaustive test – Try all n! possible input orders
Method 2: Ad hoc proof – for the example above, note that y0 is smallest, y3 is largest, and the last comparator sorts the other two outputs
Method 3: Use the zero-one principle – A comparison-based sorting algorithm is correct iff it correctly sorts all 0-1 sequences (2n tests)

## Slide 75: Elaboration on the Zero-One Principle
Deriving a 0-1 sequence that is not correctly sorted, given an arbitrary sequence that is not correctly sorted.
Let outputs yi and yi+1 be out of order, that is yi > yi+1
Replace inputs that are strictly less than yi with 0s and all others with 1s
The resulting 0-1 sequence will not be correctly sorted either

## Slide 76: 7.2 Figures of Merit for Sorting Networks
Delay: Number of levels
Cost: Number of comparators
Cost  Delay
In the following example, we have 5 comparators
The following 4-sorter has 3 comparator levels on its critical path
The cost-delay product for this example is 15
Fig. 7.4 Block diagram and schematic representation of a 4-sorter.

## Slide 77: Cost as a Figure of Merit
Fig. 7.5 Some low-cost sorting networks.

## Slide 78: Delay as a Figure of Merit
Fig. 7.6 Some fast sorting networks.
These 3 comparators constitute one level

## Slide 79: Cost-Delay Product as a Figure of Merit
Fast 10-sorter from Fig. 7.6
Low-cost 10-sorter from Fig. 7.5
Cost  Delay = 29  9 = 261
Cost  Delay = 31  7 = 217
The most cost-effective n-sorter may be neither
the fastest design, nor the lowest-cost design

## Slide 80: 7.3 Design of Sorting Networks
Fig. 7.7 Brick-wall 6-sorter based on odd–even transposition.
C(n) = n(n – 1)/2
D(n ) = n
Cost  Delay = n2(n – 1)/2 = Q(n3)

## Slide 81: Insertion Sort and Selection Sort
Fig. 7.8 Sorting network based on insertion sort or selection sort.
C(n) = n(n – 1)/2
D(n ) = 2n – 3
Cost  Delay
= Q(n3)

## Slide 82: Theoretically Optimal Sorting Networks
AKS sorting network
(Ajtai, Komlos, Szemeredi: 1983)
O(log n) depth
O(n log n)
size
Unfortunately, AKS networks are not practical owing to large (4-digit) constant factors involved; improvements since 1983 not enough
Note that even for these optimal networks, delay-cost product is suboptimal; but this is the best we can do
Existing sorting networks have O(log2 n) latency and O(n log2 n) cost
Given that log2 n is only 20 for n = 1 000 000, the latter are more practical

## Slide 83: 7.4 Batcher Sorting Networks
Fig. 7.9 Batcher’s even–odd merging network for 4 + 7 inputs.
(2, 3)-merger
a0
a1
b0
b1
b2
(1, 2)-merger
c0
d0
d1
(1, 1)
(1, 2)
(1, 1)

## Slide 84: Proof of Batcher’s Even-Odd Merge
Use the zero-one principle
Assume: x has k 0s
y has k  0s
Case a: keven = kodd v 0 0 0 0 0 0 1 1 1 1 1 1
w 0 0 0 0 0 0 1 1 1 1 1
Case b: keven = kodd+1 v 0 0 0 0 0 0 0 1 1 1 1 1
w 0 0 0 0 0 0 1 1 1 1 1
Case c: keven = kodd+2 v 0 0 0 0 0 0 0 0 1 1 1 1
w 0 0 0 0 0 0 1 1 1 1 1
Out of order
v has keven = k/2 + k /2 0s
w has kodd = k/2 + k /2 0s

## Slide 85: Batcher’s Even-Odd Merge Sorting
Batcher’s (m, m) even-odd merger,
for m a power of 2:
C(m) = 2C(m/2) + m – 1
= (m – 1) + 2(m/2 – 1) + 4(m/4 – 1) + . . .
= m log2m + 1
D(m) = D(m/2) + 1 = log2 m + 1
Cost  Delay = Q(m log2 m)
Batcher sorting networks based on the
even-odd merge technique:
C(n) = 2C(n/2) + (n/2)(log2(n/2)) + 1
 n(log2n)2/ 2
D(n) = D(n/2) + log2(n/2) + 1
= D(n/2) + log2n
= log2n (log2n + 1)/2
Cost  Delay = Q(n log4n)
Fig. 7.10 The recursive structure of Batcher’s even–odd merge sorting network.

## Slide 86: Example Batcher’s Even-Odd 8-Sorter
Fig. 7.11 Batcher’s even-odd merge sorting network for eight inputs .

## Slide 87: Bitonic-Sequence Sorter
Fig. 14.2 Sorting a bitonic sequence on a linear array.
Bitonic sequence:
1 3 3 4 6 6 6 2 2 1 0 0 Rises, then falls
8 7 7 6 6 6 5 4 6 8 8 9 Falls, then rises
8 9 8 7 7 6 6 6 5 4 6 8 The previous sequence, right-rotated by 2

## Slide 88: Batcher’s Bitonic Sorting Networks
Fig. 7.12 The recursive structure of Batcher’s bitonic sorting network.
Fig. 7.13 Batcher’s bitonic sorting network for eight inputs.

## Slide 89: 7.5 Other Classes of Sorting Networks
Fig. 7.14 Periodic balanced sorting network for eight inputs.
Desirable properties:
a. Regular / modular (easier VLSI layout).
b. Simpler circuits via reusing the blocks
c. With an extra block tolerates some faults (missed exchanges)
d. With 2 extra blocks provides tolerance to single faults (a missed or incorrect exchange)
e. Multiple passes through faulty network (graceful degradation)
f. Single-block design becomes fault-tolerant by using an extra stage

## Slide 90: Shearsort-Based Sorting Networks (1)
Fig. 7.15 Design of an 8-sorter based on shearsort on 24 mesh.

## Slide 91: Shearsort-Based Sorting Networks (2)
Fig. 7.16 Design of an 8-sorter based on shearsort on 24 mesh.
Some of the same
advantages as
periodic balanced
sorting networks

## Slide 92: 7.6 Selection Networks
Direct design may yield simpler/faster selection networks
Deriving an (8, 3)-selector from Batcher’s even-odd merge 8-sorter.

## Slide 93: Categories of Selection Networks
Unfortunately we know even less about selection networks
than we do about sorting networks.
One can define three selection problems [Knut81]:
I. Select the k smallest values; present in sorted order
II. Select kth smallest value
III. Select the k smallest values; present in any order
Circuit and time complexity: (I) hardest, (III) easiest
Classifiers:
Selectors that separate the smaller half of values from the larger half
Smaller
4 values
Larger
4 values
8 inputs
8-Classifier

## Slide 94: Type-III Selection Networks
Figure 7.17 A type III (8, 4)-selector.
8-Classifier

## Slide 95: 8 Other Circuit-Level Examples
Complement our discussion of sorting and sorting nets with:
  Searching, parallel prefix computation, Fourier transform
  Dictionary machines, parallel prefix nets, FFT circuits
Topics in This Chapter
8.1 Searching and Dictionary Operations
8.2 A Tree-Structured Dictionary Machine
8.3 Parallel Prefix Computation
8.4 Parallel Prefix Networks
8.5 The Discrete Fourier Transform
8.6 Parallel Architectures for FFT

## Slide 96: 8.1 Searching and Dictionary Operations
Example:
n = 26, p = 2
A single search in a sorted list
can’t be significantly speeded up
through parallel processing,
but all hope is not lost:
Dynamic data (sorting overhead)
Batch searching (multiple lookups)
Parallel p-ary search on PRAM
logp+1(n + 1)
= log2(n + 1) / log2(p + 1)
= Q(log n / log p) steps
Speedup  log p
Optimal: no comparison-based
search algorithm can be faster

## Slide 97: Dictionary Operations
Basic dictionary operations: record keys x0, x1, . . . , xn–1
search(y) Find record with key y; return its associated data
insert(y, z) Augment list with a record: key = y, data = z
delete(y) Remove record with key y; return its associated data
Some or all of the following operations might also be of interest:
findmin Find record with smallest key; return data
findmax Find record with largest key; return data
findmed Find record with median key; return data
findbest(y) Find record with key “nearest” to y
findnext(y) Find record whose key is right after y in sorted order
findprev(y) Find record whose key is right before y in sorted order
extractmin Remove record(s) with min key; return data
extractmax Remove record(s) with max key; return data
extractmed Remove record(s) with median key value; return data
Priority queue operations: findmin, extractmin (or findmax, extractmax)

## Slide 98: 8.2 A Tree-Structured Dictionary Machine
Fig. 8.1 A tree-structured dictionary machine.
Combining in the triangular nodes
search(y): Pass OR of match signals & data from “yes” side
findmin / findmax: Pass smaller / larger of two keys & data
findmed:
Not supported here
findbest(y): Pass
the larger of two match-degree indicators along with associated record
Search 1
Search 2
Pipelined
search

## Slide 99: Insertion and Deletion in the Tree Machine
Figure 8.2 Tree machine storing 5 records and containing 3 free slots.
Counters keep track of the vacancies
in each subtree
Deletion needs second pass to update the vacancy counters
Redundant
insertion (update?)
and deletion (no-op?)
Implementation:
Merge the circle and
triangle trees by folding

## Slide 100: Systolic Data Structures
Fig. 8.3 Systolic data structure
for minimum, maximum,
and median finding.
Each node holds the smallest (S), median (M),,and largest (L)
value in its subtree
Each subtree is balanced
or has one fewer element on the left (root flag shows this)
Update/access examples for the systolic data structure of Fig. 8.3
Example: 20 elements,
3 in root, 8 on left,
and 9 on right
8 elements:
3 + 2 + 3

## Slide 101: 8.3 Parallel Prefix Computation
Fig. 8.4 Prefix computation using a latched or pipelined function unit.
Example: Prefix sums
x0 x1 x2 . . . xi
x0 x0 + x1 x0 + x1 + x2 . . . x0 + x1 + . . . + xi
s0 s1 s2 . . . si
Sequential time with one processor is O(n)
Simple pipelining does not help

## Slide 102: Improving the Performance with Pipelining
Fig. 8.5 High-throughput prefix computation using a pipelined function unit.
Ignoring pipelining overhead, it appears that we have achieved a speedup of 4 with 3 “processors.”
Can you explain this anomaly? (Problem 8.6a)

## Slide 103: 8.4 Parallel Prefix Networks
Fig. 8.6 Prefix sum network built of one n/2-input network and n – 1 adders.
T(n) = T(n/2) + 2
= 2 log2n – 1
C(n) = C(n/2) + n – 1
= 2n – 2 – log2n
This is the Brent-Kung
Parallel prefix network
(its delay is actually
2 log2n – 2)

## Slide 104: Example of Brent-Kung Parallel Prefix Network
Fig. 8.8 Brent–Kung parallel prefix graph for n = 16.
One level of latency
Originally developed
by Brent and Kung as
part of a VLSI-friendly
carry lookahead adder
T(n) = 2 log2n – 2
C(n) = 2n – 2 – log2n

## Slide 105: Another Divide-and-Conquer Design
Fig. 8.7 Prefix sum network built of two n/2-input networks and n/2 adders.
T(n) = T(n/2) + 1
= log2n
C(n) = 2C(n/2) + n/2
= (n/2) log2n
Simple Ladner-Fisher
Parallel prefix network
(its delay is optimal,
but has fan-out issues
if implemented directly)
Ladner-Fischer construction

## Slide 106: Example of Kogge-Stone Parallel Prefix Network
Fig. 8.9 Kogge-Stone parallel prefix graph for n = 16.
T(n) = log2n
C(n) = (n – 1) + (n – 2)
+ (n – 4) + . . . + n/2
= n log2n – n – 1
Optimal in delay,
but too complex
in number of cells
and wiring pattern

## Slide 107: Comparison and Hybrid Parallel Prefix Networks
Fig. 8.10 A hybrid Brent–Kung / Kogge–Stone parallel prefix graph for n = 16.
Brent/Kung
6 levels
26 cells
Kogge/Stone
4 levels
49 cells
Han/Carlson
5 levels
32 cells

## Slide 108: Linear-Cost, Optimal Ladner-Fischer Networks
Recursive construction of the fastest possible parallel prefix network (type-0)
Define a type-x parallel prefix network as one that:
Produces the leftmost output in optimal log2 n time
Yields all other outputs with at most x additional delay
We are interested in building a type-0 overall network, but can use type-x networks (x > 0) as component parts
Note that even the Brent-Kung network produces the leftmost output in optimal time

## Slide 109: 8.5 The Discrete Fourier Transform
DFT yields output sequence yi based on input sequence xi (0  i < n)
yi = ∑j=0 to n–1wnij xj O(n2)-time naïve algorithm
where wn is the nth primitive root of unity; wnn = 1, wnj ≠ 1 (1  j < n)
Examples: w4 is the imaginary number i and w3 = (-1 + i 3)/2
The inverse DFT is almost exactly the same computation:
xi = (1/n) ∑j=0 to n–1wn-ij yj
Fast Fourier Transform (FFT):
O(n log n)-time DFT algorithm that derives y from half-length sequences
u and v that are DFTs of even- and odd-indexed inputs, respectively
yi = ui + wni vi (0  i < n/2)
yi+n/2 = ui + wni+n/2 vi
T(n) = 2T(n/2) + n = n log2n sequentially
T(n) = T(n/2) + 1 = log2n in parallel

## Slide 110: Application of DFT to Spectral Analysis

## Slide 111: Application of DFT to Smoothing or Filtering

## Slide 112: 8.6 Parallel Architectures for FFT
Fig. 8.11 Butterfly network for an 8-point FFT.
u: DFT of even-indexed inputs
v: DFT of odd-indexed inputs
yi = ui + wni vi (0  i < n/2)
yi+n/2 = ui + wni+n/2 vi

## Slide 113: Variants of the Butterfly Architecture
Fig. 8.12 FFT network variant and its shared-hardware realization.

## Slide 114: Computation Scheme for 16-Point FFT

## Slide 115: More Economical FFT Hardware
Fig. 8.13 Linear array of log2n cells for n-point FFT computation.

## Slide 116: Another Circuit Model: Artificial Neural Nets
Supervised learning
Inputs
Weights
Activation function
Output
Threshold
Feedforward network
Three layers: input, hidden, output
No feedback
Artificial neuron
Recurrent network
Simple version due to Elman
Feedback from hidden nodes to special nodes at the input layer
Diagrams from
http://www.learnartificialneuralnetworks.com/
Hopfield network
All connections are bidirectional
Characterized by connection topology and learning method