## Slide 1: Part III Mesh-Based Architectures

## Slide 2
About This Presentation
This presentation is intended to support the use of the textbook Introduction to Parallel Processing: Algorithms and Architectures (Plenum Press, 1999, ISBN 0-306-45970-1). It was prepared by the author in connection with teaching the graduate-level course
ECE 254B: Advanced Computer Architecture: Parallel Processing, at the University of California, Santa Barbara. Instructors can use these slides in classroom teaching and for other educational purposes. Any other use is strictly prohibited. © Behrooz Parhami
Edition | Released | Revised | Revised | Revised
First | Spring 2005 | Spring 2006 | Fall 2008 | Fall 2010
 |  | Winter 2013 | Winter 2014 | Winter 2016
 |  | Winter 2019 | Winter 2020 | Winter 2021

## Slide 3: III Mesh-Type Architectures
Study mesh, torus, and related interconnection schemes:
  Many modern parallel machines are mesh/torus-based
  Scalability and speed due to short, regular wiring
  Enhanced meshes, variants, and derivative networks
Topics in This Part
Chapter 9 Sorting on a 2D Mesh or Torus
Chapter 10 Routing on a 2D Mesh or Torus
Chapter 11 Numerical 2D Mesh Algorithms
Chapter 12 Mesh-Related Architectures

## Slide 4: 9 Sorting on a 2D Mesh or Torus
Introduce the mesh model (processors, links, communication):
  Develop 2D mesh sorting algorithms
  Learn about strengths and weaknesses of 2D meshes
Topics in This Chapter
9.1 Mesh-Connected Computers
9.2 The Shearsort Algorithm
9.3 Variants of Simple Shearsort
9.4 Recursive Sorting Algorithms
9.5 A Nontrivial Lower Bound
9.6 Achieving the Lower Bound

## Slide 5: 9.1 Mesh-Connected Computers
Fig. 9.1 Two-dimensional mesh-connected computer.
2D, four-neighbor (NEWS) mesh; other types in Chapter 12
Square p1/2  p1/2 or rectangular r  p/r
MIMD, SPMD, SIMD, Weak SIMD
Single/All-port model
Diameter-based or bisection-based lower bound: O(p1/2)
Input/output via boundary processors?
Column wraparound link for torus
Row wraparound link for torus

## Slide 6: MIMD, SPMD, SIMD, or Weak SIMD Mesh
Some communication modes.
All-port: Processor can communicate with all its neighbors at once (in one cycle or time step)
Single-port: Processor can send/receive one message per time step
MIMD: Processors choose their communication directions independently
SIMD: All processors directed to do the same
Weak SIMD: Same direction for all (uniaxis)

## Slide 7: Torus Implementation without Long Wires
Fig. 9.2 A 5  5 torus folded along its columns. Folding this diagram along the rows will produce a layout with only short links.
8 x 8 folded torus

## Slide 8: Processor Indexing in Mesh or Torus
Fig. 9.3 Some linear indexing schemes for the processors in a 2D mesh.
Our focus will be on row-major and snakelike row-major indexing

## Slide 9: Register-Based Communication
Fig. 9.4 Reading data from NEWS neighbors via virtual local registers.
0
North
East
West
South
Buffer
$0
$1
$2
$3
$4
$5
$6
$7
.
.
.

## Slide 10: 9.2 The Shearsort Algorithm
Fig. 9.5 Description of the shearsort algorithm on an
r-row 2D mesh.
Tshearsort = log2r (p/r + r) + p/r
On a square mesh:
Tshearsort = p1/2(log2p + 1)
Diameter-based LB:
Tsort  2p1/2 – 2

## Slide 11: Proving Shearsort Correct
Fig. 9.6 A pair of dirty rows create at least one clean row in each shearsort iteration
Assume that in doing the column sorts, we first sort pairs of elements in the column and then sort the entire column

## Slide 12: Shearsort Proof (Continued)
Fig. 9.7 The number of dirty rows halves with each shearsort iteration.
0
1
After log2r iterations, only one dirty row remains
0
1
00111010011010110

## Slide 13: Shearsort Example
Fig. 9.8 Example of shearsort on a 4  4 mesh.

## Slide 14: 9.3 Variants of Simple Shearsort
Observation: On a linear array, odd-even transposition sort needs only k steps if the “dirty” (unsorted) part of the array is of length k
0 0 0 0 0 0 1 1 0 1 0 0 0 1 0 1 1 1 1 1 1
Unsorted part
In shearsort, we do not have to sort columns completely, because only a portion of the column is unsorted (the portion shrinks in each phase)
On a square mesh:
Topt shearsort =
p1/2(½ log2p + 3) – 2
Topt shearsort = (p / r)(log2r + 1) +
r + r/2 + . . . + 2
2r – 2
Thus, 2r – 2 replaces r log2r in simple shearsort

## Slide 15: Shearsort with Multiple Items per Processor
Fig. 9.9 Example of shearsort on a 4  4 mesh with two keys stored per processor.
Perform ordinary shearsort, but replace compare-exchange with merge-split
(n/p) log2(n/p) steps for the initial sort; the rest multiplied by n/p

## Slide 16: 9.4 Recursive Sorting Algorithms
Fig. 9.10 Graphical depiction of the first recursive algorithm for sorting on a 2D mesh based on four-way divide and conquer.
Snakelike sorting order on a square mesh
T(p1/2) = T(p1/2/2) + 5.5p1/2
Note that row sort in phase 2 needs fewer steps
Trecursive 1  11p1/2

## Slide 17: Proof of the 11p1/2-Time Sorting Algorithm
Fig. 9.11 The proof of the first recursive sorting algorithm for 2D meshes.
x + x'  b + c + (a – b)/2 + (d – c)/2 + a' + d' + (b' – a')/2 + (c' – d')/2
 b + c + a' + d' + (a – b)/2 + (d – c)/2 + (b' – a')/2 + (c' – d')/2 – 4½
= (a + a')/2 + (b + b')/2 + (c + c')/2 + (d + d')/2 – 2
 p1/2 – 4
x  b + c + (a – b)/2 + (d – c)/2 A similar inequality applies to x'

## Slide 18: Some Programming Considerations
Let b (a power of 2) be the block length for snakelike sorting
snakelike-mesh-sort(b)
snakelike-mesh-sort(b/2)
snakelike-row-sort(b)
column-sort(b)
snake-odd-even-xpose(4b)
Fig. 9.10
Fig. 9.4
snakelike-row-sort(b)
for k = 0 to b – 1 Proc (i, j), j even, do
case i, k
even, even: if j  0 mod b AND
(R5) < (R3) then R5  R3
even, odd: if (R2) < (R5) then R2  R5
. . .

## Slide 19: Another Recursive Sorting Algorithm
Fig. 9.12 Graphical depiction of the second recursive algorithm for sorting on a 2D mesh based on four-way divide and conquer.
T(p1/2) = T(p1/2/2) + 4.5p1/2
Note that the distribution in phase 2 needs ½ p1/2 steps
Trecursive 2  9p1/2

## Slide 20: Proof of the 9p1/2-Time Sorting Algorithm
Fig. 9.13 The proof of the second recursive sorting algorithm for 2D meshes.

## Slide 21: Our Progress in Mesh Sorting Thus Far
Upper bounds: Deriving/analyzing algorithms and proving them correct
Lower bounds: Theoretical arguments based on bisection width, and the like
p1/2 log2p
Shearsort
11p1/2
9p1/2
2p1/2
Diameter
3p1/2
For snakelike
order only
(proved next)
Problem 9.9
Schnorr/Shamir
algorithm

## Slide 22: 9.5 A Nontrivial Lower Bound
Fig. 9.14 The proof of the 3p1/2 – o(p1/2) lower bound for sorting in snakelike row-major order.
The proof is complete if we show that the highlighted element must move by p1/2 steps in some cases

## Slide 23: Proving the Lower Bound
Fig. 9.15 Illustrating the effect of fewer or more 0s in the shaded area.
Any of the values 1-63 can be forced into any desired column in sorted order by mixing 0s and 64s in the shaded area

## Slide 24: Proving the Lower Bound
Fig. 9.15 (Alternate version) Illustrating the effect of fewer or more 0s in the shaded area.
Any of the values 1-63 can be forced into any desired column in sorted order by mixing 0s and 64s in the shaded area
0
0
0
0
1
0
0
0
2
3
0
0
4
5
6
0
7
8
9
10
11
12
13
14
15
16
16
16
16
1
16
16
16
2
3
16
16
4
5
6
16
7
8
9
10
11
12
13
14
15
0
0
0
0
0
0
0
0
0
0
1
2
3
4
5
10
9
8
7
6
11
12
13
14
15
1
2
3
4
5
10
9
8
7
6
11
12
13
14
15
16
16
16
16
16
16
16
16
16
16

## Slide 25: 9.6 Achieving the Lower Bound
Schnorr-Shamir snakelike sorting
1. Sort each block in snakelike order
2. Permute columns such that the columns of each vertical slice are evenly distributed among all slices
3. Sort each block in snakelike order
4. Sort columns from top to bottom
5. Sort Blocks 0&1, 2&3, . . . of all vertical slices together in snakelike order; i.e., sort within 2p3/8  p3/8 submeshes
6. Sort Blocks 1&2, 3&4, . . . of all vertical slices together in snakelike order
7. Sort rows in snakelike order
8. Apply 2p3/8 steps of odd-even transposition to the snake
Fig. 9.16 Notation for the asymptotically optimal sorting algorithm.

## Slide 26: Elaboration on the 3p1/2 Lower Bound
In deriving the 3p1/2 lower bound for snakelike sorting on a square mesh, we implicitly assumed that each processor holds one item at all times
Without this assumption, the following algorithm leads to a running time of about 2.5p1/2
Phase 1: Move all data to the center p1/2/2 columns
Phase 2: Perform 2-2 sorting in the half-wide center mesh
Phase 3: Distribute data from center half of each row to the entire row
p1/2/2
p1/2/4
2p1/2
p1/2/4

## Slide 27: 10 Routing on a 2D Mesh or Torus
Routing is nonexistent in PRAM, hardwired in circuit model:
  Study point-to-point and collective communication
  Learn how to route multiple data packets to destinations
Topics in This Chapter
10.1 Types of Data Routing Operations
10.2 Useful Elementary Operations
10.3 Data Routing on a 2D Array
10.4 Greedy Routing Algorithms
10.5 Other Classes of Routing Algorithms
10.6 Wormhole Routing

## Slide 28: 10.1 Types of Data Routing Operations
Point-to-point communication: one source, one destination
Collective communication
One-to-many: multicast, broadcast (one-to-all), scatter
Many-to-one: combine (fan-in), global combine, gather
Many-to-many: all-to-all broadcast (gossiping), scatter-gather

## Slide 29: Types of Data Routing Algorithms
Oblivious: A source-destination pair leads to a unique path;
non-fault-tolerant
Adaptive: One of the available paths is chosen dynamically;
can avoid faulty nodes/links or route around congested areas
Degree of adaptivity leads to trade-offs between decision simplicity
(e.g., hard to avoid infinite loops) and routing flexibility
Optimal (shortest-path): Only shortest paths considered; can be oblivious or adaptive
Non-optimal (non-shortest-path): Selection of shortest path is not guaranteed, although most algorithms tend to choose a shortest path if possible

## Slide 30: Our First Encounter with Data Routing Issues
Shared memory: Processors can communicate by storing data into and reading data from the memory
Circuit model: Sending results from one part of the system to other parts is hardwired at design time
Graph model: We must specify the routing process explicitly
Sorting network

## Slide 31: 1-to-1 Communication (Point-to-Point Messages)
Message
sources, destinations,
and routes
a
b
c
d
e
f
g
h
a
b
d
e
f
g
h
a
b
d
e
f
g
h
a
b
d
g
a
b
Source nodes
a
b
c
d
e
f
g
h
Destination nodes
c

## Slide 32: Routing Operations Specific to Meshes
Data compaction or packing
Move scattered data elements to the smallest possible submesh (e.g., for problem size reduction)
Random-access write (RAW)
Emulates one write step in PRAM (EREW vs CRCW)
Routing algorithm is critical
Random-access read (RAR)
Can be performed as two RAWs: Write source addresses to destinations; write data back to sources (emulates on PRAM memory read step)
Fig. 10.1 Example of data compaction or packing.

## Slide 33
10.2 Useful Elementary Operations
Row/Column rotation
All-to-all broadcasting in a row or column
Sorting in various orders
Chapter 9
Semigroup computation
Fig. 10.2 Recursive semigroup computation in a 2D mesh.
Parallel prefix computation
Fig. 10.3 Recursive parallel prefix compu-tation in a 2D mesh.

## Slide 34: Routing on a Linear Array (Mesh Row or Column)
Fig. 10.4 Example of routing multiple packets on a linear array.

## Slide 35: 10.3 Data Routing on a 2D Array
Fig. 10.5 Example of random-access write on a 2D mesh.
Exclusive random-access write on a 2D mesh: MeshRAW
1. Sort packets in column-major order by destination column number; break ties by destination row number
2. Shift packets to the right, so that each item is in the correct column (no conflict; at most one element in a row headed for a given column)
3. Route the packets within each column

## Slide 36: Analysis of Sorting-Based Routing Algorithm
Not a shortest-path algorithm
T = 3p1/2 + o(p1/2) {snakelike sorting}
+ p1/2 {odd column reversals}
+ 2p1/2 – 2 {row & column routing}
= 6p1/2 + o(p1/2)
= 11p1/2 + o(p1/2) with unidirectional commun.
Node buffer space requirement: 1 item at any given time

## Slide 37: 10.4 Greedy Routing Algorithms
Fig. 10.6 Greedy row-first routing on a 2D mesh.
Greedy algorithm: In each step, try to make the most progress toward the solution based on current conditions or information available
This local or short-term optimization often does not lead to a globally optimal solution; but, problems with optimal greedy algorithms do exist

## Slide 38: Analysis of Row-First Greedy Routing
T = 2p1/2 – 2
This optimal time achieved if we give priority to messages that need to go further along a column
Fig. 10.7 Demonstrating the worst-case buffer requirement with row-first routing.
Thus far, we have two mesh routing algorithms:
6p1/2-step, 1 buffer per node
2p1/2-step, time-optimal, but needs large buffers
Question: Is there a middle ground?

## Slide 39: An Intermediate Routing Algorithm
Sort (p1/2/q)  (p1/2/q) submeshes in
column-major order
Perform greedy routing
Fig. 10.8 Illustrating the structure of the intermediate routing algorithm.
Let there be rk packets in Bk headed for column j
Number of row-i packets headed for column j:
∑k=0 to q – 1rk / (p1/2/q)
< ∑ [1 + rk / (p1/2 / q)]
 q + (q / p1/2)∑rk  2q
So, 2q – 1 buffers suffice

## Slide 40: Analysis of the Intermediate Algorithm
Sort time: 4p1/2/q + o(p1/2/q)
Routing time: 2p1/2
Total time:  2p1/2 + 4p1/2/q
Fig. 10.8 Illustrating the structure of the intermediate routing algorithm.
One extreme, q = 1:
Degenerates into
sorting-based routing
Another extreme, large q:
Approaches the greedy routing algorithm
Buffers: 2q – 1,
Intermediate between
1 and O(p1/2)

## Slide 41: 10.5 Other Classes of Routing Algorithms
Row-first greedy routing has very good average-case performance, even if the node buffer size is restricted
Idea: Convert any routing problem to two random instances by picking a random intermediate node for each message
Fig. 10.9 Combining of write requests headed for the same destination.
Regardless of the routing algorithm used, concurrent writes can degrade the performance
Priority or combining scheme can be built into the routing algorithm so that congestion close to the common destination is avoided

## Slide 42: Types of Routing Problems or Algorithms
Static: Packets to be routed all available at t = 0
Dynamic: Packets “born” in the course of computation
Off-line: Routes precomputed, stored in tables
On-line: Routing decisions made on the fly
Oblivious: Path depends only on source and destination
Adaptive: Path may vary by link and node conditions
Deflection: Any received packet leaves immediately,
even if this means misrouting (via detour path);
also known as hot-potato routing
x
x

## Slide 43: 10.6 Wormhole Routing
Circuit switching: A circuit is established between source and destination before message is sent (as in old telephone networks)
Advantage: Fast transmission after the initial overhead
Packet switching: Packets are sent independently over possibly different paths
Advantage: Efficient use of channels due to sharing
Wormhole switching:
Combines the advantages of circuit and packet switching
Fig. 10.10 Worms and deadlock in wormhole routing.

## Slide 44: Route Selection in Wormhole Switching
Routing algorithm must be simple to make the route selection quick
Example: row-first routing, with 2-byte header for row & column offsets
But . . . care must be taken to avoid excessive blocking and deadlock

## Slide 45: Dealing with Conflicts
Fig. 10.11 Various ways of dealing with conflicts in wormhole routing.

## Slide 46: Deadlock in Wormhole Switching
Deadlock avoidance requires a more complicated routing algorithm and/or more conservative routing decisions
. . . nontrivial performance penalties
Two strategies for dealing with deadlocks:
1. Avoidance
2. Detection and recovery

## Slide 47: Deadlock Avoidance via Dependence Analysis
Fig. 10.12 Use of dependence graph to check for the possibility of deadlock
Less restrictive models are also possible; e.g., the turn model allows three of four possible turns for each worm
A sufficient condition for lack of deadlocks is to have a link dependence graph that is cycle-free

## Slide 48: Deadlock Avoidance via Virtual Channels
Fig. 10.13 Use of virtual channels for avoiding deadlocks.
Allow only three of the four possible turns
Deadlock Avoidance via Routing Restrictions
NE
WN
ES
SW
Virtual channel 0 active
Virtual channel 1 active

## Slide 49: 11 Numerical 2D Mesh Algorithms
Become more familiar with mesh / torus architectures by:
  Developing a number of useful numerical algorithms
  Studying seminumerical applications (graphs, images)
Topics in This Chapter
11.1 Matrix Multiplication
11.2 Triangular System of Linear Equations
11.3 Tridiagonal System of Linear Equations
11.4 Arbitrary System of Linear Equations
11.5 Graph Algorithms
11.6 Image-Processing Algorithms

## Slide 50: 11.1 Matrix Multiplication
Fig. 11.1 Matrix–vector multiplication on a linear array.
y = Ax or
yi = ∑j=0 to m–1 aij xj
With p = m processors, T = 2m – 1 = 2p – 1

## Slide 51: Another View of Matrix-Vector Multiplication
m-processor linear array for multiplying an m-vector by an m  m matrix.

## Slide 52: Mesh Matrix Multiplication
Fig. 11.2 Matrix-matrix multiplication on a 2D mesh.
C = AB or
cij = ∑k=0 to m–1 aik bkj
p = m2, T = 3m – 2

## Slide 53: Matrix-Vector Multiplication on a Ring
y = Ax or
yi = ∑j=0 to m–1 aij xj
Fig. 11.3 Matrix-vector multiplication on a ring.
With p = m processors, T = m = p

## Slide 54: Torus Matrix Multiplication
Fig. 11.4 Matrix–matrix multiplication on a 2D torus.
C = AB or
cij = ∑k=0 to m–1 aik bkj
p = m2, T = m = p1/2
B moves
A moves
For m > p1/2, use block matrix multiplication
Can gain efficiency from overlapping communication with computation

## Slide 55: 11.2 Triangular System of Linear Equations
Lower triangular:
Find x0 from the first equation, substitute in the second equation to find x1, etc.
Solution: Use forward (lower) or back (upper) substitution
a00x0 = b0
a10x0 + a11x1 = b1
a20x0 + a21x1 + a22x2 = b2
.
.
.
am-1,0x0 + am-1,1x1 + . . . + am-1,m-1xm-1 = bm-1
Fig. 11.5 Lower/upper triangular square matrix;
if aii = 0 for all i, then it is strictly lower/upper triangular.

## Slide 56: Forward Substitution on a Linear Array
Fig. 11.6 Solving a triangular system of linear equations on a linear array.
a00x0 = b0
a10x0 + a11x1 = b1
.
.
.

## Slide 57: Triangular Matrix Inversion: Algorithm
Fig. 11.7 Inverting a triangular matrix by solving triangular systems of linear equations.

## Slide 58: Triangular Matrix Inversion on a Mesh
Fig. 11.8 Inverting a lower triangular matrix on a 2D mesh.
T = 3m – 2
Can invert two matrices using one more step

## Slide 59: 11.3 Tridiagonal System of Linear Equations
Fig. 11.9 A tridiagonal system of linear equations.
l0 x–1 + d0 x0 + u0 x1 = b0
l1 x0 + d1 x1 + u1 x2 = b1
l2 x1 + d2 x2 + u2 x3 = b2
.
.
.
Special case of
a band matrix
0
0

## Slide 60: Other Types of Diagonal Matrices
A pentadiagonal matrix.
x x x 0 0 0 0 0 0 0 0 0
x x x x 0 0 0 0 0 0 0 0
x x x x x 0 0 0 0 0 0 0
0 x x x x x 0 0 0 0 0 0
0 0 x x x x x 0 0 0 0 0
0 0 0 x x x x x 0 0 0 0
0 0 0 0 x x x x x 0 0 0
0 0 0 0 0 x x x x x 0 0
0 0 0 0 0 0 x x x x x 0
0 0 0 0 0 0 0 x x x x x
0 0 0 0 0 0 0 0 x x x x
0 0 0 0 0 0 0 0 0 x x x
Tridiagonal, pentadiagonal, . . . matrices arise in the solution of differential equations using finite difference methods
Matrices with more than three diagonals can be viewed as tridiagonal blocked matrices

## Slide 61: Odd-Even Reduction
l0 x–1 + d0 x0 + u0 x1 = b0
l1 x0 + d1 x1 + u1 x2 = b1
l2 x1 + d2 x2 + u2 x3 = b2
l3 x2 + d3 x3 + u3 x4 = b3
.
.
.
Use odd equations to find odd-indexed variables in terms of even-indexed ones
d1 x1 = b1 – l1 x0 – u1 x2
d3 x3 = b3 – l3 x2 – u3 x4
.
.
.
Substitute in even equations to get a tridiagonal system of half the size
L0 x–2 + D0 x0 + U0 x2 = B0
L2 x0 + D2 x2 + U2 x4 = B2
L4 x2 + D4 x4 + U4 x6 = B4
.
.
.
Li = – li li–1/di–1
Di = di – li ui–1/di–1 – ui li+1/di+1
Ui = – ui ui+1/di+1
Bi = bi – li bi–1/di–1 – ui bi+1/di+1
The six divides are replaceable with one reciprocation per equation, to find 1/dj for odd j, and six multiplies
Sequential solution:
T(m) = T(m/2) + cm = 2cm

## Slide 62: Architecture for Odd-Even Reduction
Fig. 11.10 The structure of odd-even reduction for solving a tridiagonal system of equations.
Because we ignored communication, our analysis is valid for PRAM or for an architecture whose topology matches that of Fig. 11.10.
Parallel solution:
T(m) = T(m/2) + c
= c log2 m

## Slide 63: Odd-Even Reduction on a Linear Array
Fig. 11.11 Binary X-tree (with dotted links) and multigrid architectures.
Architecture of Fig. 11.10 can be modified to binary X-tree and then simplified to 2D multigrid
Communication time on linear array:
T(m) = 2(1 + 2 + . . . + m/2)
= 2m – 2

## Slide 64: Odd-Even Reduction on a 2D Mesh
Communication time on 2D mesh:
T(m)  2[2(1 + 2 + . . . + m1/2/2)]
 2m1/2
0
Row 0
Row 1
Row 2
Row 3
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Communication in rows
Communication in columns

## Slide 65: 11.4 Arbitrary System of Linear Equations
2x0 + 4x1 - 7x2 = 3 2x0 + 4x1 - 7x2 = 7
3x0 + 6x1 - 10x2 = 4 3x0 + 6x1 - 10x2 = 8
-x0 + 3x1 - 4x2 = 6 -x0 + 3x1 - 4x2 = -1
2 4 -7 3 7
3 6 -10 4 8
-1 3 -4 6 -1
Extended matrix A =
A
b
for system 1
b
for system 2
Ax = b
1 2 -3.5 1.5 3.5
0 0 0.5 -0.5 -2.5
0 5 -7.5 7.5 2.5
Extended matrix A =
1 0 0 -2 0
0 1 0 0 -7
0 0 1 -1 -5
Extended matrix A =
Divide row 0 by 2; subtract 3 times from row 1 (pivoting oper)
Repeat until identity matrix appears in first n columns;
read solutions from remaining columns
Gaussian elimination

## Slide 66: Performing One Step of Gaussian Elimination
Fig. 11.12 A linear array performing the first phase of Gaussian elimination.

## Slide 67: Gaussian Elimination on a 2D Mesh
Fig. 11.13 Implementation of Gaussian elimination on a 2D array.

## Slide 68: Matrix Inversion on a 2D Mesh
Fig. 11.14 Matrix inversion by Gaussian elimination.

## Slide 69: Jacobi Methods
2x0 + 4x1 - 7x2 = 3
3x0 + 6x1 - 10x2 = 4
-x0 + 3x1 - 4x2 = 6
Ax = b
x0 = -2.000x1 + 3.500x2 + 1.500
x1 = -0.500x0 + 1.667x2 + 0.667
x2 = -0.250x0 + 0.750x1 – 1.500
Use each equation to find one of the variables in terms of all others
Iterate: Plug in estimates for the unknowns on the right-hand side
to find new estimates on the left-hand side
Example: Estimate x0 = 1, x1 = 1, x2 = 1
x0 = -2.000 + 3.500 + 1.500 = 3.000
x1 = -0.500 + 1.667 + 0.667 = 1.834
x2 = -0.250 + 0.750 – 1.500 = -1.000
Solution: x0 = -2
x1 = 0
x2 = -1

## Slide 70: Jacobi Relaxation and Overrelaxation
Jacobi relaxation: Assuming aii ≠ 0, solve the ith equation for xi, yielding m equations from which new (better) approximations to the answers can be obtained.
xi(t+1) = (1 / aii)[bi – ∑ji aij xj(t)] xi(0) = initial approximation for xi
On an m-processor linear array, each iteration takes O(m) steps.
The number of iterations needed is O(log m) if certain conditions are satisfied, leading to O(m log m) average time.
A variant: Jacobi overrelaxation
xi(t+1) = (1 – g) xi(t) + (g / aii)[bi – ∑ji aij xj(t)] 0 < g ≤ 1
For g = 1, the method is the same as Jacobi relaxation
For smaller g, overrelaxation may offer better performance

## Slide 71: 11.5 Graph Algorithms
Fig. 11.15 Matrix representation of directed graphs.

## Slide 72: Transitive Closure of a Graph
A0 = I Paths of length 0 (identity matrix)
A1 = A Paths of length 1
A2 = A  A Paths of length 2
A3 = A2  A Paths of length 3 etc.
Compute “powers” of A via matrix multiplication, but use AND/OR in lieu of multiplication/addition
Transitive closure of G has the adjacency matrix
A* = A0 + A1 + A2 + . . .
A*ij = 1 iff node j is reachable from node i
Powers need to be computed up to An–1 (why?)
Graph G with adjacency matrix A

## Slide 73: Transitive Closure Algorithm
Initialization: Insert the edges (i, i), 0  i  n – 1, into the graph
Phase 0 Insert the edge (i, j) into the graph
if (i, 0) and (0, j) are in the graph
Phase 1 Insert the edge (i, j) into the graph
if (i, 1) and (1, j) are in the graph
.
.
.
Phase k Insert the edge (i, j) into the graph
if (i, k) and (k, j) are in the graph
[Graph A(k) then has an edge (i, j) iff there is
a path from i to j that goes only through
nodes {1, 2, . . . , k} as intermediate hops]
.
.
.
Phase n – 1 Graph A(n–1) is the answer A*
Graph G with adjacency matrix A

## Slide 74: Transitive Closure on a 2D Mesh
The key to the algorithm is to ensure that each phase takes constant time; overall O(n) steps. This would be optimal on an n  n mesh because the best sequential algorithm needs O(n3) time.
Graph G with adjacency matrix A
Fig. 11.16 Transitive closure algorithm on a 2D mesh.

## Slide 75: Elimination of Broadcasting via Retiming
Example of systolic retiming by delaying the inputs to CL and advancing the outputs from CL by d units [Fig. 12.8 in Computer Arithmetic: Algorithms and Hardware Designs, by Parhami, Oxford, 2000]
0
0
0
0
1
1
1
1

## Slide 76: Systolic Retiming for Transitive Closure
Fig. 11.17 Systolic retiming to eliminate broadcasting.
Add 2n – 2 = 6 units of delay to edges crossing cut 1
Move 6 units of delay from inputs to outputs of node (0, 0)

## Slide 77: 11.6 Image Processing Algorithms
The reason for considering diagonally adjacent pixels parts of the same component.
Labeling connected components in a binary image (matrix of pixels)
Worst-case component showing that a naïve “propagation” algorithm may require O(p) time.

## Slide 78: Recursive Component Labeling on a 2D Mesh
Fig. 11.18 Connected components in an 8  8 binary image.
Fig. 11.19 Finding the connected components via divide and conquer.
T(p) = T(p/4) + O(p1/2) = O(p1/2)

## Slide 79: Levialdi’s Algorithm
Figure 11.21 Example of the shrinkage phase of Levialdi’s component labeling algorithm.
Figure 11.20 Transformation or rewriting rules for Levialdi’s algorithm in the shrinkage phase
(no other pixel changes).

## Slide 80: Analysis and Proof of Levialdi’s Algorithm
Component do not merge in shrinkage phase
Consider a 0 that is about to become a 1
If any y is 1, then already connected
If z is 1 then it will change to 0 unless
at least one neighboring y is 1
x 1 y
1 0 y
y y z
Latency of Levialdi’s algorithm
T(n) = 2n1/2 – 1 {shrinkage} + 2n1/2 – 1 {expansion}
Figure 11.20 Transformation or rewriting rules for Levialdi’s algorithm in the shrinkage phase
(no other pixel changes).

## Slide 81: 12 Mesh-Related Architectures
Study variants of simple mesh and torus architectures:
  Variants motivated by performance or cost factors
  Related architectures: pyramids and meshes of trees
Topics in This Chapter
12.1 Three or More Dimensions
12.2 Stronger and Weaker Connectivities
12.3 Meshes Augmented with Nonlocal Links
12.4 Meshes with Dynamic Links
12.5 Pyramid and Multigrid Systems
12.6 Meshes of Trees

## Slide 82: 12.1 Three or More Dimensions
3D vs 2D mesh: D = 3p1/3 – 3 vs 2p1/2 – 2; B = p2/3 vs p1/2
Example: 3D 8  8  8 mesh p = 512, D = 21, B = 64
2D 22  23 mesh p = 506, D = 43, B = 23
Fig. 12.1 3D and 2.5D physical realizations of a 3D mesh.

## Slide 83: More than Three Dimensions?
qD mesh with m processors along each dimension: p = mq
Node degree d = 2q
Diameter D = q(m – 1) = q (p1/q – 1)
Bisection width: B = p1–1/q when m = p1/q is even
qD torus with m processors along each dimension = m-ary q-cube
4D, 5D, . . . meshes/tori: optical links?
2.5D and 3D packaging technologies

## Slide 84: Node Indexing in q-D Meshes
zyx order
000 0
001 1
002 2
003 3
010 4
011 5
012 6
013 7
020 8
…
100 16
101 17
…
200 32
201 33
X
Y
Z
0
1
2
3
4
5
6
16
17
8
10
13

## Slide 85: Sorting on a 3D Mesh
Sorting on 3D mesh (zyx order; reverse of node index)
Phase 1: Sort elements on each zx plane into zx order
Phase 2: Sort elements on each yz plane into zy order
Phase 3: Sort elements on each xy layer into yx order
(odd layers sorted in reverse order)
Phase 4: Apply 2 steps of odd-even transposition along z
Phase 5: Sort elements on each xy layer into yx order
A variant of shearsort is available, but Kunde’s algorithm is faster and simpler
Defining the zyx processor ordering
Time for Kunde’s algorithm
= 4  (2D-sort time) + 2
 16p1/3 steps

## Slide 86: Routing on a 3D Mesh
Greedy zyx (layer-first, row last) routing algorithm
Phase 1: Sort into zyx order by destination addresses
Phase 2: Route along z dimension to correct xy layer
Phase 3: Route along y dimension to correct column
Phase 4: Route along x dimension to destination
Simple greedy algorithm does fine usually, but sorting first reduces buffer requirements
As in 2D case, partial sorting can be used
Time for sort-based routing
= Sort time + Diameter
 19p1/3 steps

## Slide 87: Matrix Multiplication on a 3D Mesh
Assume the use of an m3/4  m3/4  m3/4 mesh with p = m9/4 processors
Each m3/4  m3/4 layer of the mesh is assigned to one of the m3/4  m3/4 matrix multiplications (m3/4 multiply-add steps)
The rest of the process can take time that is of lower order
Optimal: Matches sequential work and diameter-based lower bound
A total of (m1/4)3 = m3/4 block multiplications are needed
Matrix blocking for multiplication on a 3D mesh

## Slide 88: Low- vs High-Dimensional Meshes
A low-dimensional mesh can efficiently emulate a high-dimensional one
Question: Is it more cost effective, e.g., to have 4-port processors in a 2D mesh architecture or 6-port processors in a 3D mesh architecture, given that for the 4-port processors, fewer ports and ease of layout allow us to make each channel wider?
There is a good match between the structure of a 3D mesh and communication requirements of physical modeling problems
6  6 mesh emulating
3  3  3 mesh
(not optimal)
Lower
layer
Middle
layer
Upper
layer

## Slide 89: 12.2 Stronger and Weaker Connectivities
Fig. 12.2 Eight-neighbor and hexagonal (hex) meshes.
Fortified meshes and other models with stronger connectivities:
Eight-neighbor
Six-neighbor
Triangular
Hexagonal
As in higher-dimensional meshes, greater connectivity does not automatically translate into greater performance
Area and signal-propagation delay penalties must be factored in

## Slide 90: Simplification via Link Orientation
Figure 12.3 A 4  4 Manhattan street network.
Two in- and out-channels per node, instead of four
With even side lengths, the diameter does not change
Some shortest paths become longer, however
Can be more cost-effective than 2D mesh

## Slide 91: Simplification via Link Removal
Figure 12.4 A pruned 4  4  4 torus with nodes of degree four [Kwai97].
Pruning a high-dimensional mesh or torus can yield an architecture with the same diameter but much lower implementation cost
Honeycomb torus

## Slide 92: Simplification via Link Sharing
Fig. 12.5 Eight-neighbor mesh with shared links and example data paths.
Factor-of-2 reduction in ports and links, with no performance degradation for uniaxis communication (weak SIMD model)

## Slide 93: 12.3 Meshes Augmented with Nonlocal Links
Motivation: Reduce the wide diameter (which is a weakness of meshes)
Fig. 12.6 Three examples of bypass links along the rows of a 2D mesh.
Increases max node degree and hurts the wiring locality and regularity
Road analogy for bypass connections

## Slide 94: Using a Single Global Bus
Fig. 12.7 Mesh with a global bus and semigroup computation on it.
Semigroup computation on 2D mesh with a global bus
Phase 1: Find partial results in p1/3  p1/3 submeshes in O(p1/3) steps;
results stored in the upper left corner of each submesh
Phase 2: Combine partial results in O(p1/3) steps, using a sequential
algorithm in one node and the global bus for data transfers
Phase 3: Broadcast the result to all nodes (one step)
The single bus increases the bisection width by 1, so it does not help much with sorting or other tasks that need extensive data movement

## Slide 95: Mesh with Row and Column Buses
Fig. 12.8 Mesh with row/column buses and semigroup computation on it.
Semigroup computation on 2D mesh with row and column buses
Phase 1: Find partial results in p1/6  p1/6 submeshes in O(p1/6) steps
Phase 2: Distribute p1/3 row values left among the p1/6 rows in same slice
Phase 3: Combine row values in p1/6 steps using the row buses
Phase 4: Distribute column-0 values to p1/3 columns using the row buses
Phase 5: Combine column values in p1/6 steps using the column buses
Phase 6: Distribute p1/3 values on row 0 among p1/6 rows of row slice 0
Phase 7: Combine row values in p1/6 steps
Phase 8: Broadcast the result to all nodes (2 steps)
The bisection width doubles, so row and column buses do not fundamentally change the performance of sorting or other tasks that need extensive data movement

## Slide 96: 12.4 Meshes with Dynamic Links
Fig. 12.9 Linear array with a separable bus using reconfiguration switches.
Semigroup computation in O(log p) steps; both 1D and 2D meshes
Fig. 12.10 Some processor states in a reconfigurable mesh.
Various subsets of processors (not just rows and columns) can be configured, to communicate over shared buses

## Slide 97: Programmable Connectivity in FPGAs
Interconnection switch with 8 ports and four connection choices for each port:
0 – No connection
1 – Straight through
2 – Right turn
3 – Left turn
8 control bits (why?)
1
2
1
2
3
3
4
4
5
5
8
8
7
6
6
7

## Slide 98: An Array Reconfiguration Scheme
3-state 2  2 switch

## Slide 99: Reconfiguration of Faulty Arrays
Question: How do we know which cells/nodes must be bypassed?
Must devise a scheme in which healthy nodes set the switches

## Slide 100: 12.5 Pyramid and Multigrid Systems
Originally developed for image processing applications
Roughly 3/4 of the processors belong to the base
For an l-level pyramid: D = 2l – 2 d = 9 B = 2l
Fig. 12.11 Pyramid with 3 levels and 4  4 base along with its 2D layout.
Faster than mesh
for semigroup computation,
but not for
sorting or
arbitrary
routing

## Slide 101: Pyramid and 2D Multigrid Architectures
Fig. 12.12 The relationship between pyramid and 2D multigrid architectures.
Multigrid architecture is less costly and can emulate the pyramid architecture quite efficiently
Pyramid is to 2D multigrid what X-tree is to 1D multigrid

## Slide 102: 12.6 Meshes of Trees
Fig. 12.13 Mesh of trees architecture with 3 levels and a 4  4 base.
2m trees, each with m leaves, sharing leaves in the base
Row and column roots can be combined into m degree-4 nodes

## Slide 103: Alternate Views of a Mesh of Trees
Fig. 12.14 Alternate views of the mesh of trees architecture with a 4  4 base.

## Slide 104: Simple Algorithms for Mesh of Trees
Semigroup computation: row/column combining
Parallel prefix computation: similar
Routing m2 packets, one per processor on the
m  m base: requires W(m) = W(p1/2) steps
In the view of Fig. 12.14, with only m packets
to be routed from one side of the network to
the other, 2 log2 m steps are required,
provided destination nodes are distinct
Sorting m2 keys, one per processor on the
m  m base: emulate any mesh sorting algorithm
Sorting m keys stored in merged roots:
broadcast xi to row i and column i, compare xi to xj in leaf (i, j) to set a flag, add flags in column trees to find the rank of xi , route xi to node rank[xi]

## Slide 105: Some Numerical Algorithms for Mesh of Trees
Matrix-vector multiplication Ax = y (A stored on the base and vector x in the column roots, say; result vector y is obtained in the row roots): broadcast xj in the jth column tree, compute aijxj
in base processor (i, j), sum over row trees
Fig. 12.15 Mesh of trees variant with row, column, and diagonal trees.
Convolution of two vectors: similar

## Slide 106: Minimal-Weight Spanning Tree Algorithm
Greedy algorithm: in each of at most log2 n phases, add the minimal-weight edge that connects a component to a neighbor
Sequential algorithms, for an n-node, e-edge graph:
Kruskal’s: O(e log e)
Prim’s (binary heap):
O((e + n) log n)
Both of these algorithms are O(n2 log n) for dense graphs, with e = O(n2)
Prim’s (Fibonacci heap):
O(e + n log n), or
O(n2) for dense graphs
Fig. 12.16 Example for min-weight spanning tree algorithm.

## Slide 107: MWST Algorithm on a Mesh of Trees
The key to parallel version of the algorithm is showing that each phase can be done in O(log2n) steps; O(log3n) overall
Leaf (i, j) holds the weight W(i, j) of edge (i, j) and “knows” whether the edge is in the spanning tree, and if so, in which supernode. In each phase, we must:
a. Find the min-weight edge incident
to each supernode
b. Merge supernodes for next phase
Fig. 12.17 Finding the new supernode ID when several supernodes merge.
Subphase a takes O(log n) steps
Subphase b takes O(log2 n) steps