## Slide 1: Part IV Low-Diameter Architectures

## Slide 2
About This Presentation
This presentation is intended to support the use of the textbook Introduction to Parallel Processing: Algorithms and Architectures (Plenum Press, 1999, ISBN 0-306-45970-1). It was prepared by the author in connection with teaching the graduate-level course
ECE 254B: Advanced Computer Architecture: Parallel Processing, at the University of California, Santa Barbara. Instructors can use these slides in classroom teaching and for other educational purposes. Any other use is strictly prohibited. © Behrooz Parhami
Edition | Released | Revised | Revised | Revised
First | Spring 2005 | Spring 2006 | Fall 2008 | Fall 2010
 |  | Winter 2013 | Winter 2014 | Winter 2016
 |  | Winter 2019 | Winter 2020 | Winter 2021

## Slide 3: IV Low-Diameter Architectures
Study the hypercube and related interconnection schemes:
  Prime example of low-diameter (logarithmic) networks
  Theoretical properties, realizability, and scalability
  Complete our view of the “sea of interconnection nets”
Topics in This Part
Chapter 13 Hypercubes and Their Algorithms
Chapter 14 Sorting and Routing on Hypercubes
Chapter 15 Other Hypercubic Architectures
Chapter 16 A Sampler of Other Networks

## Slide 4: 13 Hypercubes and Their Algorithms
Study the hypercube and its topological/algorithmic properties:
  Develop simple hypercube algorithms (more in Ch. 14)
  Learn about embeddings and their usefulness
Topics in This Chapter
13.1 Definition and Main Properties
13.2 Embeddings and Their Usefulness
13.3 Embedding of Arrays and Trees
13.4 A Few Simple Algorithms
13.5 Matrix Multiplication
13.6 Inverting a Lower-Triangular Matrix

## Slide 5: 13.1 Definition and Main Properties
Begin studying networks that are intermediate between diameter-1 complete network and diameter-p1/2 mesh

## Slide 6: Very-High-Dimensional Meshes and Tori
qD mesh with m processors along each dimension: p = mq
Diameter D = q(m – 1) = q (p1/q – 1)
Bisection width: B = p1–1/q when m = p1/q is even
Node degree d = 2q
qD torus with m processors along each dimension = m-ary q-cube
What happens when q becomes as large as log2 p?
Diameter D = q (p1/q – 1) = log2 p * = O(log p)
Bisection width: B = p1–1/q = p / p1/q = p/2 * = O(p)
Node degree d = 2q = log2 p ** = O(log p)
qD torus with 2 processors along each dimension same as mesh
* What is the value of m = p1/q = p1/log2 p ?
m = p1/log2 p mlog2 p = p m = 2
** When m = 2, node degree becomes q instead of 2q

## Slide 7: Hypercube and Its History
Binary tree has logarithmic diameter, but small bisection
Hypercube has a much larger bisection
Hypercube is a mesh with the maximum possible number of dimensions
2  2  2  . . .  2
 q = log2 p 
We saw that increasing the number of dimensions made it harder to design and visualize algorithms for the mesh
Oddly, at the extreme of log2 p dimensions, things become simple again!
Brief history of the hypercube (binary q-cube) architecture
Concept developed: early 1960s [Squi63]
Direct (single-stage) and indirect (multistage) versions: mid 1970s
Initial proposals [Peas77], [Sull77] included no hardware
Caltech’s 64-node Cosmic Cube: early 1980s [Seit85]
Introduced an elegant solution to routing (wormhole switching)
Several commercial machines: mid to late 1980s
Intel PSC (personal supercomputer), CM-2, nCUBE (Section 22.3)

## Slide 8: Basic Definitions
Hypercube is generic term; 3-cube, 4-cube, . . . , q-cube in specific cases
Fig. 13.1 The recursive structure of binary hypercubes.
Parameters:
p = 2q
B = p/2 = 2q–1
D = q = log2p
d = q = log2p

## Slide 9: The 64-Node Hypercube
Only sample wraparound links are shown to avoid clutter
Isomorphic to the 4  4  4 3D torus (each has 64  6/2 links)

## Slide 10: Neighbors of a Node in a Hypercube
xq–1xq–2 . . . x2x1x0 ID of node x
xq–1xq–2 . . . x2x1x0 dimension-0 neighbor; N0(x)
xq–1xq–2 . . . x2x1x0 dimension-1 neighbor; N1(x)
. .
. .
. .
xq–1xq–2 . . . x2x1x0 dimension-(q – 1) neighbor; Nq–1(x)
The q neighbors of node x
Nodes whose labels differ in k bits (at Hamming distance k) connected by shortest path of length k
Both node- and edge-symmetric
Strengths: symmetry, log diameter, and linear bisection width
Weakness: poor scalability

## Slide 11: 13.2 Embeddings and Their Usefulness
Dilation: Longest path onto which an edge is mapped (routing slowdown)
Congestion: Max number of edges mapped onto one edge (contention slowdown)
Load factor: Max number of nodes mapped onto one node (processing slowdown)
Fig. 13.2 Embedding a seven-node binary tree into 2D meshes of various sizes.
Dilation = 1
Congestion = 1
Load factor = 1
Dilation = 2
Congestion = 2
Load factor = 1
Dilation = 1
Congestion = 2
Load factor = 2
Expansion:
ratio of the number of nodes (9/7, 8/7, and 4/7 here)

## Slide 12: 13.3 Embedding of Arrays and Trees
Hamiltonicity is an important property of a graph
A graph with n nodes is Hamiltonian if the n-node cycle is its subgraph
More generally, embedding of cycles of various lengths in an intact or faulty network of nodes may be sought
Bridges of Konigsberg: Find a path that crosses each bridge once
Hamiltonian
Non-Hamiltonian
Hamiltonian?

## Slide 13: Hamiltonicity of the Hypercube
Alternate inductive proof: Hamiltonicity of the q-cube is equivalent to the existence of a q-bit Gray code
Fig. 13.3 Hamiltonian cycle in the q-cube.
(q – 1)-bit Gray code
000 . . . 000
000 . . . 001
000 . . . 011
.
.
.
100 . . . 000
0
0
0
0
1
1
1
1
100 . . . 000
.
.
.
000 . . . 011
000 . . . 010
000 . . . 000
(q – 1)-bit Gray code
in reverse
Basis: q-bit Gray code beginning with the all-0s codeword and ending with 10q–1 exists for q = 2: 00, 01, 11, 10

## Slide 14: Mesh/Torus Embedding in a Hypercube
Is a mesh or torus a subgraph of the hypercube of the same size?
Fig. 13.5 The 4  4 mesh/torus is a subgraph of the 4-cube.
We prove this to be the case for a torus (and thus for a mesh)

## Slide 15: Torus is a Subgraph of Same-Size Hypercube
A tool used in our proof
Product graph G1  G2:
Has n1  n2 nodes
Each node is labeled by a pair of labels, one from each component graph
Two nodes are connected if either component of the two nodes were connected in the component graphs
Fig. 13.4 Examples of product graphs.
The 2a  2b  2c . . . torus is the product of 2a-, 2b-, 2c-, . . . node rings
The (a + b + c + ... )-cube is the product of a-cube, b-cube, c-cube, . . .
The 2q-node ring is a subgraph of the q-cube
If a set of component graphs are subgraphs of another set, the product graphs will have the same relationship

## Slide 16: Embedding Trees in the Hypercube
The (2q – 1)-node complete binary tree is not a subgraph of the q-cube
Proof by contradiction based on the parity of node label weights (number of 1s is the labels)
The 2q-node double-rooted complete binary tree is a subgraph of the q-cube
Fig. 13.6
The 2q-node double-rooted complete binary tree is a subgraph of the q-cube.

## Slide 17: A Useful Tree Embedding in the Hypercube
The (2q – 1)-node complete binary tree can be embedded into the (q – 1)-cube
Fig. 13.7 Embedding a 15-node complete binary tree into the 3-cube.
Despite the load factor of q, many tree algorithms entail no slowdown

## Slide 18: 13.4 A Few Simple Algorithms
Fig. 13.8 Semigroup computation on a 3-cube.
Semigroup computation on the q-cube
Processor x, 0  x < p do t[x] := v[x]
{initialize “total” to own value}
for k = 0 to q – 1 processor x, 0  x < p, do
get y :=t[Nk(x)]
set t[x] := t[x]  y
endfor
Commutativity
of the operator  is implicit here.
How can we remove this assumption?
Dim 0
Dim 1
Dim 2

## Slide 19: Parallel Prefix Computation
Fig. 13.8 Semigroup computation on a 3-cube.
Commutativity
of the operator  is implicit in this algorithm as well.
How can we remove this assumption?
t : subcube “total”
u : subcube prefix
Parallel prefix computation on the q-cube
Processor x, 0  x < p, do t[x] := u[x] := v[x]
{initialize subcube “total” and partial prefix}
for k = 0 to q – 1 processor x, 0  x < p, do
get y :=t[Nk(x)]
set t[x] := t[x]  y
if x > Nk(x) then set u[x] := y  u[x]
endfor
Dim 0
Dim 1
Dim 2

## Slide 20: Sequence Reversal on the Hypercube
Fig. 13.11 Sequence reversal on a 3-cube.
Reversing a sequence on the q-cube
for k = 0 to q – 1 Processor x, 0  x < p, do
get y := v[Nk(x)]
set v[x] := y
endfor
Dim 0
Dim 1
Dim 2

## Slide 21: Ascend, Descend, and Normal Algorithms
Graphical depiction of ascend, descend, and normal algorithms.
Parallel prefix
Sequence reversal
Semigroup
Dimension-order communication

## Slide 22: 13.5 Matrix Multiplication
Fig. 13.12 Multiplying two 2  2 matrices on a 3-cube.
1. Place elements
of A and B in registers RA & RB of m2 processors with the IDs 0jk
p = m3 = 2q processors, indexed as ijk (with three q/3-bit segments)
2. Replicate inputs: communicate across 1/3 of the dimensions
3, 4. Rearrange the data by communicating across the remaining 2/3 of dimensions so that processor ijk has Aji and Bik
6. Move Cjk to processor 0jk
Dim 0
Dim 1
Dim 2

## Slide 23: Analysis of Matrix Multiplication
The algorithm involves communication steps in three loops, each with
q / 3 iterations (in one of the 4 loops, 2 values are exchanged per iteration)
Tmul (m, m3) =
O(q) = O(log m)
Analysis in the case of block matrix multiplication (m  m matrices):
Matrices are partitioned into p1/3  p1/3 blocks of size (m / p1/3)  (m / p1/3)
Each communication step deals with m2 / p2/3 block elements
Each multiplication entails 2m3/p arithmetic operations
Tmul(m, p) = m2 / p2/3  O(log p) + 2m3 / p
Communication Computation
Dim 0
Dim 1
Dim 2

## Slide 24: 13.6 Inverting a Lower-Triangular Matrix
Tinv(m) = Tinv(m/2) + 2Tmul(m/2) = Tinv(m/2) + O(log m) = O(log2m)
B 0 B–1 0
For A = we have A–1 =
C D –D–1CB–1 D–1
Because B and D are both lower triangular, the same algorithm can be used recursively to invert them in parallel
B 0 B–1 0 BB–1 0
 =
C D –D–1CB–1 D–1 CB–1 – DD–1CB–1 DD–1
I
I
0

## Slide 25: Recursive Lower-Triangular Matrix Inversion Algorithm
B 0 B–1 0
For A = we have A–1 =
C D –D–1CB–1 D–1
0
C
B
D
Invert lower-triangular matrices B and D
Send B–1 and D–1 to the subcube holding C
–1
–1
–D–1CB–1
0
Inv
Inv
0
Inv
Inv
Compute –D–1C B–1 to in the subcube
Inv
0
Inv
Inv
0
Inv
Inv
0
Inv
Inv
0
Inv
q-cube and its four
(q – 2)-subcubes

## Slide 26: 14 Sorting and Routing on Hypercubes
Study routing and data movement problems on hypercubes:
  Learn about limitations of oblivious routing algorithms
  Show that bitonic sorting is a good match to hypercube
Topics in This Chapter
14.1 Defining the Sorting Problem
14.2 Bitonic Sorting on a Hypercube
14.3 Routing Problems on a Hypercube
14.4 Dimension-Order Routing
14.5 Broadcasting on a Hypercube
14.6 Adaptive and Fault-Tolerant Routing

## Slide 27: 14.1 Defining the Sorting Problem
Review of the hypercube:
Fully symmetric with respect to dimensions
Typical computations involve communication across all dimensions
Dim 2
Dim 1
Dim 0
Dimension-order communication
is known as “ascend” or “descend”
(0 up to q – 1, or q – 1 down to 0)
Due to symmetry, any hypercube dimension
can be labeled as 0, any other as 1, and so on

## Slide 28: Hypercube Sorting: Goals and Definitions
Arrange data in order of processor ID numbers (labels)
1-1 sorting (p items to sort, p processors)
k-k sorting (n = kp items to sort, p processors)
The ideal parallel sorting algorithm:
T(p) = Q((n log n)/p)
This ideal has not been achieved in all cases for the hypercube
Smallest
value
Largest
value
Batcher’s odd-even merge or bitonic sort: O(log2p) time
O(log p)-time deterministic algorithm not known
Optimal algorithms known for n >> p or when average running time is considered (randomized)

## Slide 29: Hypercube Sorting: Attempts and Progress
No bull’s eye yet!
There are three categories of practical sorting algorithms:
1. Deterministic 1-1,
O(log2p)-time
2. Deterministic k-k,
optimal for n >> p
(that is, for large k)
3. Probabilistic
(1-1 or k-k)
Pursuit of O(log p)-time algorithm is of theoretical interest only

## Slide 30: Bitonic Sequences
Bitonic sequence:
1 3 3 4 6 6 6 2 2 1 0 0 Rises, then falls
8 7 7 6 6 6 5 4 6 8 8 9 Falls, then rises
8 9 8 7 7 6 6 6 5 4 6 8 The previous sequence, right-rotated by 2
Fig. 14.1 Examples of bitonic sequences.
In Chapter 7, we designed bitonic sorting nets
Bitonic sorting is ideally suited to hypercube

## Slide 31: Sorting a Bitonic Sequence on a Linear Array
Fig. 14.2 Sorting a bitonic sequence on a linear array.
Time needed to sort a bitonic sequence on a p-processor linear array:
B(p) = p + p/2
+ p/4 + . . . + 2 = 2p – 2
Not competitive, because we can sort an arbitrary sequence in 2p – 2 unidirectional communication steps using odd-even transposition

## Slide 32: Bitonic Sorting on a Linear Array
5 9 10 15 3 7 14 12 8 1 4 13 16 11 6 2
----> <---- ----> <---- ----> <---- ----> <----
5 9 15 10 3 7 14 12 1 8 13 4 11 16 6 2
------------> <------------ ------------> <------------
5 9 10 15 14 12 7 3 1 4 8 13 16 11 6 2
----------------------------> <----------------------------
3 5 7 9 10 12 14 15 16 13 11 8 6 4 2 1
------------------------------------------------------------>
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16
Fig. 14.3 Sorting an arbitrary sequence on a linear array through recursive application of bitonic sorting.
Recall that
B(p) = 2p – 2
Sorting an arbitrary sequence of length p:
T(p) = T(p/2) + B(p) = T(p/2) + 2p – 2 = 4p – 4 – 2 log2p
Alternate derivation:
T(p) = B(2) + B(4) + . . . + B(p) = 2 + 6 + . . . + (2p – 2) = 4p – 4 – 2 log2p

## Slide 33: Visualizing Bitonic Sorting on a Linear Array
Phase 1: Sort half-arrays
in opposite directions
Phase 2: Shift data leftward to compare half-arrays
Phase 3: Send larger item in each pair to the right
Phase 4: Sort each bitonic half-sequence separately
Initial data sequence, stored one per processor

## Slide 34
For linear array, the 4p-step bitonic sorting algorithm is inferior to odd-even transposition which requires p compare-exchange steps (or 2p unidirectional communications)
The situation is quite different for a hypercube
14.2 Bitonic Sorting on a Hypercube
Sorting a bitonic sequence on a hypercube: Compare-exchange values in the upper subcube (nodes with xq–1 = 1) with those in the lower subcube (xq–1 = 0); sort the resulting bitonic half-sequences
B(q) = B(q – 1) + 1 = q
Sorting a bitonic sequence of size n on q-cube, q = log2n
for l = q – 1 downto 0 processor x, 0  x < p, do
if xl = 0
then get y := v[Nl(x)]; keep min(v(x), y); send max(v(x), y) to Nl(x)
endif
endfor
Complexity: 2q communication steps
This is a “descend” algorithm

## Slide 35: Bitonic Sorting on a Hypercube
T(q) = T(q – 1) + B(q)
= T(q – 1) + q
= q(q + 1)/2
= O(log2 p)
Fig. 14.4 Sorting a bitonic sequence of size 8 on the 3-cube.
Dim 0
Dim 1
Dim 2

## Slide 36: 14.3 Routing Problems on a Hypercube
Recall the following categories of routing algorithms:
Off-line: Routes precomputed, stored in tables
On-line: Routing decisions made on the fly
Oblivious: Path depends only on source & destination
Adaptive: Path may vary by link and node conditions
Good news for routing on a hypercube:
Any 1-1 routing problem with p or fewer packets can be solved in O(log p) steps, using an off-line algorithm; this is a consequence of there being many paths to choose from
Bad news for routing on a hypercube:
Oblivious routing requires W(p1/2/log p) time in the worst case
(only slightly better than mesh)
In practice, actual routing performance is usually much closer to the log-time best case than to the worst case.

## Slide 37: Limitations of Oblivious Routing
Theorem 14.1: Let G = (V, E) be a p-node, degree-d network. Any oblivious routing algorithm for routing p packets in G needs W(p1/2/d) worst-case time
Proof Sketch: Let Pu,v be the unique path
used for routing messages from u to v
There are p(p – 1) possible paths for
routing among all node pairs
These paths are predetermined and do not
depend on traffic within the network
Our strategy: find k node pairs ui, vi (1  i  k)
such that ui  uj and vi  vj for i  j, and
Pui,vi all pass through the same edge e
Because  2 packets can go through a link in one step, W(k) steps
will be needed for some 1-1 routing problem
The main part of the proof consists of showing that k can be
as large as p1/2/d

## Slide 38: 14.4 Dimension-Order Routing
Source 01011011
Destination 11010110
Differences ^ ^^ ^
Path: 01011011
11011011
11010011
11010111
11010110
Fig. 14.5 Unfolded 3-cube or the 32-node butterfly network.
Unfolded hypercube (indirect cube, butterfly) facilitates the discussion, visualization, and analysis of routing algorithms
Dimension-order routing between nodes i and j in q-cube can be viewed as routing from node i in column 0 (q) to node j in column q (0) of the butterfly

## Slide 39: Self-Routing on a Butterfly Network
From node 3 to 6: routing tag = 011  110 = 101 “cross-straight-cross”
From node 3 to 5: routing tag = 011  101 = 110 “straight-cross-cross”
From node 6 to 1: routing tag = 110  001 = 111 “cross-cross-cross”
Fig. 14.6 Example dimension-order routing paths.
Number of cross links taken = length of path in hypercube

## Slide 40: Butterfly Is Not a Permutation Network
Fig. 14.7 Packing is a “good” routing problem for dimension-order routing on the hypercube.
Fig. 14.8 Bit-reversal permutation is a “bad” routing problem for dimension-order routing on the hypercube.

## Slide 41: Why Bit-Reversal Routing Leads to Conflicts?
Consider the (2a + 1)-cube and messages that must go from nodes 0 0 0 . . . 0 x1 x2 . . . xa–1 xa to nodes xa xa–1 . . . x2 x1 0 0 0 . . . 0
a + 1 zeros a + 1 zeros
If we route messages in dimension order, starting from the right end, all of these 2a = Q(p1/2) messages will pass through node 0
Consequences of this result:
1. The Q(p1/2) delay is even worse than W(p1/2/d) of Theorem 14.1
2. Besides delay, large buffers are needed within the nodes
True or false? If we limit nodes to a constant number of message buffers, then the Q(p1/2) bound still holds, except that messages are queued at several levels before reaching node 0
Bad news (false): The delay can be Q(p) for some permutations
Good news: Performance usually much better; i.e., log2 p + o(log p)

## Slide 42: Wormhole Routing on a Hypercube
Good/bad routing problems are good/bad for wormhole routing as well
Dimension-order routing is deadlock-free

## Slide 43: 14.5 Broadcasting on a Hypercube
Flooding: applicable to any network with all-port communication
00000 Source node
00001, 00010, 00100, 01000, 10000 Neighbors of source
00011, 00101, 01001, 10001, 00110, 01010, 10010, 01100, 10100, 11000 Distance-2 nodes
00111, 01011, 10011, 01101, 10101, 11001, 01110, 10110, 11010, 11100 Distance-3 nodes
01111, 10111, 11011, 11101, 11110 Distance-4 nodes
11111 Distance-5 node
Binomial broadcast tree with single-port communication
Fig. 14.9
The binomial broadcast tree for a 5-cube.

## Slide 44: Hypercube Broadcasting Algorithms
Fig. 14.10 Three hypercube broadcasting schemes as performed on a 4-cube.
Dim 0
Dim 1
Dim 2
Dim 3

## Slide 45: 14.6 Adaptive and Fault-Tolerant Routing
There are up to q node-disjoint and edge-disjoint shortest paths between any node pairs in a q-cube
Thus, one can route messages around congested or failed nodes/links
A useful notion for designing adaptive wormhole routing algorithms is that of virtual communication networks
Each of the two subnetworks in Fig. 14.11 is acyclic
Hence, any routing scheme that begins by using links in subnet 0, at some point switches the path to subnet 1, and from then on remains in subnet 1, is deadlock-free
Fig. 14.11 Partitioning a 3-cube into subnetworks for deadlock-free routing.

## Slide 46: Robustness of the Hypercube
The fault diameter of the q-cube is q + 1.
Source
Destination
X
X
X
Three faulty nodes
The node that is furthest from S is not its diametrically opposite node in the fault-free hypercube
S
Rich connectivity provides many alternate paths for message routing
Dim 0
Dim 1
Dim 2
Dim 3

## Slide 47: 15 Other Hypercubic Architectures
Learn how the hypercube can be generalized or extended:
  Develop algorithms for our derived architectures
  Compare these architectures based on various criteria
Topics in This Chapter
15.1 Modified and Generalized Hypercubes
15.2 Butterfly and Permutation Networks
15.3 Plus-or-Minus-2i Network
15.4 The Cube-Connected Cycles Network
15.5 Shuffle and Shuffle-Exchange Networks
15.6 That’s Not All, Folks!

## Slide 48: 15.1 Modified and Generalized Hypercubes
Fig. 15.1 Deriving a twisted 3-cube by redirecting two links in a 4-cycle.
Diameter is one less than the original hypercube

## Slide 49: Folded Hypercubes
Fig. 15.2 Deriving a folded 3-cube by adding four diametral links.
Fig. 15.3 Folded 3-cube viewed as
3-cube with a redundant dimension.
Diameter is half that of the original hypercube

## Slide 50: Generalized Hypercubes
A hypercube is a power or homogeneous product network
q-cube = (oo)q ; q th power of K2
Generalized hypercube = qth power of Kr
(node labels are radix-r numbers)
Node x is connected to y iff x and y differ in one digit
Each node has r – 1 dimension-k links
Example: radix-4 generalized hypercube
Node labels are radix-4 numbers
x0
x1
x2
x3
Dimension-0 links

## Slide 51: Bijective Connection Graphs
Beginning with a c-node seed network, the network size is recursively doubled in each step by linking nodes in the two halves via an arbitrary one-to-one mapping. Number of nodes = c 2q
Hypercube is a special case, as are many hypercube variant networks (twisted, crossed, mobius, . . . , cubes)
Bijective
mapping
Special case of c = 1:
Diameter upper bound is q
Diameter lower bound is an open problem (it is better than q + 1/2)

## Slide 52: 15.2 Butterfly and Permutation Networks
Fig. 7.4 Butterfly and wrapped butterfly networks.

## Slide 53: Structure of Butterfly Networks
The 16-row butterfly network.
Fig. 15.5 Butterfly network with permuted dimensions.

## Slide 54: Fat Trees
Fig. 15.6 Two representations of a fat tree.
Skinny tree?
Fig. 15.7 Butterfly network redrawn as a fat tree.

## Slide 55: Butterfly as Multistage Interconnection Network
Fig. 6.9 Example of a multistage memory access network
Generalization of the butterfly network
High-radix or m-ary butterfly, built of m  m switches
Has mq rows and q + 1 columns (q if wrapped)
Fig. 15.8 Butterfly network used to connect modules that are on the same side

## Slide 56: Beneš Network
Fig. 15.9 Beneš network formed from two back-to-back butterflies.
A 2q-row Beneš network:
Can route any 2q  2q permutation
It is “rearrangeable”

## Slide 57: Routing Paths in a Beneš Network
Fig. 15.10 Another example of a Beneš network.
To which memory modules can we connect proc 4 without rearranging the other paths?
What about
proc 6?

## Slide 58: 15.3 Plus-or-Minus-2i Network
Fig. 15.11 Two representations of the eight-node PM2I network.
The hypercube is a subgraph of the PM2I network

## Slide 59: Unfolded PM2I Network
Fig. 15.12 Augmented data manipulator network.
Data manipulator network was used in Goodyear MPP, an early SIMD parallel machine.
“Augmented” means that switches in a column are independent, as opposed to all being set to same state (simplified control).

## Slide 60: 15.4 The Cube-Connected Cycles Network
The cube-connected cycles network (CCC) is the earliest example of what later became known as
X-connected cycles, with X being an arbitrary network
Transform a p-node, degree-d network into a pd-node, degree-3 network by replacing each of the original network nodes with a d-node cycle
L0
L1
L2
L3
L4
L5
L7
L6
x
Original degree-8 node in a network, with its links labeled L0 through L7
x0
x1
x2
x3
x4
x5
x7
x6
L0
L1
L2
L3
L4
L5
L7
L6
Replacement
8-node cycle, with each of
its 8 nodes accommodating one of the links L0 through L7

## Slide 61: A View of The CCC Network
Fig. 15.14 Alternate derivation of CCC from a hypercube.
Replacing each node of a high-dimensional q-cube by a cycle of length q is how CCC was originally proposed
Example of hierarchical substitution to derive a lower-cost network from a basis network

## Slide 62: Another View of the Cube-Connected Cycles Network
Fig. 15.13 A wrapped butterfly (left) converted into cube-connected cycles.
The cube-connected cycles network (CCC) can be viewed as a simplified wrapped butterfly whose node degree is reduced from 4 to 3.

## Slide 63: Emulation of a 6-Cube by a 64-Node CCC
With proper node mapping, dim-0 and dim-1 neighbors of each node will map onto the same cycle
Suffices to show how to communicate along other dimensions of the 6-cube

## Slide 64: Emulation of Hypercube Algorithms by CCC
Node (x, j) is communicating along dimension j; after the next rotation, it will be linked to its dimension-(j + 1) neighbor.
Fig. 15.15 CCC emulating
a normal hypercube algorithm.
Ascend, descend,
and normal algorithms.

## Slide 65: 15.5 Shuffle and Shuffle-Exchange Networks
Fig. 15.16 Shuffle, exchange, and shuffle–exchange connectivities.

## Slide 66: Shuffle-Exchange Network
Fig. 15.17 Alternate views of an eight-node shuffle–exchange network.
S
SE
S
SE
S
SE
S
SE
S
SE
S
SE
S
SE
S
SE

## Slide 67: Routing in Shuffle-Exchange Networks
In the 2q-node shuffle network, node x = xq–1xq–2 . . . x2x1x0
is connected to xq–2 . . . x2x1x0xq–1 (cyclic left-shift of x)
In the 2q-node shuffle-exchange network, node x is additionally connected to xq–2 . . . x2x1x0x q–1
01011011 Source
11010110 Destination
^ ^^ ^ Positions that differ
01011011 Shuffle to 10110110 Exchange to 10110111
10110111 Shuffle to 01101111
01101111 Shuffle to 11011110
11011110 Shuffle to 10111101
10111101 Shuffle to 01111011 Exchange to 01111010
01111010 Shuffle to 11110100 Exchange to 11110101
11110101 Shuffle to 11101011
11101011 Shuffle to 11010111 Exchange to 11010110

## Slide 68: Diameter of Shuffle-Exchange Networks
For 2q-node shuffle-exchange network: D = q = log2p, d = 4
With shuffle and exchange links provided separately, as in Fig. 15.18, the diameter increases to 2q – 1 and node degree reduces to 3
Fig. 15.18 Eight-node network with separate shuffle and exchange links.
E
S
S
S
S
S
S
S
S
E
E
E

## Slide 69: Multistage Shuffle-Exchange Network
Fig. 15.19 Multistage
shuffle–exchange network
(omega network)
is the same as butterfly network.

## Slide 70: 15.6 That’s Not All, Folks!
D = log2 p + 1
d = (log2 p + 1)/2
B = p/4
When q is a power of 2, the 2qq-node cube-connected cycles network derived from the q-cube, by replacing each node with a q-node cycle,
is a subgraph of the (q + log2q)-cube  CCC is a pruned hypercube
Other pruning strategies are possible, leading to interesting tradeoffs
Fig. 15.20 Example of a pruned hypercube.

## Slide 71: Möbius Cubes
Dimension-i neighbor of x = xq–1xq–2 ... xi+1xi ... x1x0 is:
xq–1xq–2 ... 0xi... x1x0 if xi+1 = 0 (xi complemented, as in q-cube)
xq–1xq–2 ... 1xi... x1x0 if xi+1 = 1 (xi and bits to its right complemented)
For dimension q – 1, since there is no xq, the neighbor can be defined
in two possible ways, leading to 0- and 1-Mobius cubes
A Möbius cube has a diameter of about 1/2 and an average internode distance of about 2/3 of that of a hypercube
Fig. 15.21 Two 8-node Möbius cubes.

## Slide 72: 16 A Sampler of Other Networks
Complete the picture of the “sea of interconnection networks”:
  Examples of composite, hybrid, and multilevel networks
  Notions of network performance and cost-effectiveness
Topics in This Chapter
16.1 Performance Parameters for Networks
16.2 Star and Pancake Networks
16.3 Ring-Based Networks
16.4 Composite or Hybrid Networks
16.5 Hierarchical (Multilevel) Networks
16.6 Multistage Interconnection Networks

## Slide 73: 16.1 Performance Parameters for Networks
A wide variety of direct interconnection networks have been proposed for, or used in, parallel computers
They differ in topological, performance, robustness, and realizability attributes.
Fig. 4.8 (expanded)
The sea of direct interconnection networks.

## Slide 74: Diameter and Average Distance
Diameter D (indicator of worst-case message latency)
Routing diameter D(R); based on routing algorithm R
Average internode distance D (indicator of average-case latency)
Routing average internode distance D(R)
For the 3  3 mesh:
D = (4  18 + 4  15 +12)
/ (9  8) = 2
[or 144 / 81 = 16 / 9]
Finding the average internode distance of a 3  3 mesh.
For the 3  3 torus:
D = (4  1 + 4  2) / 8
= 1.5 [or 12 / 9 = 4 / 3]

## Slide 75: Bisection Width
Fig. 16.2 A network whose bisection width is not as large at it appears.
Node bisection and link bisection
Indicator or random communication capacity
Hard to determine; Intuition can be very misleading

## Slide 76: Determining the Bisection Width
Establish upper bound by taking a number of trial cuts.
Then, try to match the upper bound by a lower bound.
Establishing a lower bound on B:
Embed Kp into p-node network
Let c be the maximum congestion
B  p2/4/c
Improved,
corrected
version of
this diagram
on next slide

## Slide 77: Example for Bounding the Bisection Width
Embed K9 into
3  3 mesh
Observe the max congestion of 7
p2/4 = 20
Must cut at least
3 bundles to
sever 20 paths
Bisection width of a 3  3 mesh is at least 3
Given the upper bound of 4:
3  B  4
7
6
4
5
7
7
5
6
7
5
6
7

## Slide 78: Degree-Diameter Relationship
Age-old question: What is the best way to interconnect p nodes of degree d to minimize the diameter D of the resulting network?
Alternatively: Given a desired diameter D and nodes of degree d, what is the max number of nodes p that can be accommodated?
Moore bounds (digraphs)
p  1 + d + d2 + . . . + dD = (dD+1 – 1)/(d – 1)
D  logd [p(d – 1) + 1] – 1
Only ring and Kp match these bounds
x
d nodes
d 2 nodes
Moore bounds (undirected graphs)
p  1 + d + d(d – 1) + . . . + d(d – 1)D–1
= 1 + d [(d – 1)D – 1]/(d – 2)
D  logd–1[(p – 1)(d – 2)/d + 1]
Only ring with odd size p and a few other
networks match these bounds
x
d nodes
d (d – 1) nodes

## Slide 79: Moore Graphs
A Moore graph matches the bounds on diameter and number of nodes.
For d = 2, we have p  2D + 1
Odd-sized ring satisfies this bound
Fig. 16.1 The 10-node Petersen graph.
For d = 3, we have p  3  2D – 2
D = 1 leads to p  4 (K4 satisfies the bound)
D = 2 leads to p  10 and the first nontrivial example (Petersen graph)

## Slide 80: How Good Are Meshes and Hypercubes?
For d = 4, we have D  log3[(p + 1)/2]
So, 2D mesh and torus networks are far from optimal in diameter, whereas butterfly is asymptotically optimal within a constant factor
For d = log2 p (as for d-cube), we have D = W(d / log d)
So the diameter d of a d-cube is a factor of log d over the best possible
We will see that star graphs match this bound asymptotically
Summary:
For node degree d, Moore’s bounds establish the lowest possible diameter D that we can hope to achieve with p nodes, or the largest number p of nodes that we can hope to accommodate for a given D.
Coming within a constant factor of the bound is usually good enough; the smaller the constant factor, the better.

## Slide 81: Layout Area and Longest Wire
The VLSI layout area required by an interconnection network is intimately related to its bisection width B
The longest wire required in VLSI layout affects network performance
For example, any 2D layout of a p-node hypercube requires wires of length W((p / log p)1/2); wire length of a mesh does not grow with size
When wire length grows with size, the per-node performance is bound to degrade for larger systems, thus implying sublinear speedup
If B wires must cross the bisection in 2D layout of a network and wire separation is 1 unit, the smallest dimension of the VLSI chip will be  B
The chip area will thus be W(B2) units
p-node 2D mesh needs O(p) area
p-node hypercube needs at least W(p2) area

## Slide 82: Measures of Network Cost-Effectiveness
Composite measures, that take both the network performance and its implementation cost into account, are useful in comparisons
Robustness must be taken into account in any practical comparison of interconnection networks (e.g., tree is not as attractive in this regard)
One such measure is the degree-diameter product, dD
Mesh / torus: Q(p1/2)
Binary tree: Q(log p)
Pyramid: Q(log p)
Hypercube: Q(log2 p)
However, this measure is somewhat misleading, as the node degree d is not an accurate measure of cost; e.g., VLSI layout area also depends on wire lengths and wiring pattern and bus based systems have low node degrees and diameters without necessarily being cost-effective
Not quite similar in cost-performance

## Slide 83: 16.2 Star and Pancake Networks
Fig. 16.3 The four-dimensional star graph.
Has p = q ! nodes
Each node labeled with a string x1x2 ... xq which is a permutation of {1, 2, ... , q}
Node x1x2 ... xi ... xq is connected to xi x2 ... x1 ... xq for each i (note that x1 and xi are interchanged)
When the i th symbol is switched with x1 , the corresponding link is called a dimension-i link
d = q – 1; D = 3(q – 1)/2
D, d = O(log p / log log p)

## Slide 84: Routing in the Star Graph
Source node 1 5 4 3 6 2
Dimension-2 link to 5 1 4 3 6 2
Dimension-6 link to 2 1 4 3 6 5
Last symbol now adjusted
Dimension-2 link to 1 2 4 3 6 5
Dimension-5 link to 6 2 4 3 1 5
Last 2 symbols now adjusted
Dimension-2 link to 2 6 4 3 1 5
Dimension-4 link to 3 6 4 2 1 5
Last 3 symbols now adjusted
Dimension-2 link to 6 3 4 2 1 5
Dimension-3 link to 4 3 6 2 1 5
Last 4 symbols now adjusted
Dimension-2 link (Dest’n) 3 4 6 2 1 5
We need a maximum of two routing steps per symbol, except that last two symbols need at most 1 step for adjustment  D  2q – 3
The diameter of star is in fact somewhat less D = 3(q – 1)/2
Clearly, this is not a shortest-path routing algorithm.
Correction to text, p. 328: diameter is not 2q – 3

## Slide 85: Star’s Sublogarithmic Degree and Diameter
d = Q(q) and D = Q(q); but how is q related to the number p of nodes?
p = q !  e–qqq (2pq)1/2 [ using Striling’s approximation to q ! ]
ln p  –q + (q + 1/2) ln q + ln(2p)/2 = Q(q log q) or q = Q(log p / log log p)
Hence, node degree and diameter are sublogarithmic
Star graph is asymptotically optimal to within a constant factor with regard to Moore’s diameter lower bound
Routing on star graphs is simple and reasonably efficient; however, virtually all other algorithms are more complex than the corresponding algorithms on hypercubes
Network diameter 4 5 6 7 8 9
Star nodes 24 -- 120 720 -- 5040
Hypercube nodes 16 32 64 128 256 512

## Slide 86: The Star-Connected Cycles Network
Fig. 16.4 The four-dimensional star-connected cycles network.
Replace degree-(q – 1) nodes with (q – 1)-cycles
This leads to a scalable version of the star graph whose node degree of 3 does not grow with size
The diameter of SCC is about the same as that of a comparably sized CCC network
However, routing and other algorithms for SCC are more complex

## Slide 87: Pancake Networks
Similar to star networks in terms of node degree and diameter
Dimension-i neighbor obtained by “flipping” the first i symbols;
hence, the name “pancake”
1234
2134
3214
4321
Dim 2
Dim 3
Dim 4
Source node 1 5 4 3 6 2
Dimension-2 link to 5 1 4 3 6 2
Dimension-6 link to 2 6 3 4 1 5
Last 2 symbols now adjusted
Dimension-4 link to 4 3 6 2 1 5
Last 4 symbols now adjusted
Dimension-2 link (Dest’n) 3 4 6 2 1 5
We need two flips per symbol in the worst case; D  2q – 3

## Slide 88: Cayley Networks
Group:
A semigroup with an identity element and inverses for all elements.
Example 1: Integers with addition or multiplication operator form a group.
Example 2: Permutations, with the composition operator, form a group.
Node x
x  g1
x  g2
x  g3
Gen g1
Gen g2
Gen g3
Star and pancake networks are instances of Cayley graphs
Cayley graph:
Node labels are from a group G, and a subset S of G defines the connectivity via the group operator 
Node x is connected to node y
iff x  g = y for some g  S
Elements of S are “generators” of G if every element of G can be expressed as a finite product of their powers

## Slide 89: Star as a Cayley Network
Fig. 16.3 The four-dimensional star graph.
Four-dimensional star:
Group G of the permutations of {1, 2, 3, 4}
The generators are the following permutations:
(1 2) (3) (4)
(1 3) (2) (4)
(1 4) (2) (3)
The identity element is:
(1) (2) (3) (4)
(1 4) (2) (3)
(1 3) (2) (4)

## Slide 90: 16.3 Ring-Based Networks
Fig. 16.5 A 64-node ring-of-rings architecture composed of eight 8-node local rings and one second-level ring.
Rings are simple, but have low performance and lack robustness
Hence, a variety of multilevel and augmented ring networks have been proposed

## Slide 91: Chordal Ring Networks
Fig. 16.6 Unidirectional ring, two chordal rings, and node connectivity in general.
Given one chord type s, the optimal length for s is approximately p1/2
Routing algorithm: Greedy routing

## Slide 92: Chordal Rings Compared to Torus Networks
Fig. 16.7 Chordal rings redrawn to show their similarity to torus networks.
The ILLIAC IV interconnection scheme, often described as
8  8 mesh or torus, was really a 64-node chordal ring with skip distance 8.
A class of chordal rings, studied at UCSB (two-part paper in IEEE TPDS, August 2005) have a diameter of D = 2
Perfect difference {0, 1, 3}: All numbers in the range 1-6 mod 7 can be formed as the difference of two numbers in the set.
Perfect Difference Networks

## Slide 93: Periodically Regular Chordal Rings
Fig. 16.8 Periodically regular chordal ring.
Modified greedy routing: first route to the head of a group; then use pure greedy routing

## Slide 94: Some Properties of PRC Rings
Fig. 16.9 VLSI layout for a 64-node periodically regular chordal ring.
Remove some skip links for cost-performance tradeoff; similar in nature to CCC network with longer cycles
Fig. 16.10 A PRC ring redrawn as a butterfly- or ADM-like network.

## Slide 95: 16.4 Composite or Hybrid Networks
Motivation: Combine the connectivity schemes from two (or more) “pure” networks in order to:
 Achieve some advantages from each structure
 Derive network sizes that are otherwise unavailable
 Realize any number of performance / cost benefits
A very large set of combinations have been tried
New combinations are still being discovered

## Slide 96: Composition by Cartesian Product Operation
Fig. 13.4 Examples of product graphs.
Properties of product graph G = G  G:
Nodes labeled (x , x ), x   V , x   V 
p = pp
d = d  + d 
D = D + D
 =  + 
Routing: G -first
(x , x )  (y , x )
 (y , y )
Broadcasting
Semigroup & parallel prefix computations

## Slide 97: Other Properties and Examples of Product Graphs
Fig. 16.11 Mesh of trees compared with mesh-connected trees.
If G and G are Hamiltonian, then the p  p torus is a subgraph of G
For results on connectivity and fault diameter, see [Day00], [AlAy02]
Mesh of trees (Section 12.6)
Product of two trees

## Slide 98: 16.5 Hierarchical (Multilevel) Networks
Can be defined
from the bottom up or from the top down
We have already seen several examples of hierarchical networks: multilevel buses (Fig. 4.9); CCC; PRC rings
Fig. 16.13 Hierarchical or multilevel bus network.
Take first-level ring networks and interconnect them as a hypercube
Take a top-level hypercube and replace its nodes with given networks

## Slide 99: Example: Mesh of Meshes Networks
Fig. 16.12 The mesh of meshes network exhibits greater modularity than a mesh.
The same idea can be used to form ring of rings, hypercube of hypercubes, complete graph of complete graphs, and more generally, X of Xs networks
When network topologies at the two levels are different, we have X of Ys networks
Generalizable to three levels (X of Ys of Zs networks), four levels, or more

## Slide 100: Example: Swapped Networks
Two-level swapped network with 2  2 mesh as its nucleus.
0
1
2
3
Level-1 link
00
10
20
30
01
11
21
31
02
12
22
32
03
13
23
33
Level-2 link
Build a p2-node network using p-node building blocks (nuclei or clusters) by connecting node i in cluster j to node j in cluster i
Cluster #
Node #
Cluster #
Node #
We can square the network size by adding one link per node
Also known in the literature as OTIS (optical transpose interconnect system) network

## Slide 101: Swapped Networks Are Maximally Fault-Tolerant
One case of several cases in the proof, corresponding to source and destination nodes being in different clusters
For any connected, degree-d basis network G, Swap(G) = OTIS(G) has the maximal connectivity of d and can thus tolerate up to d – 1 faults
Source: Chen, Xiao, Parhami,
IEEE TPDS, March 2009

## Slide 102: Example: Biswapped Networks
Build a 2p2-node network using p-node building blocks (nuclei or clusters) by connecting node i in cluster j of part 0 to node j in cluster i of part 1
p-node basis network
p copies
Two parts
0
1

## Slide 103: Data-Center Networks
Data-center communication patterns are different from parallel processors
Current networks are variations of the fat-tree concept
Two competing approaches:
- Specialized hardware and communication protocols (e.g., InfiniBand)
- Commodity Ethernet switches and routers for interconnecting clusters

## Slide 104: 16.6 Multistage Interconnection Networks
Numerous indirect or multistage interconnection networks (MINs) have been proposed for, or used in, parallel computers
They differ in topological, performance, robustness, and realizability attributes
We have already seen the butterfly, hierarchical bus, beneš, and ADM networks
Fig. 4.8 (modified)
The sea of indirect interconnection networks.

## Slide 105: Self-Routing Permutation Networks
Do there exist self-routing permutation networks? (The butterfly network is self-routing, but it is not a permutation network)
Permutation routing through a MIN is the same problem as sorting
Fig. 16.14 Example of sorting on a binary radix sort network.

## Slide 106: Partial List of Important MINs
Augmented data manipulator (ADM): aka unfolded PM2I (Fig. 15.12)
Banyan: Any MIN with a unique path between any input and any output (e.g. butterfly)
Baseline: Butterfly network with nodes labeled differently
Beneš: Back-to-back butterfly networks, sharing one column (Figs. 15.9-10)
Bidelta: A MIN that is a delta network in either direction
Butterfly: aka unfolded hypercube (Figs. 6.9, 15.4-5)
Data manipulator: Same as ADM, but with switches in a column restricted to same state
Delta: Any MIN for which the outputs of each switch have distinct labels (say 0 and 1
for 2  2 switches) and path label, composed of concatenating switch output labels
leading from an input to an output depends only on the output
Flip: Reverse of the omega network (inputs  outputs)
Indirect cube: Same as butterfly or omega
Omega: Multi-stage shuffle-exchange network; isomorphic to butterfly (Fig. 15.19)
Permutation: Any MIN that can realize all permutations
Rearrangeable: Same as permutation network
Reverse baseline: Baseline network, with the roles of inputs and outputs interchanged

## Slide 107: 16.6* Natural and Human-Made Networks
Since multistage networks will move to Part II’ (shared memory), the new version of this subsection will discuss the classes of small-world and scale-free networks
Example of a collaboration network
(e.g., co-authors of papers) showing clusters and inter-cluster connectivity
Image credit:
Univ. Leiden

## Slide 108: Professional Connections Networks
Image credit:
LinkedIn