## Slide 1
Objectives: Acoustic Modeling Language Modeling Feature Extraction Search Pronunciation Modeling
Resources: J.P.: Speech Recognition - Part I T.H.: Speech Recognition - Part II ISIP: ASR Tutorial ISIP: ASR Resources IEEE: SP Magazine
• URL: .../publications/courses/ece_8443/lectures/current/lecture_29.ppt
LECTURE 29: EXAMPLES OF PATTERN RECOGNITION IN SPEECH RECOGNITION
Notes: MS Equation 3.0 was used with settings of: 18, 12, 8, 18, 12.

## Slide 2
Speech technology has quietly become a pervasive influence in our daily lives despite widespread concerns about research progress over the past 20 years.
The ability of a hidden Markov models to explain (and predict) variations in the acoustic signal have been the cornerstone of this progress.
Other statistical modeling techniques (e.g., SVMs, finite state machines, entropy-based language modeling) have had significant impact.
Generative models have given way to discriminative models that attempt to directly optimize objective measures such as word error rate.
Why research human language technology?
“Language is the preeminent trait of the human species.”
“I never met someone who wasn’t interested in language.”
“I decided to work on language because it seemed to be the hardest problem to solve.”
Fundamental challenge: diversity of data that often defies mathematical descriptions or physical constraints.
Solution: Integration of multiple knowledge sources.
In this lecture we will focus on use of pattern recognition in high performance speech recognition systems.
Introduction

## Slide 3
Traditional Output:
  best word sequence
  time alignment of information
Other Outputs:
  word graphs
  N-best sentences
  confidence measures
  metadata such as speaker identity, accent, and prosody
Applications:
  Information localization
  data mining
  emotional state
  stress, fatigue, deception
Speech Recognition Is Information Extraction

## Slide 4
What Makes Acoustic Modeling So Challenging?

## Slide 5
Regions of overlap represent classification error
Reduce overlap by introducing acoustic and linguistic context
Comparison of “aa” in “lOck” and “iy” in “bEAt” for conversational speech
What Makes Acoustic Modeling So Challenging?

## Slide 6
Statistical Approach: Noisy Communication Channel Model

## Slide 7
Given an observation sequence, O, and a word sequence, W, we want minimal uncertainty about the correct answer (i.e., minimize the conditional entropy):
To accomplish this, the probability of the word sequence given the observation must increase.
The mutual information, I(W;O), between W and O:
Two choices: minimize H(W) or maximize I(W;O)
Information Theoretic Basis

## Slide 8
Maximizing the mutual information is equivalent to choosing the parameter set  to maximize:
Maximization implies increasing the numerator term (maximum likelihood estimation – MLE) or decreasing the denominator term (maximum mutual information estimation – MMIE)
The latter is accomplished by reducing the probabilities of incorrect, or competing, hypotheses.
Relationship to Maximum Likelihood Methods

## Slide 9
Core components:
transduction
feature extraction
acoustic modeling (hidden Markov models)
language modeling (statistical N-grams)
search (Viterbi beam)
knowledge sources
Our focus will be on the acoustic modeling components of the system.
Speech Recognition Architectures

## Slide 10
Signal Processing in Speech Recognition

## Slide 11
Feature Extraction in Speech Recognition

## Slide 12
Adding More Knowledge to the Front End

## Slide 13
Noise Compensation Techniques

## Slide 14
Acoustic Modeling: Hidden Markov Models

## Slide 15
Training Recipes Are Complex And Iterative

## Slide 16
Bootstrapping Is Key In Parameter Reestimation

## Slide 17
Controlling Model Complexity

## Slide 18
Data-Driven Parameter Sharing Is Crucial

## Slide 19
Context-Dependent Acoustic Units

## Slide 20
What we haven’t talked about: duration models, adaptation, normalization, confidence measures, posterior-based scoring, hybrid systems, discriminative training, and much, much more…
Applications of these models to language (Hazen), dialog (Phillips, Seneff), machine translation (Vogel, Papineni), and other HLT applications
Machine learning approaches to human language technology are still in their infancy (Bilmes)
A mathematical framework for integration of knowledge and metadata will be critical in the next 10 years.
Information extraction in a multilingual environment -- a time of great opportunity!
Summary

## Slide 21
Language Modeling in Speech Recognition

## Slide 22
Demonstrations
Audio Demonstrations: Why is speech recognition so difficult?
Phonetic Units: Context is very important in speech recognition
State of the Art: Example of high performance speech recognition systems

## Slide 23
Useful textbooks:
X. Huang, A. Acero, and H.W. Hon, Spoken Language Processing - A Guide to Theory, Algorithm, and System Development, Prentice Hall, ISBN: 0-13-022616-5, 2001.
D. Jurafsky and J.H. Martin, SPEECH and LANGUAGE PROCESSING: An Introduction to Natural Language Processing, Computational Linguistics, and Speech Recognition, Prentice-Hall, ISBN: 0-13-095069-6, 2000.
F. Jelinek, Statistical Methods for Speech Recognition, MIT Press, ISBN: 0-262-10066-5, 1998.
L.R. Rabiner and B.W. Juang, Fundamentals of Speech Recognition, Prentice-Hall, ISBN: 0-13-015157-2, 1993.
J. Deller, et. al., Discrete-Time Processing of Speech Signals, MacMillan Publishing Co., ISBN: 0-7803-5386-2, 2000.
R.O. Duda, P.E. Hart, and D.G. Stork, Pattern Classification, Second Edition, Wiley Interscience, ISBN: 0-471-05669-3, 2000 (supporting material available at http://rii.ricoh.com/~stork/DHS.html).
D. MacKay, Information Theory, Inference, and Learning Algorithms, Cambridge University Press, 2003.
Relevant online resources:
“Intelligent Electronic Systems,” http://www.cavs.msstate.edu/hse/ies, Center for Advanced Vehicular Systems, Mississippi State University, Mississippi State, Mississippi, USA, June 2005.
Internet-Accessible Speech Recognition Technology,” http://www.cavs.msstate.edu/hse/ies/projects/speech, June 2005.
“Speech and Signal Processing Demonstrations,” http://www.cavs.msstate.edu/hse/ies/projects/speech/software/demonstrations, June 2005.
“Fundamentals of Speech Recognition,” http://www.isip.msstate.edu/publications/courses/ece_8463, September 2004.
Appendix: Relevant Publications