## Slide 1
Question: Which involves more engineering design: a golf club or an iPod?
Objectives: Definition of Design The Design Process The Project Abstract
Resources:
Wiki: Engineering Design NASA: Design Process EWB: Design Process SU: Design Lecture MIT: Design and Prototyping S.K.: Engineering Design
LECTURE 02: ENGINEERING DESIGN
Audio:
URL:
Notes: MS Equation 3.0 was used with settings of: 18, 12, 8, 18, 12.

## Slide 2
“The scientist seeks to understand what is; the engineer seeks to create what never was”
Theodore von Karman
“The Father of Supersonic Flight”
1881 – 1963
(http://www.nmspacemuseum.org/halloffame/detail.php?id=31)
Motivation

## Slide 3
Senior Design is not about:
creating a unique project concept
inventing a new gadget
doing something that has never been done before
Senior Design is about:
Translating customer needs into quantitative design constraints
Optimizing a design to meet these constraints
Verifying that your design meets these constraints
Fabricating a prototype to demonstrate proof of concept.
Key elements of this class include:
Learning how to communicate your ideas to management and the customer
Appreciating the multidisciplinary aspects of engineering design
Understanding how practical constraints such as cost and sustainability influence the design process at every step.
The Essence of Senior Design

## Slide 4
Schedule
Product Development Trade-offs
Cost
Performance
Risk
Performance: ability to do the primary mission
Cost: development, operation life-cycle cost
Schedule: time to first unit, production rate
Risk: of technical and/or financial failure

## Slide 5
An Iterative Design Process
Problem
Design Constraints
Test Specification
Design
Simulation
Test Verification
Prototyping
Test Verification
Hardware Implementation
Test Verification

## Slide 6
The Design Methodology
Problem: recognize that a problem exists, and develop a concise statement of the problem.
Objectives: study the parameters of the problem, and convert them into engineering language you are familiar with.
Literature Survey: assimilate existing knowledge about the problem, and search for similar data (related experiments, evaluations, etc.)
Analysis: analyze the problem based on the knowledge gained from the literature survey, produce a set of design constraints, and generate test specifications to verify these design constraints.
Synthesis: manipulate the analysis to yield a family of solutions (typically through simulation and prototyping).
Evaluation: choose the best solution and verify it meets the design constraints.
Presentation: communicate the solution to your peers/management.
Note: In Senior Design I, some amount of simulation, modeling or even rapid prototyping will be required to ensure that your project is feasible!

## Slide 7
The Project Abstract
150 to 200 words
Discusses what you will do, how you will do it, and why this is important.
Contains numerical or quantitative goals (e.g., improve efficiency by 25%).
Discusses your unique contributions.
Describes the implications of success.
Example:
The rich harmonic response of a vibrating string makes for a sound that is pleasing to the ear. Guitars have been amplified by resonate chambers in the body until magnetic pickups were introduced in 1928 by George Beauchamp. Magnetic pickups are widely accepted as the industry standard for the electrification of guitars. While this method provides acceptable sound quality, there are drawbacks. Magnetic pickups are highly susceptible to 60 Hz interference. It is common to pick up noise from household electrical wiring occurrence when using standard pickups. In addition, the magnet under a given string is susceptible to vibrations from adjacent strings. An optical guitar pickup system detects the string's displacement rather than its velocity, as practiced by magnetic pickups. A small source infrared LED transmits across the string onto an phototransistor. The string's shadow casts an analog representation of the guitar's note into the detector circuit. Sensitive detector circuits with high dynamic range and high signal to noise ratio will give the needed response for an acceptable output. The lower strings yield a higher response due to the displacement based function. For this reason, each string will have a separate detector circuit, biased for the strings own characteristics. Optical devices eliminate 60Hz hums. Light pollution is combated with a metal guard enclosing the mounted transmitter and receiver pairs. Users will have control over the high and low tone knobs as well as the master volume.
More examples will follow.

## Slide 8
Design Project Example (Interactive)
Problem Statement: choose a problem…
Objectives: study the parameters of the problem, and convert them into engineering language you are familiar with.
Literature Survey: where do we go for information?
Analysis: produce a set of design constraints, and generate test specifications to verify these design constraints.
Synthesis: manipulate the analysis to yield a family of solutions (typically through simulation and prototyping).
Evaluation: choose the best solution and verify it meets the design constraints.
Presentation: communicate the solution to your peers/management.

## Slide 9
Abstracts are due next Friday (on web site)
A revised pdf file containing your technical specification is due next Friday also.
Next lecture: quantitative design constraints.
Summary