## Slide 1
ASSESSING SEARCH TERM STRENGTH IN SPOKEN TERM DETECTION Amir Harati and Joseph Picone
Institute for Signal and Information Processing, Temple University
Experimentation
  Correlation (R) and mean square error (MSE) are used to assess the prediction quality.
  Duration is the most significant feature with around 40% correlation.
Features
Most features can be derived from some basic representations (Table 3).
  A duration model based on N-gram phonetic representation developed and trained using TIMIT dataset.
Machine Learning Algorithms
Using machine learning algorithms to learn the relationship between a phonetic representation of a word and its word error rate (WER).
The score is defined based on average WER predicted for a word.
        Strength Score =1-WER
Algorithms: Linear Regression, Feed-Forward Neural Network, Regression Tree and K-nearest neighbors (KNN) in the phonetic space.
Preprocessing includes whitening using singular value decomposition (SVD).
Neural Network has two layers with 30 neurons and trained by back-propagation algorithm.
Figure 4. The relationship between duration and error rate shows that longer words generally result in better performance.
Results
Table 5- Results for feature based method over NIST 2006.
Table 6- Results for KNN in Phonetic space for BBN dataset.
Introduction
Searching audio, unlike text data, is approximate and is based on likelihoods.
Performance depends on acoustic channel, speech rate, accent, language and confusability.
Unlike text-based searches, the quality of the search term plays a significant role in the overall perception of the usability of the system.
Goal: Develop a tool similar to how password checkers assess the strength of a password.
Figure 1. A screenshot of our demonstration software:
http://www.isip.piconepress.com/projects/ks_prediction/demo
Spoken Term Detection (STD)
STD Goal: “…detect the presence of a term in large audio corpus of heterogeneous speech…”
STD Phases:
        Indexing the audio file.
        Searching through the indexed data.
Error types:
        False alarms.
        Missed detections.
Figure 2. A common approach in STD is to use a speech to text system to index the speech signal (J. G. Fiscus, et al., 2007).
Features | Train |  |  |  |  |  | Eval |  |  |  |  | 
 | Regression |  | NN |  | DT |  | Regression |  | NN |  | DT | 
 | MSE | R | MSE | R | MSE | R | MSE | R | MSE | R | MSR | R
Duration | 0.045 | 0.46 | 0.057 | 0.43 | 0.044 | 0.48 | 0.045 | 0.46 | 0.060 | 0.40 | 0.046 | 0.45
Duration + No. Syllables | 0.045 | 0.46 | 0.055 | 0.45 | 0.041 | 0.53 | 0.045 | 0.46 | 0.060 | 0.38 | 0.046 | 0.46
Duration + No. Consonants | 0.045 | 0.46 | 0.055 | 0.46 | 0.040 | 0.54 | 0.046 | 0.46 | 0.058 | 0.41 | 0.051 | 0.39
Duration + No. Syllables + No. Consonants | 0.045 | 0.46 | 0.056 | 0.43 | 0.036 | 0.60 | 0.046 | 0.46 | 0.060 | 0.37 | 0.050 | 0.41
Duration + Length + No. Syllables /Duration | 0.044 | 0.47 | 0.055 | 0.45 | 0.021 | 0.80 | 0.045 | 0.46 | 0.059 | 0.40 | 0.068 | 0.29
Duration +#Consonants + Length/Duration + #Syllables / Duration +CVC2 | 0.044 | 0.47 | 0.049 | 0.48 | 0.018 | 0.83 | 0.046 | 0.45 | 0.054 | 0.42 | 0.065 | 0.34
K | Train |  | Eval | 
 | MSE | R | MSR | R
1 | 0.00 | 0.97 | 0.05 | 0.32
3 | 0.02 | 0.74 | 0.03 | 0.43
100 | 0.03 | 0.54 | 0.03 | 0.53
400 | 0.03 | 0.53 | 0.03 | 0.51
Figure 5. The predicted error rate is plotted against the reference error rate, demonstrating good correlation between the two.
Figure 3. An overview of our approach to search term strength prediction that is based on decomposing terms into features.
www.isip.piconepress.com
Word | tsunami
Phonemes | t s uh n aa m iy
Vowels | uh aa iy
Consonants | t s n m
Syllables | Tsoo nah mee
BPC | S F V N V N V
CVC | C C V C V C V
Class | Phone
Stops (S) | b p d t g k
Fricative (F) | jh ch s sh z zh f th v dh hh
Nasals (N) | m n ng en
Liquids (L) | l el r w y
Vowels (V) | iy ih eh ey ae aa aw ay ah ao ax oy ow uh uw er
Table 2- Broad Phonetic Classes (BPC)
Table 3- Example of converting word into basic feature representations
Observations
Maximum correlation around 46% means just around 21% of the variance in the data is explained by the predictor.
Features used in this work are highly correlated.
Part of the error rate related to factors beyond the “structure” of the word itself. For example, speech rate or acoustic channel are greatly effect the error rate associated with a word.
KNN on phonetic space shows a better prediction capability.
Trained models have some intrinsic inaccuracy because of the conditional diversity of the Data.
Feature Set |  |  |  |  |  |  | 
Duration | Length | No. of Syllables | No. Consonants | No. of Vowels | phoneme Freq. | BPC Freq. | CVC Freq.
2-Grams of Phoneme , BPC, CVC | 2-Gram Of BPC | 2-Grmas of CVC | 3-Grams of CVC | No. Syllables/ Duration | Length/ Duration | No. Vowels/ No Consonants | Start-End Phone
Table1- Features used to predict the keyword strength.
Data Set | NIST Spoken Term Detection 2006 Evaluation results |  | 
Sites | BBN | IBM | SRI
Sources | Broadcast News (3hrs) | Conversational Telephone Speech (3 hrs) | Conference Meetings (2 hrs).
Table 4- Results for feature based method over NIST 2006.
Future Works
Use data generated carefully from acoustically clean speech with proper speech rate and accent for training.
Finding features with small correlation to the existed set of features. Among the candidates are confusability score and expected number of occurrences of a word in the language model.
Combining the outputs of several machines using optimization techniques such as particle swarm optimization (PSO).
Using more complicated models such as nonparametric Bayesian models (e.g. Gaussian process.) for regression.
We have developed algorithms based on some of these suggestions which improves the correlation to around 76% which corresponds to explaining 58% of the variance of the observed data. The results will be published in the near future.