## Slide 1
Virtual White Matter:
A Novel System for Cross-Dish Neural Interaction and Modulation
A Thesis Proposal
Submitted to
the Temple University Graduate Board
In Partial Fulfillment of the Requirements for the Degree
DOCTOR OF PHILOSOPHY
By Mehdi Khantan
24th of April 2025

## Slide 2: INTRODUCTION
Introduction
  Biological vs. Artificial Neural Networks
      Key Differences and Complementary Strengths
  Neuronal Biology
  Applications of Biological Neural Networks (BNNs)
  Research Gaps in BNNs
      Current Limitations
      Unexplored Opportunities
Aim One: Establishing a Virtual White Matter (VWM)
  Concept and Objectives
  Experimental System Setup
  Technical Barriers and Solutions
  Metrics for Evaluation
  Bidirectional Connectivity in VWM
Aim Two: Information Transmission via VWM
  Encoding and Sending a Message
Timeline
Outlines:

## Slide 3: INTRODUCTION
Question: Can we use BNNs for problem solving?
Feature | Biological Neural Networks (BNNs) | Artificial Neural Networks (ANNs)
Basic Unit | Neuron (cell) | Node (mathematical function)
Signal Type | Electrochemical (spikes, synapses) | Numerical (floating-point values)
Speed | Milliseconds | Microseconds or faster
Energy Efficiency | Extremely efficient (20W for whole brain) | Power hungry (Requires large GPUs and electricity)
Biological Realism | Natural, evolved over millions of years | Inspired by biology, but simplified
(A)
Biological vs. Artificial Neural Networks:
(B)
(C)
(D)

## Slide 4
Neuronal Communication:
Electrical Signal: impulse travels down axon
Synaptic Transmission: triggers neurotransmitter release - Glutamate ( Excitatory) GABA (Inhibitory)
Chemical Messengers: neurotransmitters bind to next neuron
Signal Propagation: new impulse starts in receiving neuron
Dendrites
Soma (Cell Body)
Axon
Axon Terminal

## Slide 5
Resting State: negative membrane potential around -70mV
Depolarization: Na⁺ channels open → Na⁺ enters → inside becomes positive
Action Potentials:
Repolarization: K⁺ channels open → K⁺ exits → inside becomes negative
Hyperpolarization: excess K⁺ leaves → more negative than resting
Return to Resting: Na⁺/K⁺ pump and leak channels restore balance

## Slide 6
Interface with Biological Neural Networks (BNNs):
Information Encoding: Deliver patterned electrical stimulation to induce neural activity
Information Decoding: Record extracellular action potentials
Preparation: Cultured dissociated neurons or acute brain slices plated on Microelectrode Arrays (MEAs)

## Slide 7: Cell Culture Overview:
Dissociated hippocampal neurons from Embryonic Rat E18
Used MED64 Micro Electrode Arrays (MEA)
Poly-D-Lysine (PDL) Coating
Laminin Coating
Cell Placement
Media Change: Twice a week (NBActive4)
Incubation: 14 – 41 days at 37 °C, 95% humidity
150µm

## Slide 8: Applications of BNNs:
DeMarse, University of Florida, 2005.
Warwick, University of Reading, 2008.
Cai, Monash University & Cortical Labs, 2023.

## Slide 9: Next Steps:
BNNs abilities are limited to simple tasks.
Achieving complex functionality requires new ways to interconnect them.
VWM acts as a virtual bridge to link multiple neural cultures, enabling dynamic, user-controlled communication.
It supports building complex systems like full brain models or virtual embodiments by interconnecting separate brain regions.

## Slide 10
Spike Detection
AI
Synchronization
Stimulation
Recording
Source MEA
Target MEA
Proof of Concept :
Mono Directional VWM

## Slide 11
USB
Digital Inputs
ARM STM32F410
Intan I/O Expander
Custom
Adapters
Computer
Intan RHX
VWM Software
TCP
Source MEA
Target MEA
SPI
SPI
USB
Head stages
USB
Setup Diagram:

## Slide 12
Read Thread
Artificial Intelligence
GUI Thread
Signal Processing Thread
Circular Buffer
Band-pass Filter
250Hz-5kHz
Spike Detection
Fetching
ARM STM32F410
Circular Data Buffer
Synchronization Unit
Digital I/O
Intan I/O Expander
VWM Software
Intan System
Microcontroller
Target MEA
Source MEA
USB
USB
Head stages A-B
Head stages C-D
SPI
TCP
a
Data
TCP
Save Data (Binary)
Intan Controller
Intan RHX Software
Save Settings (JSON)
Command
TCP
User Interface
Details of the system:

## Slide 13: Spike Detection:
Find t0 where V crosses A:
  If |V| > C in window (-1ms, 2ms): AP[i] = 2 (Voltages Above Limits)
  If V crosses A in 1ms before t0: AP[i] = 3 (Consecutive Threshold Crossing)
For T2 after t0:
  If V crosses B in less than T1: AP[i] = 5 (Rapid Repolarization)
  If V crosses B between T1 & T2:
    Find t1 where crossing occurs
    For T4 after t1:
      If V crosses zero in less than T3: AP[i] = 7 (Rapid Refractory)
      If V crosses zero between T3 & T4: AP[i] = 1 (Spike Detected)
      If V does not cross zero in T4: AP[i] = 6 (Refractory Timeout)
  If V does not cross B in T2:
  AP[i] = 4 (Repolarization Timeout)
T1
T2
T3
T4

## Slide 14: Threshold Selection by spike sorting:
K Means Classifier
PCA
Detect Spikes Using Low Threshold
Plot sorted Neurons
Visualize Spikes
Select Thresholds
RMS-Based Thresholding Thresholds are set as a multiple of the signal’s Root Mean Square (RMS).
Threshold Selection Choosing the correct multiplier is a critical step for reliable spike detection.
Spike Sorting Validation Spike sorting is used to evaluate and refine the selected threshold multiplier having the RMS of the signal.

## Slide 15: Spike Detection Development:

## Slide 16: Spike Detection Test:
MK-801 (a receptor antagonist) applied to inhibit synaptic activity
Post-stimulus responses were silenced, confirming suppression of biological activity
Removal of MK-801 led to reappearance of post-stimulus activity
Confirms that responses are biologically mediated, not stimulation artifacts
Voltage (µv)
Before adding blocker
Voltage (µv)
After adding blocker
Voltage (µv)
After removing the blocker

## Slide 17
Read Thread
Artificial Intelligence
GUI Thread
Signal Processing Thread
Circular Buffer
Band-pass Filter
250Hz-5kHz
Spike Detection
Fetching
ARM STM32F410
Circular Data Buffer
Synchronization Unit
Digital I/O
Intan I/O Expander
VWM Software
Intan System
Microcontroller
Target MEA
Source MEA
USB
USB
Head stages A-B
Head stages C-D
SPI
TCP
a
Data
TCP
Save Data (Binary)
Intan Controller
Intan RHX Software
Save Settings (JSON)
Command
TCP
User Interface
Details of the system:

## Slide 18: Synchronization Process:
t
Data Timing
Data Entry Times to CB
Data Read Times from CB
Start Button
First Data Entry
First Data Process
Last Data Process
Last Data entry
Fixed Delay
200.0±1.0ms
Data is processed in discrete chunks of 25.6 ms
Each chunk takes a variable amount of time to be processed
This introduces inconsistent delays in the system
A microcontroller is added to synchronize timing
  Ensures consistent delays
  Triggers stimulation at
  precise intervals

## Slide 19: Timing Test:
T=200ms
T=200ms
T=200ms
T=200ms
Source E0
Target E0
Target E1
Source E1
Recording E45
Recording E10
Voltage
(µV)
(µV)
(mV)
(mV)
(mV)
(mV)
A timing test shows that the delays between an activity detection and delivering the stimulation are consistent (200.0±1.0ms)

## Slide 20: Stimulation:
Charge-balanced, bidirectional pulses were used for stimulation.
The NeuroTuner (NT) software was developed to optimize pulse parameters and electrode selection.
NT allows systematic sweeping of:
  Pulse amplitude
  Pulse width
  Electrode selection
  Pulse shape
  Number of pulses
Future studies may expand on NT for more advanced pulse shape and type tuning.

## Slide 21: Stimulation Electrode Selection:
21
Receive user settings via GUI
Update GUI
Retrieve settings from Intan RHX
Configure Intan acquisition system
Send stimulation commands
Record data
Spike Detection
Band-pass Filter
250Hz-5kHz
Load Raw Data
Post-Stim Spike Counting
Sums spike counts per stimulation event
Generate Spike Matrix 64*1
Stimulation Sweep:
Spike Counts:
A semi-automated analysis script identifies electrodes with the strongest post-stimulus responses.

## Slide 22: Post-Stimulus Time Histogram (PSTH) :
PSTH on A21 with stimulation at A8
PSTH on A21 with stimulation at B20
PSTH on B10 with stimulation at A8
PSTH on B10 with stimulation at B20

## Slide 23: Spike-Based Classification Workflow:
Spike Detection & Binning
  Spikes from post-stimulus activity were binned using 1 ms bins
  200 ms window → 200 bins per sample
  Data used as input for machine learning models
  Support Vector Machine (SVM), K-nearest neighbor (KNN), and Random Forest (RF) were used.
Spike Detection
Band-pass Filter
250Hz-5kHz
Raw Data
Bins of 1ms
SVM
KNN
RF
Stimulation Source
Label
Features
Normalized
PCA
0.95

## Slide 24: Cross-Validation and Scoring Metrics:
StratifiedKFold Cross-Validation Ensures each fold has the same class distribution as the full dataset.
  n_splits=10: Split dataset into 10 folds
  shuffle=True: Randomly shuffle before splitting
Metrics:

## Slide 25: Single Electrode Analysis:
Classification individually on all 64 electrodes
Top-performing 32 electrodes selected

## Slide 26: Multiple Electrode Analysis:
Combined data from selected electrodes used for classification (max combination =100)
Explored multiple electrode combinations
Standard Error Mean:

## Slide 27: Information Richness test:
Information Gain
Chi-Square (X2)
Fisher Score

## Slide 28: Information Gain:
Sample* | X1 | X2 | X3 | Y
1 | 0 | 0 | 0 | A
2 | 0 | 1 | 0 | A
3 | 1 | 0 | 0 | B
4 | 1 | 1 | 1 | B
IG(X) | 1 | 0 | 0.31 | -
*Sample = Electrode Number, Xi=Bin number

## Slide 29: Chi-Square (X2):
Sample* | X1 | X2 | X3 | Y
1 | 0 | 0 | 0 | A
2 | 0 | 1 | 0 | A
3 | 1 | 0 | 0 | B
4 | 1 | 1 | 1 | B
X2 | 4 | 0 | 1.33 | -
*Sample = Electrode Number, Xi=Bin number
Observed = Expected → Feature and class label are independent
Observed ≠ Expected → There's a deviation from independence → possible dependence

## Slide 30: Fisher Score:
Sample* | X1 | X2 | X3 | Y
1 | 0 | 0 | 0 | A
2 | 0 | 1 | 0 | A
3 | 1 | 0 | 0 | B
4 | 1 | 1 | 1 | B
F(X) | ∞ | 0 | 0.25 | -
Numerator: How different the class means are from the overall mean → bigger = more separation between classes
Denominator: How spread out the feature values are within each class → smaller = tighter, more compact clusters per class
*Sample = Electrode Number, Xi=Bin number

## Slide 31: Analysis using different time frames:
Analysis across multiple time windows using features from 32 selected electrodes
Results showed that the 10 ms window yielded the best results, as expected.

## Slide 32: Analysis using different number of electrodes:
Analysis across different electrode combinations using data from the initial 10 ms
Results revealed that meaningful results can be achieved even with a small subset of electrodes.

## Slide 33: Single vs Double Threshold Spike Detection:
Chart: Machine Learning Results with and without MK-801
| Double Threshold with MK-801 (0-200ms) | Double Threshold without MK-801 (0-200ms) | Single Threshold with MK-801 (0-200ms) | Single Threshold without MK-801 (0-200ms) | Double Threshold with MK-801 (0-10ms)
KNN | 0.44294 | 0.97839 | 0.96646 | 0.98599 | 0.44338
RF | 0.56618 | 0.93199 | 0.94828 | 0.91703 | 0.56921
SVM | 0.5755 | 0.97406 | 0.94219 | 0.93426 | 0.56921
Classification results analyzed for single and double threshold
Results show that the using double threshold was neccasary

## Slide 34: Bidirectional VWM:
Spike Detection
Synchronization
Stimulation
Recording
MEA 1
MEA 2
Spike Detection
Synchronization
Stimulation
Most neural regions are interconnected bidirectionally.
Reconstructing more complete brain-like BNNs requires establishing such two-way communication.

## Slide 35: Bidirectional VWM Classification Results:
a
b
c
d
a: MEA 1 using 200ms post stimulus activity
b: MEA 2 using 200ms post stimulus activity
c: MEA 1 using 10ms post stimulus activity
d: MEA2 using 10ms post stimulus activity

## Slide 36: Sending a message through VWM:
Decoding the Message
Encoding a Message
Encoding the Message
Decoding the Message
Machine Learning
Machine Learning
Replace spontaneous activity with controlled stimulation to encode binary messages
Two electrodes represent binary values: “0” and “1”
Enables transmission of structured data (letters, numbers, Morse code)
Uses a simplified 3-bit binary system for demonstration
Number | Code
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 37: Direct interface with BNN:
32
32
Spike Detection
Encoding the Message
Decoding the Message
Decoding the Message
Encoding a Message
Spike Detection
Goal: Remove ML inference between MEA1 and MEA2
Direct stimulation of MEA2 using binned spike data from MEA1
Prior ML results: >80% accuracy using spike data from 5 electrodes
Select 6 top-performing electrodes to build stimulation patterns
Binned spike data from three electrode stimulates one electrode
Recovered code proves data transfer without ML inference
Number | Code
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 38: Experiment Timeline:
Plating Date | Usable Window (DIV 14 –35) | Purpose
April 9 | April 23 – May 5 | First round of experiments (Step one)
April 30 | May 14 – May 28 | Continued Fig. Step 1 + ML training
May 21 | June 4 – June 25 | BNN-based testing (Step 2)
June 11 | June 25 – July 16 | Repetition of Step 1 and step 2
July 2 | July 16 – August 6 | Redundant ML training
July 23 | August 6 – August 27 | Final testing and creating manuscript figures
August 13 | August 27 – September 17 | Backup MEAs for extended data recording
September 3 | September 17 – October 8 | Final experimental, replication, refinement

## Slide 39: Experiment Timeline:
May: Step 1 – ML-based decoding of 3-bit codes; train 4 models; collect initial decoding data.
June–July: Step 2 – biological signal transfer without ML in transmission; continue data collection across MEAs for Step 1.
Aug–Sept: Redundant testing on different MEA; validate optimal configurations.
Oct–Dec: Focus on final analysis, writing manuscript #2, and completing PhD thesis for submission by year-end.

## Slide 40: Publications:
The NuroSleeve – A user-centered, 3D-printed hybrid orthosis developed for individuals with upper extremity impairment. Published in: Journal of NeuroEngineering and Rehabilitation, 2023
Linking physically isolated in vitro neural specimens on separate three-dimensional microelectrode arrays. Presented at: Society for Neuroscience Annual Meeting (SfN), Washington, D.C., 2023
Microstimulation of Visual Thalamocortical Slices – Investigated spatiotemporal neural dynamics via microstimulation on 3D MEAs. Presented at: Society for Neuroscience Annual Meeting (SfN), Washington, D.C., 2023
Initial feasibility evaluation of the RISES system: An innovative and activity-based closed-loop framework for spinal cord injury rehabilitation and recovery Published in: Journal of Rehabilitation and Assistive Technologies Engineering, 2024
Virtual White Matter - A Novel System for Cross-Dish Neural Interaction and Modulation
Accepted in: Journal of Neural Engineering, 2025

## Slide 41: Acknowledgements:
I would like to thank Dr. Iyad Obeid, Dr. Mijail Serruya, and Dr. Alessandro Napoli for their mentorship, feedback, and continued support.
Special thanks to the Raphael Center for Neurorestoration team at Thomas Jefferson University for their collaboration and contributions to this research.

## Slide 42
Thank You
Thank you for your time and attention. I welcome your questions and feedback.