## Slide 1
Virtual White Matter:
A NOVEL SYSTEM FOR CROSS-DISH NEURAL INTERACTION AND MODULATION
A Thesis
Submitted to
the Temple University Graduate Board
In Partial Fulfillment
of the Requirements for the Degree
DOCTOR OF PHILOSOPHY
By Mehdi Khantan
May 4th 2026

## Slide 2: INTRODUCTION
Introduction
  Biological vs. Artificial Neural Networks
  Applications of Biological Neural Networks (BNNs)
  Research Gaps in BNNs
      Current Limitations
      Unexplored Opportunities
Aim One: Establishing a Virtual White Matter (VWM)
  Concept and Objectives
  Experimental System Setup
  Technical Barriers and Solutions
  Metrics for Evaluation
  Bidirectional Connectivity in VWM
Aim Two: Information Transmission via VWM
  Concept and Objectives
  Electrode Selection
  System Architecture
  Temporal Stability
  Results of Monodirectional and Bidirectional communication
  Threshold Based Decoding
  Publication
Outlines:

## Slide 3: INTRODUCTION
Question: Can we use BNNs for problem solving?
Feature | Biological Neural Networks (BNNs) | Artificial Neural Networks (ANNs)
Basic Unit | Neuron (cell) | Node (mathematical function)
Signal Type | Electrochemical (spikes, synapses) | Numerical (floating-point values)
Speed | Milliseconds | Microseconds or faster
Energy Efficiency | Extremely efficient (20W for whole brain) | Power hungry (Requires large GPUs and electricity)
Biological Realism | Natural, evolved over millions of years | Inspired by biology, but simplified
(A)
Biological vs. Artificial Neural Networks:
(B)
(C)
(D)

## Slide 4: Applications of BNNs:
DeMarse, University of Florida, 2005.
Warwick, University of Reading, 2008.
Cai, Monash University & Cortical Labs, 2023.

## Slide 5: Next Steps:
BNNs abilities are limited to simple tasks.
Achieving complex functionality requires new ways to interconnect them.
VWM acts as a virtual bridge to link multiple neural cultures, enabling dynamic, user-controlled communication.
It supports building complex systems like full brain models or virtual embodiments by interconnecting separate brain regions.

## Slide 6
Spike Detection
Synchronization
Stimulation
Recording
Source MEA
Target MEA
Aim One - Proof of Concept :
Mono Directional VWM

## Slide 7
USB
Digital Inputs
ARM STM32F410
Intan I/O Expander
Custom
Adapters
Computer
Intan RHX
VWM Software
TCP
Source MEA
Target MEA
SPI
SPI
USB
Head stages
USB
Setup Diagram:

## Slide 8
Read Thread
Artificial Intelligence
GUI Thread
Signal Processing Thread
Circular Buffer
Band-pass Filter
250Hz-5kHz
Spike Detection
Fetching
ARM STM32F410
Circular Data Buffer
Synchronization Unit
Digital I/O
Intan I/O Expander
VWM Software
Intan System
Microcontroller
Target MEA
Source MEA
USB
USB
Head stages A-B
Head stages C-D
SPI
TCP
Data
TCP
Save Data (Binary)
Intan Controller
Intan RHX Software
Save Settings (JSON)
Command
TCP
User Interface
Details of the system:

## Slide 9: Stimulation:
Charge-balanced, bidirectional pulses were used for stimulation.
The NeuroTuner (NT) software was developed to optimize pulse parameters and electrode selection.
NT allows systematic sweeping of:
  Pulse amplitude
  Pulse width
  Electrode selection
  Pulse shape
  Number of pulses
Future studies may expand on NT for more advanced pulse shape and type tuning.

## Slide 10: Spike Detection:
Find t0 where V crosses A:
  If |V| > C in window (-1ms, 2ms): AP[i] = 2 (Voltages Above Limits)
  If V crosses A in 1ms before t0: AP[i] = 3 (Consecutive Threshold Crossing)
For T2 after t0:
  If V crosses B in less than T1: AP[i] = 5 (Rapid Repolarization)
  If V crosses B between T1 & T2:
    Find t1 where crossing occurs
    For T4 after t1:
      If V crosses zero in less than T3: AP[i] = 7 (Rapid Refractory)
      If V crosses zero between T3 & T4: AP[i] = 1 (Spike Detected)
      If V does not cross zero in T4: AP[i] = 6 (Refractory Timeout)
  If V does not cross B in T2:
  AP[i] = 4 (Repolarization Timeout)
T1
T2
T3
T4

## Slide 11: Threshold Selection by spike sorting:
K Means Classifier
PCA
Detect Spikes Using Low Threshold
Plot sorted Neurons
Visualize Spikes
Select Thresholds
RMS-Based Thresholding Thresholds are set as a multiple of the signal’s Root Mean Square (RMS).
Threshold Selection Choosing the correct multiplier is a critical step for reliable spike detection.
Spike Sorting Validation Spike sorting is used to evaluate and refine the selected threshold multiplier having the RMS of the signal.

## Slide 12: Spike Detection Test:
MK-801 (a receptor antagonist) applied to inhibit synaptic activity
Post-stimulus responses were silenced, confirming suppression of biological activity
Removal of MK-801 led to reappearance of post-stimulus activity
Confirms that responses are biologically mediated, not stimulation artifacts
Voltage (µv)
Before adding blocker
Voltage (µv)
After adding blocker
Voltage (µv)
After removing the blocker

## Slide 13
Read Thread
Artificial Intelligence
GUI Thread
Signal Processing Thread
Circular Buffer
Band-pass Filter
250Hz-5kHz
Spike Detection
Fetching
ARM STM32F410
Circular Data Buffer
Synchronization Unit
Digital I/O
Intan I/O Expander
VWM Software
Intan System
Microcontroller
Target MEA
Source MEA
USB
USB
Head stages A-B
Head stages C-D
SPI
TCP
Data
TCP
Save Data (Binary)
Intan Controller
Intan RHX Software
Save Settings (JSON)
Command
TCP
User Interface
Details of the system:

## Slide 14: Synchronization Process:
t
Data Timing
Data Entry Times to CB
Data Read Times from CB
Start Button
First Data Entry
First Data Process
Last Data Process
Last Data entry
Fixed Delay
200.0±1.0ms
Data is processed in discrete chunks of 25.6 ms
Each chunk takes a variable amount of time to be processed
This introduces inconsistent delays in the system
A microcontroller is added to synchronize timing
  Ensures consistent delays
  Triggers stimulation at
  precise intervals

## Slide 15: Timing Test:
T=200ms
T=200ms
T=200ms
T=200ms
Source E0
Target E0
Target E1
Source E1
Recording E45
Recording E10
Voltage
(µV)
(µV)
(mV)
(mV)
(mV)
(mV)
A timing test shows that the delays between an activity detection and delivering the stimulation are consistent (200.0±1.0ms)

## Slide 16: Post-Stimulus Time Histogram (PSTH) :
PSTH on A21 with stimulation at A8
PSTH on A21 with stimulation at B20
PSTH on B10 with stimulation at A8
PSTH on B10 with stimulation at B20

## Slide 17: Spike-Based Classification Workflow:
Spike Detection & Binning
  Spikes from post-stimulus activity were binned using 1 ms bins
  200 ms window → 200 bins per sample
  Data used as input for machine learning models
  Support Vector Machine (SVM), K-nearest neighbor (KNN), and Random Forest (RF) were used.
Spike Detection
Band-pass Filter
250Hz-5kHz
Raw Data
Bins of 1ms
SVM
KNN
RF
Stimulation Source
Label
Features
PCA
0.95
200ms
window

## Slide 18: Single Electrode Analysis:
Classification individually on all 64 electrodes
Top-performing 32 electrodes selected

## Slide 19: Multiple Electrode Analysis:
Combined data from selected electrodes used for classification (max combination =100)
Explored multiple electrode combinations
Standard Error Mean:

## Slide 20: Cross-Validation and Scoring Metrics:
StratifiedKFold Cross-Validation Ensures each fold has the same class distribution as the full dataset.
  n_splits=10: Split dataset into 10 folds
  shuffle=True: Randomly shuffle before splitting
Metrics:

## Slide 21: Information Richnesfiss test:
Information Gain
Chi-Square (X2)
Fisher Score

## Slide 22: Analysis using different time frames:
Analysis across multiple time windows using features from 32 selected electrodes
Results showed that the 10 ms window yielded the acceptable results, as expected.

## Slide 23: Analysis using different number of electrodes:
Analysis across different electrode combinations using data from the initial 10 ms
Results revealed that meaningful results can be achieved even with a small subset of electrodes.

## Slide 24: Single vs Double Threshold Spike Detection:
Chart: Machine Learning Results with and without MK-801
| Double Threshold with MK-801 (0-200ms) | Double Threshold without MK-801 (0-200ms) | Single Threshold with MK-801 (0-200ms) | Single Threshold without MK-801 (0-200ms) | Double Threshold with MK-801 (0-10ms)
KNN | 0.44294 | 0.97839 | 0.96646 | 0.98599 | 0.44338
RF | 0.56618 | 0.93199 | 0.94828 | 0.91703 | 0.56921
SVM | 0.5755 | 0.97406 | 0.94219 | 0.93426 | 0.56921
Classification results analyzed for single and double threshold
Results show that the using double threshold was neccasary

## Slide 25: Bidirectional VWM:
Spike Detection
Processing
Stimulation
Recording
MEA 1
MEA 2
Spike Detection
Processing
Stimulation
Most neural regions are interconnected bidirectionally.
Reconstructing more complete brain-like BNNs requires establishing such two-way communication.

## Slide 26: Bidirectional VWM Classification Results:
a
b
c
d
a: MEA 1 using 200ms post stimulus activity
b: MEA 2 using 200ms post stimulus activity
c: MEA 1 using 10ms post stimulus activity
d: MEA2 using 10ms post stimulus activity

## Slide 27: Conclusion of Aim One:
VWM System Performance
• Delays between event detection and stimulation were fixed at 200.0 ± 1.0 ms
• Double-threshold spike detection successfully rejected stimulation artifacts in the first 10 ms post-stimulus, a window conventionally blanked entirely, and outperformed single-threshold classification
Classification Results
• Stimulation-source classification exceeded 85% accuracy
• Optimal feature window: 10 ms post-stimulus using 32 electrodes at 1 ms bins; 200 ms window using top 6 electrodes at 1 ms bins
• SVM, KNN, and RF validated via 10-fold StratifiedKFold cross-validation with PCA (95% variance retained); SVM showed the best classification across all conditions
Key Outcome
• Established mono- and bidirectional VWM; published in Journal of Neural Engineering (2025): “Virtual white matter: a novel system for cross-dish neural interaction and modulation”

## Slide 28
Aim Two:
Structured Binary Communication Between Dissociated Cortical Cultures in Physically Separate MEA dishes
Stimulation
Biphasic, 10 μA, 500 μs/phase Charge density: 2×10⁻⁴ C/cm² per phase
Timing
1 s inter-bit interval
2 s inter-word interval
2 stimulation electrodes per MEA
6 recording electrodes per MEA
Electrodes
3-bit data words + 1 parity bit
400-word pre-generated dictionary
Even parity check; lowest-confidence
bit toggled on parity failure
Error Correction
Data Structure
Electrode one represents as binary 0
Electrode two represents as binary 1
Encoding
Monodirectional
Dataset → MEA1 (encode) → decode A-bits → error correct → re-encode → MEA2 → decode B-bits → compare output
Bidirectional
Mono path completed first, then decoded word from MEA2 re-encoded → transmitted back to MEA1 → decoded → compared to original message for round-trip fidelity
Comparative Baseline
ML decoder replaced with spike-count threshold classifier to evaluate contribution of classifier complexity to decoding performance

## Slide 29: Electrode Selection – Target Electrodes
Selection Protocol — Step by Step
1
Sequential Electrode Stimulation
Each MEA electrode stimulated individually using NeuroTuner
Spike Detection
Evoked spikes detected across all electrodes post-stimulation
Feature Extraction (0–200 ms)
Stimulation-evoked spikes summed per event within post-stim window
Evoked Response Quantification
Total evoked spikes per stimulation event computed per electrode
Electrode Impact Ranking
Electrodes ranked by aggregate evoked spike count
Topological Active Selection
Top two electrode selected spatially distant from each other
5
2
4
3
6

## Slide 30: Electrode Selection – Source Electrodes
Selection Protocol — Step by Step
1
4-Bit Random Dataset Generation
Randomized dictionary of 4-bit packets (3 data + 1 parity bit) generated
Dictionary-Guided Stimulation
Two target electrodes stimulated sequentially per dictionary entry
Spike Detection on All Electrodes
Post-stim spike activity recorded across all 64 MEA channels
Feature Extraction (1 ms bins)
Binary spike train binned at 1 ms resolution over 0–200 ms window
Electrode-Specific ML Classification
Classifier trained per electrode; each evaluated individually for accuracy
Ranking & Aggregated Model Training
Top 6 electrodes selected; final model trained on combined feature set
5
2
4
3
6

## Slide 31: System Architecture
Main data flow was made based on the initial architecture
Real time feature extractions and real time machine learning was added
Real time parity-based error correction was added to the system
Timing constraints was added to send the 4-bit data on each section
All the data flow was done using python in a multi threaded form
Main Improvements:

## Slide 32
Machine Learning for
Realtime Neural Decoding
Feature Extraction
200 × 6 binary matrix per trial (1 ms bins, 0–200 ms)
6 preselected output electrodes from 64-electrodes
PCA retaining 95% variance
Classifiers evaluated: SVM, Random Forest, K-Nearest Neighbors
Stratified 10-fold cross-validation; 400 Word communication for training
SVM (sigmoid kernel, C=10) selected — highest accuracy
Each 4-bit word decoded bit-independently via real-time pipeline
Parity bit appended to each 3-bit transmission word
Even parity check performed after all bits decoded
On failure: lowest-confidence bit toggled to correct error
Improves reliable word reconstruction over raw decoding
Classifier Design
Error Correction
Cumulative Accuracy for 5 data sets across 400-word Transmission
Use Spikes Detected on the Six Selected Source Electrodes 400*4-bit trials
Aggregate the Binned Spikes of 200 per electrodes 1200*1
Using a new database run the machine learning in real time mode
Error Correction
Train Machine Learning in Offline Mode
Save Job Lib files

## Slide 33: Results of Monodirectional VWM
Higher than success rate shows that the system can act as a reliable communication
Results show a meaningful contribution of the parity error correction
Neural Decoder for
A-bits
Data Set
Neural Decoder for
B-bits
MEA1
MEA2
A-bits
B-bits

## Slide 34
Temporal Stability in
Monodirectional Neural Communication
Background
Electrical stimulation drives neural plasticity by modifying synaptic efficacy, reorganizing and altering network connectivity. Since the machine learning classifier relies on spike-timing relationships, plasticity-induced reconfiguration may degrade decoder performance over time.
Most Data sets stay stable during the 400-word transmission.
Dataset 2 exhibited a sustained decline after ~100 trials (converging near chance level).
Dataset 1:
Stable
Dataset 2:
Declined to ~0.52 after trial 100
Dataset 3:
Stable
Dataset 4:
Stable
Dataset 5:
Stable
Periodic classifier retraining or online adaptive machine learning is recommended to sustain optimal decoding performance during extended stimulation protocols.
Findings
Dataset Performance Summary
Recommendation
Cumulative Accuracy for 5 data sets across 400-word Transmission

## Slide 35: Results of Bidirectional VWM
A-bits
B-bits
C-bits
D-bits

## Slide 36
Threshold-Based Decoding
Background
To assess the contribution of classifier complexity to decoding performance, the SVM-based decoder on MEA1 (A-Bits) was replaced with an optimal minimum-error threshold classifier.
The spike counts from the six electrodes stimulated through the two electrode overlap with each other making the classification complicated.
Findings
The Architecture of the Decoders
Spike Count Distribution by Stimulus Electrode over 1000 Stimulation
Monodirectional Neural Communication

## Slide 37: Results of Threshold-Based Decoding
A-bits
B-bits
Bits A1–A4: 60–75% accuracy
Only marginally above chance (50%)
Bits_A1–A3 aggregate 30% with parity but remains near chance.
Bits B1–B4: 63–84% accuracy
Substantially outperforms threshold stage across all channels
Demonstrates ML necessity for reliable multi-MEA communication
Final word success rate: around 18%
Bottleneck is threshold-based MEA1 stage
Errors compound across pipeline stages
MEA2 — ML Decoding (SVM)
MEA1 — Threshold Decoding
Overall System Outcome

## Slide 38
Publications
Peer-Reviewed Journal Articles
Developing a Binary Communication Protocol Between Biological Neural Networks Using Virtual White Matter
2026
[5]
Lim, J. T., Khantan, M., Napoli, A., & Serruya, M. D.
Biomedical Engineering Education
Submitted
Machine Learning-Assisted Characterization of Hippocampal Input-Output Transformations on an Ex Vivo 3D MEA Platform
2026
[4]
Khantan, M., Lim, J., Bernhardt, A., Napoli, A., Obeid, I., & Serruya, M. D.
Journal of Neural Engineering
Submitted
Developing a Binary Communication Protocol Between Biological Neural Networks Using Virtual White Matter
38
2025
Khantan, M., Lim, J., Napoli, A., Obeid, I., & Serruya, M. D.
Journal of Neural Engineering
Published
Virtual White Matter: A Novel System for Cross-Dish Neural Interaction and Modulation
2024
[2]
Madarshahian, S., Guerrero, T., Aung, P. T., Gustafson, K., Harrop, J. S., Johnson, D. R., Khantan, M., et al.
Journal of Rehabilitation and Assistive Technologies Engineering
Published
Initial Feasibility Evaluation of the RISES System: An Innovative Activity-Based Closed-Loop Framework for Spinal Cord Injury Rehabilitation and Recovery
2023
[1]
Khantan, M., Avery, M., Aung, P. T., Zarin, R. M., Hammelef, E., Shawki, N., Serruya, M. D., & Napoli, A.
Journal of NeuroEngineering and Rehabilitation
Published
The NuroSleeve: A User-Centered, 3D-Printed Hybrid Orthosis for Individuals with Upper Extremity Impairment
[3]

## Slide 39
Publications
Poster Presentations at International Scientific Meetings
Developing a Binary Communication Protocol Between Biological Neural Networks Using Virtual White Matter
2023
Madarshahian, S., Guerrero, T., Aung, P. T., Grampurohit, N., Gustafson, K., Harrop, J., Khantan, M., et al.
Progress in Clinical Motor Control II — Movement and Rehabilitation Sciences
The RISES System: An Innovative and Activity-Based Closed-Loop Platform for Spinal Cord Injury Rehabilitation and Recovery
2023
[1]
Khantan, M., Lim, J. T., Napoli, A., Obeid, I., & Serruya, M. D.
Society for Neuroscience (SfN) Annual Meeting
Linking Physically Isolated In Vitro Neural Specimens on Separate Three-Dimensional Microelectrode Arrays
[3]
2023
[2]
Lim, J. T., Khantan, M., Shawki, N., Napoli, A., Obeid, I., & Serruya, M. D.
Society for Neuroscience (SfN) Annual Meeting
Microstimulation-Induced Spatiotemporal Dynamics of Organotypic Visual Thalamocortical Slices on a 3D Multi-Electrode Array

## Slide 40
Thank You
Thank you for your time and attention. I welcome your questions and feedback.

## Slide 41: Acknowledgements:
1. Dr. Iyad Obeid, Thesis Advisor
For his guidance, support, and help shaping this research and building good scientific habits.
2. Center for Neurorestoration, Thomas Jefferson University, Dr. Mijail D. Serruya & Dr. Alessandro Napoli
For their funding, equipment, ideas, and collaborative spirit that supported this work.
3. Doctoral Committee — Dr. Picone · Dr. Spence · Dr. Serruya · Dr. Napoli · Dr. Smith
For their feedback, expertise, and time given throughout this dissertation.
4. The Broader Scientific Community — Neural Engineering · Biocomputing · Machine Learning
For the foundational work that made the Virtual White Matter system possible. I hope this work adds to that ongoing effort.

## Slide 42: Information Richness test:
Information Gain
Chi-Square (X2)
Fisher Score

## Slide 43: Information Gain:
Sample* | X1 | X2 | X3 | Y
1 | 0 | 0 | 0 | A
2 | 0 | 1 | 0 | A
3 | 1 | 0 | 0 | B
4 | 1 | 1 | 1 | B
IG(X) | 1 | 0 | 0.31 | -
*Sample = Electrode Number, Xi=Bin number

## Slide 44: Chi-Square (X2):
Sample* | X1 | X2 | X3 | Y
1 | 0 | 0 | 0 | A
2 | 0 | 1 | 0 | A
3 | 1 | 0 | 0 | B
4 | 1 | 1 | 1 | B
X2 | 4 | 0 | 1.33 | -
*Sample = Electrode Number, Xi=Bin number
Observed = Expected → Feature and class label are independent
Observed ≠ Expected → There's a deviation from independence → possible dependence

## Slide 45: Fisher Score:
Sample* | X1 | X2 | X3 | Y
1 | 0 | 0 | 0 | A
2 | 0 | 1 | 0 | A
3 | 1 | 0 | 0 | B
4 | 1 | 1 | 1 | B
F(X) | ∞ | 0 | 0.25 | -
Numerator: How different the class means are from the overall mean → bigger = more separation between classes
Denominator: How spread out the feature values are within each class → smaller = tighter, more compact clusters per class
*Sample = Electrode Number, Xi=Bin number