## Slide 1: SafeStep
An Automatic Hazards Detection Blind Cane
Kevin Bui, Mohamad Charabi, Nathan Pervin, Mikita Piatsevich
Advisor: Dr. Joseph Picone
Instructor: Dr. Brian Thomson

## Slide 2: Blindness and vision impairment are increasing globally, increasing reliance on mobility aids.
Source:
https://www.sciencedirect.com/science/article/pii/S2214109X20304253

## Slide 3: Automatic Hazards Detection Can Prevent User Injuries
Source: https://www.researchgate.net/figure/Schematics-of-A-an-individual-with-the-white-cane-facing-daily-life-obstacles-the-cane_fig1_350820013
Blind canes can’t detect all hazards.
Source: https://youtu.be/S0n9UQ9eNrs?si=bu-2d58Qq2Apc4Jm
As a result, collisions and falls can occur.
Notes: EDIT 1

## Slide 4: Fall and Injury Rates Among the Visually Impaired
76 people with visual impairment were studied over a 12-month period
74% reported at least 1 fall or injury event
63% of falls resulted in an injury
Our project aims to mitigate the trips and misplaced steps that are causes of falls.

## Slide 5: Proposed Solution: SafeStep, a smart blind cane
Vibration Warning
Ultrasonic Sensor
Camera

## Slide 6: Proposed Solution: SafeStep, a smart blind cane
Scan environment for hazards
Alert user to hazards
Process data

## Slide 7: Sensing
Ultrasonic sensor detects obstacles in walking path
Camera Captures Image of Walking Path

## Slide 8: Processing
Sensing Data
Alert User
Process Data

## Slide 9: Battery
Both sources are designed to provide regulated 5V required for Raspberry Pi operation
5V 3.7V
5V
5V regulated output (direct supply)
3.7V battery boosted to 5V

## Slide 10: Design Requirements
Constraint
Detection
Distance
False Positive Rate
Target Value
Time
Distance
Percentage
Metric
< 220 ms
Why?
6 ft
< 1%
Fast enough
For human response
Allows early
hazard detection
Prevents false alerts
Hazard
Detection Latency

## Slide 11: Design Requirements (Power System)
System Load Power: P = V × I = 5V × 1.1A = 5.5W
Primary Battery (Power Bank): Runtime = 45Wh / 5.5W ≈ 8.2 hours (~7–10 hrs)
Backup Battery (18650 + Boost): Runtime = 9.95Wh / 5.5W ≈ 1.8 hours (~2 hrs)
Runtime (hours) = (Battery Energy (Wh) × Efficiency) / Load Power (W)

## Slide 12: Design Constraints
Constraint
Handle Diameter
Handle Length
Portability
Target Value
Physical Dimension
Physical Dimension
Operation
Metric
2.5 cm
Why?
20 cm
Cane is foldable
Provides a comfortable grip
Improves control over cane
Easy to store and carry

## Slide 13: Proposed Solution: Ultrasonic Sensor
Ultrasonic sensor detects obstacles in walking path
Vibration Alerts User

## Slide 14: Proposed solution: Vibration motor

## Slide 15: Proposed Solution: Machine Learning
Camera Captures Image of Walking Path
Machine Learning Model Identifies Hazard
Vibration Alerts User
Hazard: Stairs

## Slide 16: Proposed Solution: Power System
Both sources are designed to provide regulated 5V required for Raspberry Pi operation
5V 3.7V
5V
5V regulated output (direct supply)
3.7V battery boosted to 5V

## Slide 17: System Integration
Power
Raspberry Pi Zero 2 W Computer
Raspberry Pi AI Camera
Data
Ultrasonic Sensor
Vibration Motor
Battery
Live Camera Feed
1080p Images
Distance Measurement (cm)
5V
5V
3.3V
5V
ON/OFF

## Slide 18: Engineering Design and Progress
Power
Raspberry Pi Zero 2 W Computer
Raspberry Pi AI Camera
Data
Ultrasonic Sensor
Vibration Motor
Battery
Live Camera Feed
1080p Images
Distance Measurement (cm)
5V
5V
3.3V
5V
ON/OFF

## Slide 19: Engineering Design
Camera
Ultrasonic Sensor
Battery
Vibration Warning

## Slide 20: Engineering Design
Camera
Ultrasonic Sensor
Battery
Vibration Warning

## Slide 21: Engineering Design

## Slide 22: Engineering Design: Ultrasonic Sensor
GND to Pin 6
V+ to Pin 2
Pin 4 to (GPIO18)

## Slide 23: Engineering Design: Machine Learning

## Slide 24: Engineering Design: Battery System
5V
Primary Voltage Source (fixed - 5V)
Secondary Voltage Source (3.7)
Low Voltage (3.7V)
DC – DC Boost Converter
5V

## Slide 25: Engineering Design: Vibration Motor

## Slide 26: Alert

## Slide 27: Engineering Design: Alert

## Slide 28: Engineering Design and Progress
Data Collection:
5729 total images
2650 normal
1641 stairs
1438 curbs

## Slide 29: Engineering Design and Progress
The most optimal placement of the ultrasonic sensor will be at a 45-degree angle for the best view.
Programmed in Vs Code
Using Python.

## Slide 30: Engineering Design and Progress
Data Collection:
5729 total images
2650 normal
1641 stairs
1438 curbs
3D Model of handle segment with component mounting points
SolidWorks was chosen for its accessibility to Temple Students and its extensive documentation.

## Slide 31: Engineering Design and Progress

## Slide 32: Testing Setup and Results
3D Print Testing
Components Mounted
3D Model

## Slide 33: Testing Setup and Results

## Slide 34: Testing Setup and Results
Integrated
Testing

## Slide 35: Testing Setup and Results

## Slide 36: Future Work
Standards
ISO 9999 code 12 39 03
Tactile sticks or white canes:
Cane dimensions, used for design constraints
Increase training data set by collecting more images.
Complete 3D model and prints of the protective component enclosure.
Test the ultrasonic sensor while it is integrated with the system.
Write system-wide code
to integrate all inputs and vibration motor output

## Slide 37: Future Work
Standards
ISO 9999 code 12 39 03
Tactile sticks or white canes:
Cane dimensions, used for design constraints
Increase training data set by collecting more images.
Reduce enclosure size

## Slide 38: Questions?

## Slide 39: Design Requirements
Hazard
Detection Latency
Detection
Distance
False Positive
Rate
Target: < 220 ms
Metric: Distance
Why? Fast enough
For human reaction
Metric: Time
Target: 6ft
Why: Allows early
hazard detection
Metric: Accuracy
Target: <1%
Why: Prevents false alerts

## Slide 40
https://www.researchgate.net/figure/Up-left-and-down-right-stairs-detected-with-the-electronic-white-cane_fig5_51873006
Sensing
Battery
Alert
Processing
Data Collection:
7550 total images
3168 normal
2233 stairs
2149 curbs